## Slide 1: Further discussion on EN-DC Refsens test requirements handling
ZTE Corporation
3GPP TSG-RAN5 Meeting #106 R5-251074 Athens, Greece, February 17 – 21, 2025

## Slide 2: Minimum requirements for EN-DC Refsens
In the latest TS 38.101-3, the minimum requirements for reference sensitivity of inter-band EN-DC have been updated to use the new table template. In the new table, the uplink allocation are merged into the MSD table. For each type of Refsens exception, only up to two downlink channel bandwidths are chosen instead of using all the possible downlink channel bandwidths. The corresponding changes for test specification in TS 38.521-3 were approved in [1] with a small number of combinations of UL configurations and DL channel bandwidths for minimum requirements shown as below.
References
[1] R5-243672, Update of 7.3B.2 reference sensitivity of inter-band EN-DC, Huawei, HiSilicon, RAN5#103
UL band | DL band | UL BW | SCS of UL band | UL RB Allocation | DL BW | MSD | UL/DL fc condition | UL/DL harmonic order
 |  | (MHz) | (kHz) | LCRB | (MHz) | (dB) |  | 
1 | n77 | 5 | 15 | 25 (RBstart=0) | 10 | 23.9 | NOTE 2 | UL2/DL1 direct-hit
1 | n77 | 20 | 15 | 100 (RBstart=0) | 100 | 13.8 | NOTE 2 | UL2/DL1 direct-hit
1 | n77 | 5 | 15 | 25 (RBstart=0) | 10 | 1.1 | NOTE 6 | UL2/DL1 near-miss
2 | n77 | 5 | 15 | 25 (RBstart=0) | 10 | 23.9 | NOTE 2 | UL2/DL1 direct-hit
2 | n77 | 10 | 15 | 50 (RBstart=0) | 100 | 13.8 | NOTE 2 | UL2/DL1 direct-hit
2 | n77 | 5 | 15 | 25 (RBstart=0) | 10 | 1.1 | NOTE 6 | UL2/DL1 near-miss
Table 7.3B.2.0.3.1-1: Reference sensitivity exceptions (MSD) due to UL harmonic for EN-DC in NR FR1

## Slide 3: Test requirements for EN-DC Refsens
For the test requirements for EN-DC Refsense, a new table template was introduced in [2] to merge the different exception types. An action point AP#104.22 was set for companies to check the latest Refsens requirements and update the test points per EN-DC configuration with exception type. As a transition phase, the new table template as shown in Table 7.3B.2.3.5-0 will co-exist with the old table templates in the spec for the time being.
References
[2] R5-246013, Discussion on reference sensitivity of inter-band EN-DC, Huawei, HiSilicon, RAN5#104.
CA configuration | Test ID | DL band | CBW (MHz) | REFSENS test requirement (dBm) | Exception type
DC_39A_n41A | 1 | 39 | 20 | REFSENS | Cross band isolation
 |  | n41 | 10 | -91.5+TT | 
 | 2 | 39 | 5 | -97.7 | Cross band isolation
 |  | n41 | 100 | REFSENS | 
DC_40A_n41A | 1 | 40 | 5 | -67.9 | Cross band isolation
 |  | n41 | 100 | REFSENS | Cross band isolation
DC_26A_n41A | 1 | 26 | 5 | REFSENS | UL harmonic
 |  | n41 | 100 | -81.8+TT | interference
 | 1a | 26 | 5 | REFSENS | 
 |  | n41 | 10 | -81.1+TT | 
 | 2 | 26 | 5 | REFSENS | UL harmonic exception
 |  | n41 | 10 | REFSENS | avoided
 | 3 | 26 | 5 | -81.2 | dual uplink operation
 |  | n41 | 10 | REFSENS | 
 | 4 | 26 | 5 | -72.5 | harmonic mixing
 |  | n41 | 10 | REFSENS | 
 | 5 | 26 | 15 | -69.5 | 
 |  | n41 | 15 | REFSENS | 
 | 6 | 26 | 15 | REFSENS | harmonic mixing
 |  | n41 | 15 | REFSENS | avoiding
Table 7.3B.2.3.5-0: Reference sensitivity requirement for PC3 EN-DC
UL band | DL band | SCS (kHz) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm)
1, 3 | n772 | 15 |  | -71.4 +TT | -71.4 +TT | -71.3 +TT |  |  | -71.2 +TT | -71.3 +TT |  |  |  | 
 |  | 30 |  | -71.7 +TT | -71.5 +TT | -71.5 +TT |  |  | -71.3 +TT | -71.4 +TT | -71.4 +TT | -71.3 +TT | -71.3 +TT | -71.3 +TT
 |  | 60 |  | -72.1 +TT | -71.8 +TT | -71.7 +TT |  |  | -71.5 +TT | -71.5 +TT | -71.5 +TT | -71.4 +TT | -71.4 +TT | -71.4 +TT
 | n773 | 15 |  | -94.2 +TT | -92.7 +TT | -91.9 +TT |  |  |  |  |  |  |  | 
 |  | 30 |  | -94.5 +TT | -92.8 +TT | -92.1 +TT |  |  |  |  |  |  |  | 
 |  | 60 |  | -94.9 +TT | -93.1 +TT | -92.3 +TT |  |  |  |  |  |  |  | 
Table 7.3B.2.3.5-1: Reference sensitivity due to UL harmonic for EN-DC in NR FR1
UL band | DL band | SCS (kHz) | 5MHz (dBm) | 10MHz (dBm) | 15MHz (dBm) | 20MHz (dBm) | 25MHz (dBm) | 40MHz (dBm) | 50MHz (dBm) | 60MHz (dBm) | 80MHz (dBm) | 90MHz (dBm | 100MHz (dBm)
2 | n714 | 15 | -70.4 +TT | -70.4 +TT | -70.4 +TT | -70.4 +TT |  |  |  |  |  |  | 
 |  | 30 |  | -70.7 +TT | -70.7 +TT | -71.8 +TT |  |  |  |  |  |  | 
 |  | 60 |  | -72.4 +TT | -72.7 +TT | -77.0 +TT |  |  |  |  |  |  | 
n2 | 71 | N/A | -69.7 | -69.9 | -70.1 | -71.2 |  |  |  |  |  |  | 
Table 7.3B.2.3.5-2: Reference sensitivity due to receiver harmonic mixing for PC3 EN-DC in NR FR1

## Slide 4: Further considerations on test requirements for EN-DC Refsens (Ⅰ)
In the new MSD table template in Table 7.3B.2.3.5-0, the Refsens test requirement is identified by Test ID which is defined in Table 7.3B.2.3.4.2.1-6 for DC configuration test setting. The test requirements include DL band, CBW, exception type and Refsens requirements. However, it is noted that in the minimum requirements, the Refsens is specified by the combination of UL configuration and DL channel bandwidths. It is inaccurate for Table 7.3B.2.3.5-0 if only DL band and CBW are mentioned, for example for DC_39A_n41A Test ID=1, the Refsens test requirement is calculated based on UL band=39, UL BW=20MHz, and DL band=n41, DL BW=10MHz. The exception type is Cross band isolation and the interference source is “>ACLR2”.
UL band | DL band | UL Fc | UL BW | SCS of UL band | UL RB Allocation | DL Fc | DL BW | MSD | Cross-band Interference source
 |  | (MHz) | (MHz) | (kHz) | LCRB | (MHz) | (MHz) | (dB) | 
39 | n41 | 1910 | 20 | 15 | 100 (RBSTART=0) | 2501 | 10 | 3.3 | >ACLR2
n41 | 39 | 2546 | 100 | 30 | 270 (RBSTART=3) | 1917.5 | 5 | 1.6 | >ACLR2
Observation 1: The Refsens requirements for EN-DC configuration is specified by the combination of UL configuration and DL channel bandwidths.

## Slide 5: Further considerations on test requirements for EN-DC Refsens (Ⅱ)
Based on the above discussion, it is noted that for the Refsens test requirements for EN-DC, both UL configuration and DL channel bandwidths should be considered in Table 7.3B.2.3.5-0. Furthermore, since there is no information of “Interference order” such as “ULx/DLy”, “IMDx” and “ACLRx”, etc both in the table of test setting and the table of test requirements, to make it clearer to the test users it is suggested to add a column of “Interference order” in Table 7.3B.2.3.5-0 for information.
CAEN-DC configuration | Test ID | DLE-UTRA/NR band | UL/DL CBW (MHz) | REFSENS test requirement (dBm) | Exception type | Interference order
DC_39A_n41A | 1 | 39 | 20 | REFSENS | Cross band isolation | >ACLR2
 |  | n41 | 10 | -91.5+TT |  | 
 | 2 | 39 | 5 | -97.7 | Cross band isolation | >ACLR2
 |  | n41 | 100 | REFSENS |  | 
DC_40A_n41A | 1 | 40 | 5 | -67.9 | Cross band isolation | ACLR2
 |  | n41 | 100 | REFSENS | Cross band isolation | 
DC_26A_n41A | 1 | 26 | 5 | REFSENS | UL harmonic | UL3/DL1
 |  | n41 | 100 | -81.8+TT | interference | direct-hit
 | 1a | 26 | 5 | REFSENS |  | 
 |  | n41 | 10 | -81.1+TT |  | 
 | 2 | 26 | 5 | REFSENS | UL harmonic exception | N/A
 |  | n41 | 10 | REFSENS | avoided | 
 | 3 | 26 | 5 | -81.2 | dual uplink operation | IMD3
 |  | n41 | 10 | REFSENS |  | 
 | 4 | 26 | 5 | -72.5 | harmonic mixing | UL1/DL3
 |  | n41 | 10 | REFSENS |  | 
 | 5 | 26 | 15 | -69.5 |  | 
 |  | n41 | 15 | REFSENS |  | 
 | 6 | 26 | 15 | REFSENS | harmonic mixing | N/A
 |  | n41 | 15 | REFSENS | avoiding | 
Table 7.3B.2.3.5-0: Reference sensitivity test requirement for PC3 EN-DC
Proposal 1: It is suggested to correct the “CA configuration” to “EN-DC configuration”, “DL band” to “E-UTRA/NR band”, “CBW” to “UL/DL CBW” and to add a column of “Interference order” in Table 7.3B.2.3.5-0 for EN-DC Refsens test requirements.

## Slide 6: Further considerations on test requirements for EN-DC Refsens (Ⅲ)
Based on the conclusion of action point AP#104.22, the test requirements in old table template will eventually be merged into Table 7.3B.2.3.5-0. However, the Refsens test requirements in Table 7.3B.2.3.5-0 are only for PC3 EN-DC configurations. To make the test requirements more clear on PC2 EN-DC configurations, it is suggested to create a new Table 7.3B.2.3.5-0a to collect the test requirements for PC2 exception types, such as to collect the requirements in Table 7.3B.2.3.5-2a for PC2 harmonic mixing, Table 7.3B.2.3.5-3a for PC2 cross band isolation, and Table 7.3B.2.3.5-5 for PC2 dual uplink. An example of PC2 DC_2A_n41A Refsens test requirements is given as below.
Proposal 2: It is suggested to create a new Table 7.3B.2.3.5-0a to collect the test requirements for PC2 exception types shown as an example as above.
EN-DC configuration | Test ID | E-UTRA/NR band | UL/DL CBW (MHz) | REFSENS test requirement (dBm) | Exception type
DC_2A_n41A | 1 | 2 | 5 | -95.7 | Cross band isolation
 |  | n41 | 100 | REFSENS | 
NOTE 1: The symbol "REFSENS" in this table refers to the reference sensitivity values for single carrier specified in Table 7.3.5-1 of TS 36.521-1 [10] for 2 antenna port E-UTRA band, Table 7.3_1.5-1 of TS 36.521-1 [10] for 4 antenna port E-UTRA band, Table 7.3.2.5-1a and Table 7.3.2.5-1b of TS 38.521-1 [8] for 2 antenna port NR band, Table 7.3.2.5-2a and Table 7.3.2.5-2b of TS 38.521-1 [8] for 4 antenna port NR band, Table 7.3.2.5-2c and Table 7.3.2.5-2d of TS 38.521-1 [8] for PC2 UE on NR FDD bands. |  |  |  |  | 
Table 7.3B.2.3.5-0a: Reference sensitivity test requirement for PC2 EN-DC

## Slide 7: Further considerations on test requirements for EN-DC Refsens (Ⅳ)
For EN-DC Refsens test requirements in Table 7.3B.2.3.5-0 and test requirement tables in old templates, it is observed that some Refsens values include TT while some other values do not include. Readers may confuse if TT is missing in the table or not. For example, in Table 7.3B.2.3.5-4 for Refsens exception due to dual uplink operation for PC3, the exception value for EN-DC configuration DC_3A_n7A has the format of “xx+TT” on band n7 while DC_3A_n8A has the format of “xx” on band n8.
f ≤ 3.0GHz | 3.0GHz < f ≤ 6.0 GHz
0.7 dB | 1.0 dB
Table 7.3B.2.3.5-1a: Test Tolerance (TT) for RX sensitivity level
NR or E-UTRA Band / Channel bandwidth |  |  |  |  |  |  |  |  | 
EN-DC Configuration | EUTRA or NR band | SCS (kHz) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 40 MHz (dBm) | IMD order | Duplex mode
… | … | … | … | … | … | … | … | … | …
DC_3A_n7A | 3 | N/A | REFSENS | - | - | - | - | - | 
 | n7 | 15 | - | -84.6 +TT5 | - | - | - | - | 
DC_3A_n8A | 3 | N/A | - | REFSENS | - | - | - | N/A | FDD
 | n8 | 15 | -88.3 | - | - | - | - | IMD43 | FDD
 | 3 | N/A | - | -86.9 | - | - | - | IMD5 | FDD
 | n8 | 15 | REFSENS | - | - | - | - | N/A | FDD
Table 7.3B.2.3.5-4: Reference sensitivity exceptions due to dual uplink operation for PC3 EN-DC in NR FR1 (two bands)
Observation 2: It is observed that in current EN-DC Refsens test requirement tables, some exception values include TT while some other exception values do not include TT which make readers quite confusing whether TT is missing or not.
Observation 3: It is observed that for Refsens on E-UTRA bands, the TT has already been included in the exception values, while for Refsens on NR bands, the TT is referenced to Table 7.3B.2.3.5-1a with the format of “xx+TT”.
EN-DC Configuration | Test ID | EUTRA/ NR band | SCS (kHz) | 5 MHz (dBm) | 10 MHz (dBm) | 20 MHz (dBm) | 40 MHz (dBm) | Duplex mode | IMD order | Single UL allowed
DC_20A_n28A-n78A | 1 | 20 | N/A | REFSENS | - | - | - | FDD | N/A | 
 |  | n28 | 15 | REFSENS | - | - | - | FDD | N/A | 
 |  | n78 | 15 | - | -86.1 | - | - | TDD | IMD4 | 
 | 2 | 20 | N/A | REFSENS | - | - | - | FDD | N/A | 
 |  | n78 | 15 | - | REFSENS | - | - | TDD | N/A | 
 |  | n28 | 15 | -89.1+TT | - | - | - | FDD | IMD4 | 
Table 7.3B.2.3_1.1.5-1: Reference sensitivity exceptions for Scell due to dual uplink operation for PC3 EN-DC in NR FR1 (three bands)
Missing “+TT” ?
Missing “+TT” ?

## Slide 8: Further considerations on test requirements for EN-DC Refsens (Ⅴ)
For EN-DC Refsens test requirements, it is suggested to have a general rule regarding to the TT. If the Refsens is on E-UTRA band, since the TT has already been considered in the test requirements for single carrier reference sensitivity, there is no need to include extra TT in the EN-DC test requirements. If the Refsens is on NR band, since the TT is referenced to Table 7.3B.2.3.5-1a, the format of “xx+TT” is suggested to be used. An example of applying the TT rules for DC_3A_n8A is given as below.
f ≤ 3.0GHz | 3.0GHz < f ≤ 6.0 GHz
0.7 dB | 1.0 dB
Table 7.3B.2.3.5-1a: Test Tolerance (TT) for RX sensitivity level
NR or E-UTRA Band / Channel bandwidth |  |  |  |  |  |  |  |  | 
EN-DC Configuration | EUTRA or NR band | SCS (kHz) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 40 MHz (dBm) | IMD order | Duplex mode
… | … | … | … | … | … | … | … | … | …
DC_3A_n7A | 3 | N/A | REFSENS | - | - | - | - | - | 
 | n7 | 15 | - | -84.6 +TT5 | - | - | - | - | 
DC_3A_n8A | 3 | N/A | - | REFSENS | - | - | - | N/A | FDD
 | n8 | 15 | -88.3 -89.0+TT | - | - | - | - | IMD43 | FDD
 | 3 | N/A | - | -86.9 | - | - | - | IMD5 | FDD
 | n8 | 15 | REFSENS | - | - | - | - | N/A | FDD
Table 7.3B.2.3.5-4: Reference sensitivity exceptions due to dual uplink operation for PC3 EN-DC in NR FR1 (two bands)
Proposal 3: It is suggested the following rules of using TT should be applied for EN-DC Refsens test requirements.
For Refsens on E-UTRA bands, the format of “xx” is to be used, i.e. “xx” including the Test Tolerance (TT).
For Refsens on NR bands, the format of “xx+TT” is to be used, the Test Tolerance (TT) is referenced to Table 7.3B.2.3.5-1a.

## Slide 9: Thank you!