## Slide 1: Wayforward on TT & MU values in FR1
Orange, Telecom Italia, Vodafone, CMCC, China Unicom, China Telecom, AT&T, Dish
3GPP TSG-RAN5 WG5 Meeting # 79
Busan, South Korea 21st – 25th May 2018
R5-183911r1

## Slide 2: Background
“How to define TT from MU in FR1” was already approved in R5-177454 in Reno:
  Proposal 1-2 : Sub-6GHz TT values about Type 1 TCs are defined with same value as MU for NR.
  Proposal 2-1 : Sub-6GHz TT values about Type 2 TCs are defined as zero in same way as legacy LTE
  (Type 1 is TT ≠0 in LTE, Type 2 is TT=0 in LTE)
For FR1, BW>20MHz there is no agreement yet
Regarding FR2, approach is not approved yet.

## Slide 3: MU&TT Proposal in this meeting
R5-182789r1& R5-182927
Test | Minimum Requirement in TS 38.101-1 | Test Tolerance (TT) | Test Requirement in TS 38.521-1
6.2.1 UE maximum output power | BW ≤ 40MHz f ≤ 3.0GHz Power class 3: 23dBm +2/-2.5 dB 3.0GHz < f ≤ 4.2GHz Power class 3: 23dBm +2/-2.5 dB 4.2GHz < f ≤ 6GHz Power class 3: 23dBm +TBD dB 40MHz < BW ≤ 100MHz Power class 3: 23dBm +2/-2.5 dB | 0.7 dB 1.0 dB 1.5 dB 2.3 dB | Formula: Upper limit + TT, Lower limit – TT Power class 3: 23dBm +2.7/-3.2 dB Power class 3: 23dBm +3/-3.5 dB Power class 3: 23dBm +TBD dB Power class 3: 23dBm +4.3/-4.8 dB
example

## Slide 4: Background: UL coverage for FR1 TDD
R1-1711817 :TDD NR deployment assumptions @3.5GHz:
  Massive MIMO is a defining feature of NR @3.5GHz (typical configuration 64T64R with 128/256 antenna elements)
  Thanks to beam sweeping or other techniques (power boosting etc.) it is expected that all NR physical common and control channels in DL will match or exceed NR-PDSCH coverage at its maximum beamformed range
  UL/DL traffic asymmetry is expected to be heavily DL biased, e.g., 1:3 to 1:10
  To support this traffic asymmetry the UL/DL transmission times will also be highly asymmetric, e.g., at least 1:3
  The UE is power limited
These assumptions lead to an UL NR-PUSCH coverage which is 10 to 15 dB lower than DL 3500 in TDD for a downlink oriented UL/DL frame configuration of 1:3 and a PUSCH/PDSCH data rate asymmetry of 1:10
These assumptions lead to an UL NR-PUSCH coverage which is 6dB lower than DL 700MHz in TDD for a downlink oriented UL/DL frame configuration of 1:3 and a PUSCH/PDSCH data rate asymmetry of 1:10

## Slide 5: MU &TT impact on coverage
Upper limit + TT, Lower limit – TT
TT=2,3dBm & MU= 2/-2,5 dBm->+4.3/-4.8 dB
Pmax= 18,2dBm can be measured as 23dBm
These assumptions lead to an UL NR-PUSCH coverage which is 14,8 to 19,8 dB lower than DL 3500MHz in TDD
These assumptions lead to an UL NR-PUSCH coverage which is 10,8dB lower than DL 700MHz in TDD
and this we are talking in conducted!!!

## Slide 6: MU &TT impact on QoS
Upper limit + TT, Lower limit – TT
TT=2,3dBm & MU= 2/-2,5 dB ->+4.3/-4.8 dB
Pmax= 27,3dBm can be measured as 23dBm
UL Interference, SAR, energy consumption
and this is for conducted measurement!!!

## Slide 7: MU values issues
Some MU values are coming from the beginning of LTE technology.. 10years ago…
Expect more cooperation from SS vendors and provide 3GPP new realistic values, based on their equipment evolution and progress.

## Slide 8: Proposal
Proposal1: The proposed TT Values are included in the spreadsheet file, based on the following assumption:
  The TT values should not exceed the value adopted in pure LTE (TS 36.521-1 BW ≤ 20 MHz f ≤ 4.2 GHz). It is assumed that the amount of uncertainty exceeding the E-UTRAN shall not be considered.
Proposal2: for FR1 and BW>20MHz, MU values should be revised