## Slide 1: Wayforward on TT & MU values in FR1
Orange, Telecom Italia, Vodafone, CMCC, China Unicom, China Telecom, AT&T, Dish
3GPP TSG-RAN5 WG5 Meeting # 79
Busan, South Korea 21st – 25th May 2018
R5-183911r3

## Slide 2: Background
“How to define TT from MU in FR1” was already approved in R5-177454 in Reno:
  Proposal 1-2 : Sub-6GHz TT values about Type 1 TCs are defined with same value as MU for NR.
  Proposal 2-1 : Sub-6GHz TT values about Type 2 TCs are defined as zero in same way as legacy LTE
  (Type 1 is TT ≠0 in LTE, Type 2 is TT=0 in LTE)
For FR1, BW>20MHz there is no agreement yet
Regarding FR2, approach is not approved yet.

## Slide 3: Background: UL coverage for FR1 TDD
R1-1711817 :TDD NR deployment assumptions @3.5GHz:
  Massive MIMO is a defining feature of NR @3.5GHz (typical configuration 64T64R with 128/256 antenna elements)
  Thanks to beam sweeping or other techniques (power boosting etc.) it is expected that all NR physical common and control channels in DL will match or exceed NR-PDSCH coverage at its maximum beamformed range
  UL/DL traffic asymmetry is expected to be heavily DL biased, e.g., 1:3 to 1:10
  To support this traffic asymmetry the UL/DL transmission times will also be highly asymmetric, e.g., at least 1:3
  The UE is power limited
These assumptions lead to an UL NR-PUSCH coverage which is 10 to 15 dB lower than DL 3500 in TDD for a downlink oriented UL/DL frame configuration of 1:3 and a PUSCH/PDSCH data rate asymmetry of 1:10
These assumptions lead to an UL NR-PUSCH coverage which is 6dB lower than DL 700MHz in TDD for a downlink oriented UL/DL frame configuration of 1:3 and a PUSCH/PDSCH data rate asymmetry of 1:10

## Slide 4: MU Proposal (example)
R5-183910r2
38.521-1 | 6 | trasmitter characteristics |  | 
38.521-1 | 6.2 | transmit power |  | 
38.521-1 | 6.2.1 | UE maximum output power | BW ≤ 20MHz ±0.7 dB, f ≤ 3.0GHz (P ≥ 0dBm) ±1.0 dB, 3.0GHz < f ≤ 4.2GHz (P ≥ 0dBm) ±1.3 dB, 4.2GHz < f ≤ 6.0GHz (P ≥ 0dBm) 20 MHz < BW ≤ 40MHz ±0.7 dB, f ≤ 3.0GHz (P ≥ 0dBm) ±1.0 dB, 3.0GHz < f ≤ 4.2GHz (P ≥ 0dBm) ±1.5 dB, 4.2GHz < f ≤ 6.0GHz (P ≥ 0dBm) 40MHz < BW ≤ 100 MHz ±1.4 dB, f ≤ 3.0GHz (P ≥ 0dBm) ±1.6 dB, 3.0GHz < f ≤ 4.2GHz (P ≥ 0dBm) ±1.6 dB, 4.2GHz < f ≤ 6.0GHz (P ≥ 0dBm) | BW ≤ 20MHz 0.7 dB, f ≤ 3.0GHz 1.0 dB, 3.0GHz < f ≤ 4.2GHz 1.3 dB, 4.2GHz < f ≤ 6GHz 20 MHz < BW ≤ 40MHz 0.7 dB, f ≤ 3.0GHz 1.0 dB, 3.0GHz < f ≤ 4.2GHz 1.5 dB, 4.2GHz < f ≤ 6.0GHz 40MHz < BW ≤ 100MHz 1.4 dB, f ≤ 3.0GHz 1.6 dB, 3.0GHz < f ≤ 4.2GHz 1.6 dB, 4.2GHz < f ≤ 6.0GHz
Revised

## Slide 5: Discussion about TT < MU
There is a wide consensus among operators to adopt an approach with minimal TT with strong preference for adopting TT = 0.
  a minimal TT can also be accepted, a reasonable value is represented by LTE values with f ≤ 4.2 GHz and BW ≤ 20 MHz, the lately introduced values for eLAA and V2V shall not me considered.
a minimal TT approach (with TT < MU) introduces a fairer method among operators and UE/Chipset Vendor (R5-073326)
  Shared Risk (TT = 0):
    50% probability to harm the overall system performance  Risk for Operators,
    a 50% probability that a conformant UE is considered not compliant  Risk for UE manufactures
  Never Fail a good UE (TT = MU):
    97.5% probability to harm the overall system performance  Risk for Operators,
    a 2.5% probability that a conformant UE is considered not compliant  Risk for UE manufactures.
  TT < MU:
    Minimal TT  more balanced risk among the parties
The RAN4 already adopted the TT < MU method for OTA since many releases with the introduction of minimal TT values (i.e. 1 dB for TRP).
The minimal TT of 1 dB have been adopted for OTA across frequencies and access technologies since many releases,
  for conducted measure is not realistic to have bigger values than values defined for OTA.
new

## Slide 6: TT < MU Proposal (example)
Attached spreadsheet
38.521-1 | 6 | trasmitter characteristics |  | 
38.521-1 | 6.2 | transmit power |  | 
38.521-1 | 6.2.1 | UE maximum output power | BW ≤ 20MHz ±0.7 dB, f ≤ 3.0GHz (P ≥ 0dBm) ±1.0 dB, 3.0GHz < f ≤ 4.2GHz (P ≥ 0dBm) ±1.3 dB, 4.2GHz < f ≤ 6.0GHz (P ≥ 0dBm) 20 MHz < BW ≤ 40MHz ±0.7 dB, f ≤ 3.0GHz (P ≥ 0dBm) ±1.0 dB, 3.0GHz < f ≤ 4.2GHz (P ≥ 0dBm) ±1.5 dB, 4.2GHz < f ≤ 6.0GHz (P ≥ 0dBm) 40MHz < BW ≤ 100MHz ±1.4 dB, f ≤ 3.0GHz (P ≥ 0dBm) ±1.6 dB, 3.0GHz < f ≤ 4.2GHz (P ≥ 0dBm) ±1.6 dB, 4.2GHz < f ≤ 6.0GHz (P ≥ 0dBm) | BW ≤ 20MHz 0.7 dB, f ≤ 3.0GHz 1.0 dB, 3.0GHz < f ≤ 4.2GHz [1.0] dB, 4.2GHz < f ≤ 6GHz 20 MHz < BW ≤ 40MHz 0.7 dB, f ≤ 3.0GHz 1.0 dB, 3.0GHz < f ≤ 4.2GHz [1.0] dB, 4.2GHz < f ≤ 6.0GHz 40MHz < BW ≤ 60MHz [1.0] dB, f ≤ 3.0GHz [1.0] dB, 3.0GHz < f ≤ 4.2GHz [1.0] dB, 4.2GHz < f ≤ 6.0GHz
new

## Slide 7: TT < MU Proposal
Proposal: The proposed TT Values are included in the spreadsheet file, based on the following assumption:
  The TT values should not exceed the value adopted in pure LTE (TS 36.521-1 BW ≤ 20 MHz f ≤ 4.2 GHz). It is assumed that the amount of uncertainty exceeding the E-UTRAN shall not be considered.