## Slide 1: Specification structure of FR2 NSA UL CA
NTT DOCOMO, INC.
3GPP TSG-RAN5 Meeting #83 R5-193825r2
Reno, Nevada, United States, 13th May 2019 - 17th May 2019
Agenda Item : 5.3.5.17
Document for : Discussion and Endorsement

## Slide 2: Summary
Introduction
  The purpose of this contribution is to define “How to treat EN-DC configurations with 2 to 8 UL CCs”.
Observations
  CA configurations up to UL 8 CCs (e.g. CA_n257M, 100MHz x 8 CC) are captured in Rel-15 TS 38.101-2.
  Only single UL EN-DC configurations (e.g. DC_1A_n257A) are captured in Rel-15 TS 38.101-3.
  EN-DC configurations up to UL 8 CCs (e.g. DC_1A_n257M) are captured in Rel-16 TS 38.101-3 (Feb-2019 version).
  EN-DC configurations up to UL 8 CCs are release independent from Rel-15 according to TS 38.307.
Proposals
  FR2 NSA Transmit test cases about 2 to 8 UL CCs to be introduced with Rel-16 WI.
  Test applicability of these TCs to be defined as below.
    This test case applies to all types of E-UTRA UE release 15 and forward, supporting inter-band EN-DC including FR2 with XCCs
  To update Rel-16 WP to include up to 8 UL CCs configuration. (Possible options are described in slide #3.)
  To introduce FR2 NSA Transmit test cases with structure / numbering described in slide #4

## Slide 3: [Proposal 3] WP updates
Following is current WP of Rel-16 NR. (except for SUL cases)
  “LTE (≤ 5 CCs) + FR2 (≤ 8DL / ≤ 8UL)” is not covered and corresponding items should be introduced.
  The number of items will increase dramatically if items are defined per “number of CCs”
Type of configuration | Current Completeness | Number of configs | Number of RAN4 completed configs. | Number of company assigned configs. | Number of completed configs.
EN-DC of 1 LTE band (1DL/1UL) and 1 NR Band (1DL/1UL) | 0.0% | 1326 (+427) | 446 | 3 | 0
EN-DC of 2 bands LTE inter-band CA (2DL/1UL) and 1 NR band (1DL/1UL) | 0.0% | 882 (+104) | 44 | 0 | 0
EN-DC of 3 bands LTE inter-band CA (3DL/1UL) and 1 NR band (1DL/1UL) | 0.0% | 920 (+118) | 568 | 0 | 0
EN-DC of 4 bands LTE inter-band CA (4DL/1UL) and 1 NR band (1DL/1UL) | 0.0% | 277 (+48) | 146 | 4 | 0
EN-DC of 5 bands LTE inter-band CA (5DL/1UL) and 1 NR band (1DL/1UL) | 0.0% | 0 | 0 | 0 | 0
EN-DC of x bands (x=1,2,3,4) LTE inter-band CA (xDL/1UL) and 2 bands NR inter-band CA (2DL/1UL) | 0.0% | 648 (+309) | 221 | 0 | 0
NR intra-band CA for xCC DL/yCC UL including contiguous and non-contiguous spectrum (x>=y) | 0.0% | 344 (+212) | 118 | 1 | 0
NR Inter-band CA for 2 bands DL with x bands UL (x=1,2) FR1 and/or FR2 | 0.0% | 340 (+241) | 31 | 0 | 0
NR Inter-band DC for 2 bands DL with x bands UL (x=1,2) FR1 and/or FR2 | 0.0% | 0 | 0 | 0 | 0

## Slide 4: [Proposal 4] Spec structure
Same structure in receiver tests can be reused. (Blue highlighted parts are new introduced.)
Clause | Title
6.X | Transmitter test
- 6.XB | - Transmitter test for EN-DC
- 6.XB.1 | - Transmitter test for intra-band contiguous EN-DC
- 6.XB.2 | - Transmitter test for intra-band non-contiguous EN-DC
- 6.XB.3 | - Transmitter test for inter-band EN-DC within FR1
- 6.XB.4 | - Transmitter test for inter-band EN-DC including FR2
- 6.XB.4.1 | - Transmitter test for inter-band EN-DC including FR2 (2 CCs)
- 6.XB.4.2 | - Transmitter test for inter-band EN-DC including FR2 (3 CCs)
- 6.XB.4.3 | - Transmitter test for inter-band EN-DC including FR2 (4 CCs)
- 6.XB.4.4 | - Transmitter test for inter-band EN-DC including FR2 (5 CCs)
- 6.XB.4.5 | - Transmitter test for inter-band EN-DC including FR2 (6 CCs)
- 6.XB.4.6 | - Transmitter test for inter-band EN-DC including FR2 (7 CCs)
- 6.XB.4.7 | - Transmitter test for inter-band EN-DC including FR2 (8 CCs)
- 6.XB.5 | - Transmitter test for inter-band EN-DC including both FR1 and FR2
7.Y | Receiver test
- 7.YB | - Receiver test for EN-DC
- 7.YB.0 | - Minimum Conformance Requirements
- 7.YB.1 | - Receiver test for intra-band contiguous EN-DC (2 CCs)
- 7.YB.2 | - Receiver test for intra-band non-contiguous EN-DC (2 CCs)
- 7.YB.3 | - Receiver test for inter-band EN-DC within FR1 (2 CCs)
- 7.YB.4 | - Receiver test for inter-band EN-DC including FR2
- 7.YB.4.1 | - Receiver test for inter-band EN-DC including FR2 (2 CCs)
- 7.YB.4.2 | - Receiver test for inter-band EN-DC including FR2 (3 CCs)
- 7.YB.4.3 | - Receiver test for inter-band EN-DC including FR2 (4 CCs)
- 7.YB.4.4 | - Receiver test for inter-band EN-DC including FR2 (5 CCs)
- 7.YB.4.5 | - Receiver test for inter-band EN-DC including FR2 (6 CCs)
- 7.YB.5 | - Receiver test for inter-band EN-DC including both FR1 and FR2

## Slide 5: [Appendix] Observation 1
Observation 1
  CA configurations up to UL 8 CCs (e.g. CA_n257M, 100MHz x 8 CC) are captured in Rel-15 TS 38.101-2.
Comments
  Following is extract of TS 38.101-2 (v15.5.0)

## Slide 6: [Appendix] Observation 2
Observation 2
  Only single UL EN-DC configurations (e.g. DC_1A_n257A) are captured in Rel-15 TS 38.101-3.
Comments
  Following is extract of TS 38.101-3 (v15.5.0), and UL CA configuration is not captured in this version.

## Slide 7: [Appendix] Observation 3
Observation 3
  EN-DC configurations up to UL 8 CCs (e.g. DC_1A_n257M) are captured in Rel-16 TS 38.101-2 (Feb-2019 version).
Comments
  Following is extract of TS 38.101-3 (v16.x.x, Feb-2019), and UL CA configurations are captured in this version.

## Slide 8: [Appendix] Observation 4
Observation 4
  EN-DC configurations up to UL 8 CCs are release independent from Rel-15 according to TS 38.307.
Comments
  Following is extract of TS 38.307 (v15.2.0), and UL CA configurations (up to 8 CCs) are release independent.
    TS 38.307 : Requirements on User Equipments (UEs) supporting a release-independent frequency band

## Slide 9: [Appendix] Status of RAN4
Comments
  RAN4 draft CR to update TS 38.101-3 was treated in Monday session during RAN4#91 (May-2019).
  Though the document is not approved yet due to other concerns, RAN4 has reached common understanding that EN-DC requirements shall also refer to the FR2 UL CA requirements in TS 38.101-2. With this agreement above, RAN5 can start corresponding work now since RAN4 dependency was solved.
R4-1905684 draft CR of modification on reference for inter-band EN-DC including FR2 for TS 38.101-3 38.101-3 CR- rev Cat: (Rel-15) v15.5.0 Source: NTT DOCOMO INC.
  Abstract:
  Discussion:
  Huawei: For uplink CA requirements, there are some open issues for 3UL CA are still discussing.
  Ericsson: For standalone requirements, there is some notes in the applicability section. It is clear to better clarify the applicability of standalone requirements. For anchor agnostic testing, we also have to clarify this.
  => It is common understanding the EN-DC requirements shall also refer to the FR2 uplink CA requirements.
  Decision: The document was Revised in R4-1907594