## Slide 1: Band n259 core requirement
NTT DOCOMO, INC.
3GPP TSG-RAN5 Meeting #85 R5-197731r1
Reno, Nevada, United States, 18th Nov 2019 - 22nd Nov 2019
Agenda Item : 5.3.18.10
Document for : Information

## Slide 2: 1. Introduction
During the last RAN5#84 (Aug-2019), WID for new NR band n259 was endorsed in [1].
  This WID includes not only Band n259 but also other new bands and extensions.
Core requirement for Band n259 is not completed yet.
  Agreements in RAN4 are not captured in the latest core specifications (TS 38.101-2, 3).
  In order to treat band n259 in RAN5, it is beneficial to summarize RAN4 agreements and endorsements first.
The purpose of this contribution is to summarize the core requirement for Band n259.
  Definition of the band
  Time plan in RAN4 (and RAN Plenary)
  Progress (agreements and open issues) in RAN4

## Slide 3: 2-1. Definiton of Band n259
Band definition for Band n259 (according to WF [2])
Summary
  Frequency range is 39.5 to 43.5 GHz.
  Band n259 upper limit (43.5 GHz) exceeds Band n260 upper limit (40.0 GHz).
    43.5 GHz also exceeds current MU assumption (≤ 40.8 GHz). This topic to be treated in [3].
  Total bandwidth is 4.0 GHz, and also exceeds current maximum value (3.0 GHz of Band n260 etc.).
Operating Band | Uplink (UL) operating band BS receive UE transmit |  |  | Downlink (DL) operating band BS transmit UE receive |  |  | Duplex Mode
 | FUL_low – FUL_high |  |  | FDL_low – FDL_high |  |  | 
n257 | 26500 MHz | – | 29500 MHz | 26500 MHz | – | 29500 MHz | TDD
n258 | 24250 MHz | – | 27500 MHz | 24250 MHz | – | 27500 MHz | TDD
n259 | 39500 MHz | – | 43500 MHz | 39500 MHz | – | 43500 MHz | TDD
n260 | 37000 MHz | – | 40000 MHz | 37000 MHz | – | 40000 MHz | TDD
n261 | 27500 MHz | – | 28350 MHz | 27500 MHz | – | 28350 MHz | TDD

## Slide 4: 2-2. Time plan (core)
During the last RAN#85 (Sep-2019), completion target of Band n259 (core) was extended to Mar-2020 in [4].
  RAN4 target is RAN4#94 (Feb-2020), and 2 meetings are left.
  RAN5 target is RAN5#87 (May-2020), and 3 meetings are left.
Work plan are summarized as below according to [2].
  RAN4#93 (Nov-2019) : Transmitter and receiver requirements and draft CRs will be agreed.
  RAN4#94 (Feb-2020) : All related CRs including RRM will be agreed.
 | Aug-19 | Sep-19 | Oct-19 | Nov-19 | Dec-19 | Jan-20 | Feb-20 | Mar-20 | Apr-20 | May-20 | Jun-20
RAN4 |  |  |  |  |  |  |  |  |  |  | 
RAN5 |  |  |  |  |  |  |  |  |  |  | 
RAN |  |  |  |  |  |  |  |  |  |  | 
#93
#94
#94bis
#95
#85
#86
#87
#86
#87
#88

## Slide 5: 2-3. Progress in RAN4
Agreements
  Minimum peak EIRP and EIS requirements for PC3 was agreed in [5].
Open issues (RF)
  Non band agnostic test cases (e.g. ACLR)
    Minimum requirement for band depended test cases are proposed by [6] at RAN4#94 (Nov-2019).
  EIRP and EIS Spherical coverage
  Multi-band relaxation including Band n259
    MBR including Band n259 is proposed by [7] at RAN4#93 (Nov-2019).
Operating band | Frequency range | Min peak EIRP (dBm) | REFSENS (dBm/50MHz)
n257 | 26.5 – 29.5 GHz | 22.4 | -88.3
n258 | 24.25 – 27.5 GHz | 22.4 | -88.3
n259 | 39.5 – 43.5 GHz | 18.7 | -84.7
n260 | 37.0 – 40.0 GHz | 20.6 | -85.7
n261 | 27.5 – 28.35 GHz | 22.4 | -88.3

## Slide 6: 3. Conclusion
Band n259 work in core WG is still ongoing. (Progress is roughly 50%.)
  Completion target of RAN4 is Feb-2020.
  2 meetings are left for RAN4 while 3 meetings for RAN5.
Frequency range of Band n259 exceeds current upper limits.
  Upper edge of Band n259 is 43.5 GHz, while that of FR2b is 40.8 GHz.
Some transmitter and receiver requirements are already agreed in RAN4.
  Remaining issues are 1) Spherical coverage, 2) Multi-band relaxation.
  With proposals in [6] and [7], Band n259 core requirement is almost completed.
Observation
  In order to complete conformance test specification in time (RAN5#87), it is highly required to proceed RAN5’s Band n259 work in parallel with RAN4.

## Slide 7: References
[1] R5-197140 : “New WID on UE Conformance Test Aspects - Introduction of new Rel-16 NR bands and extension of existing NR bands”, Ericsson, RAN5#84 (Aut-2019)
[2] R4-1912182 : “WF for Introduction of band n259 WI”, Ericsson, RAN4#92bis (Oct-2019)
[3] R5-197733 : “Frequency range of Band n259”, NTT DOCOMO, INC., RAN5#85 (Nov-2019)
[4] RP-191880 : ”Revised WID: introduction of Band n259”, Ericsson, RAN#85 (Sep-2019)
[5] R4-1912977 : “WF on EIRP and EIS for n259”, Huawei, HiSilicon, RAN4#92bis (Oct-2019)
[6] R4-1914191 : “n259 associated band specific requirements”, NTT DOCOMO, INC., RAN4#93 (Nov-2019)
[7] R4-1913546 : “Multi-band framework for band n259”, Apple Inc., RAN4#93 (Nov-2019)