## Slide 1: FR2 NR TT Way Forward update
3GPP TSG-RAN WG5 Meeting #85
Reno, Nevada, USA, 18 – 22 November 2019
R5-198302r1
Telecom Italia, Ericsson

## Slide 2: Background
At RAN5 5G-AH#3 New FR2 MU values for IFF method introduced in R5-186344
At RAN5#81 several contributions regarding TT are presented:
  R5-186888: proposing TT = 0 and highlight Network coverage impact
  R5-187576: defining upper bound for TTs (TT = 2.1 dB)
  R5-187568: proposing TT = 0.65xMU
  R5-187235: proposing basically TT = 0.82xMU
At RAN5#81 a WF for FR2 in TS 38.521-2 is agreed in R5-188058 and a MU update in R5-188224 and R5-188225
At RAN RAN5 5G-AH#4 MU values are updated in TS 38.903 and Spherical Coverage MU values are introduced in R5-190576
At RAN5#82 contributions regarding TT spherical coverage test cases are presented (still under discussion):
  R5-191727 and R5-191836: proposing TT = 0.65xMU
  R5-192657: proposing TT = 2 dB Upper bound
At RAN5#83 Agreed SEM MUs and TTs (R5-195159, R5-195158)
At RAN5#84 Quiet Zone sizes and MU changes (R5-197498, R5-197505, R5-197501) and new CA TCs
At RAN5#85 it is agreed the impact of systematic error in the TT

## Slide 3: Agreed FR2 WF TS 38.521-2
Except the FFS and empty items, the proposed FR2 TT Values are included in the spreadsheet file, based on the following assumption:
TTs shall be defined case by case
TT = 0.65 * MU (the upper bound of MU value used for TT calculation is 5.5 dB, 0.65 upper bound TT/MU ratio). Applies to following Test Cases:
    Min Peak EIRP
    Max TRP
    Reference Sensitivity
    ACLR and SEM (no MU Upper Bound Applied)
Min EIRP at 50t%-tile CDF and EIS spherical coverage still under discussion.
TT = 0.50 * MU (the upper bound of MU value used for TT calculation is 0.01ppm , 0.5 upper bound TT/MU ratio) Applies to following Test Cases:
    Frequency error
Since TT have dependency from MU, no TT value can be defined if the corresponding MU is not finalized (business as usual).
TT values may decrease based on the experience on the field and when all parties will have more confidence in device performance
The TT values and the method to derive the TT defined until RAN5#85 (November 2019) for execution in any possible certification. At RAN5#85 the TT values shall be re-evaluated
  Required actions are specified in editor’s note in Annex F
TTUL CA = TTSINGLE for CA configuration that aggregated BW ≤ 400MHz (agreed in R5-195150) for Intra-band contiguous CA and Priority 1, 2 transmit test cases

## Slide 4: TT and systematic error agreement
MTSU in Annex F.1 is defined for two purposes
  Requirements on test system
  Basis for calculating TT
With regard of bullet 1 above, MTSU defined in Annex F.1 will be a symmetric value regardless of whether there exist systematic errors or not (observation 1 in R5-198446r1)
For derivation of TT (Annex F.3) it is agreed that systematic errors in MTSU do not always have a negative effect on the UE fail rate. In such a case it should not be included in the TT
  This is valid for any lower limit test case (min req > limit)
  Example:
    Annex F.1 MTSU = +/-X dB (including systematic error of Y dB due to noise)
    Annex F.3 TT:
      Calculated using MTSU but substracting influence of noise:
      TT = (TT ratio) * (X- Y)

## Slide 5: Attached Spreadsheets update
FR2 TT After RAN5#84
  Quiet Zone sizes and MU changes (R5-197498, R5-197505, R5-197501)
  New TCs:
    Additional Spurious emission
    Spherical coverage for CA
    Minimum output power for CA
    Transmit ON/OFF time mask for CA
    General ON/OFF time mask for UL MIMO
    Error Vector magnitude for CA
    Carrier leakage for CA
    Transmitter Spurious emissions for CA
    Spurious emission band UE co-existence for CA
    Additional spurious emission for CA
    Reference sensitivity power level for CA