## Slide 1
NB-IoT NTN: UE Coarse Location Information Reporting
Rel-18
MediaTek Inc., Airbus, CEWiT, Echostar, ESA, Gatehouse, Inmarsat/Viasat, JSAT, Ligado, Lockheed Martin, Novamint, OQ Technology, Sateliot, Skylo, Thales, TNO
SP-231594
3GPP TSG SA#102 SP-231594
December 11 – 15, 2023 Agenda Item 18.2
Edinburgh, UK

## Slide 2: Need for NB-IoT Coarse Location Reporting
RRC reporting of UE Coarse Location is possible for eMTC, NR
RRC reporting of UE Coarse Location is prevented for NB-IoT (privacy issues)
3GPP TS 36.331 / 38.331 define
  coarseLocationInfo: This field indicates the coarse location information reported by the UE. This field is coded as the Ellipsoid-Point IE defined in TS 37.355 [109]. The first/leftmost bit of the first octet contains the most significant bit. The least significant bits of degreesLatitude and degreesLongitude are set to 0 to meet the accuracy requirement which corresponds to a granularity of approximately 2 km. It is up to UE implementation as to how many LSBs are set to 0 to meet the accuracy requirement.
  Upon network request, after AS security is established in connected mode, BL UEs and UEs in enhanced coverage can report its coarse UE location information (most significant bits of the GNSS coordinates, ensuring an accuracy in the order of 2km) to the eNB if available
Major concerns from satellite community have been expressed and repeated on resulting system inefficiencies in some NB-IoT NTN deployments
  SA2/Feb 2022 had previously concluded: if an NB-IoT UE does not provide any location information over AS to an eNB, then SA2 assumes that the E-UTRAN would provide its best estimate of the UE’s location as a TAI+CGI to the MME when the NB-IOT UE is entering or in the ECM CONNECTED state. SA2 concludes that there are no serious issues from an SA2 perspective if an NB-IoT UE does not provide any location information over AS to an eNB
  Key concerns:
    The “best estimate” is just not good enough without knowledge of the UE Coarse Location – this was one of the key reasons why the UE Coarse Location information was introduced in the first place
    Insufficiently accurate information reported to the MME (ULI) could trigger significant signaling overhead (considering the #UEs accessing the network) as a) the MME will proceed with MM/SM procedures before b) initiation of the UE location procedure and c) potentially triggering detaching the UE
    With a coverage area across misc. regulatory areas, the UE location needs verification for every UE in the area
  Reporting of the UE Coarse Location Information at NAS is a necessary simple effective means to address these concerns and put all 3GPP NTN technologies reasonably on par.
Background
SP-231594
There is an undeniably urgent commercial need to address the concerns from the satellite community and introduce UE Coarse Location Reporting at NAS

## Slide 3: Proposal
Basic Principle
Inclusion of UE Coarse Location Reporting capability in UE Core Network Capabilities (this allows a supporting MME to request the information from the UE)
Reporting of UE Coarse Location Information, if a security context is established between the UE and the network, in Attach, TAU procedures and applicable ESM procedures (incl. Service Request, PDN connectivity Request), upon network request only
MME usage of the reported UE Coarse Location Information and ULI to determine whether or not the UE is allowed to operate in its location
The proposal piggy-backs the information into existing NAS signaling (Attach, TAU and applicable ESM signaling) as early as possible in these procedures.
A CR to 23.401 is provided in SP-231595
Attach Procedure
UE Coarse Location Reporting capability in UE CN capability (Attach Request)
MME request of UE Coarse Location reporting in Security Mode Command and UE response with Coarse Location Information in Security Mode Complete (this message is always ciphered)
  NOTE: SMC can be triggered at any time by the MME
TAU Procedure
UE Coarse Location Reporting capability in UE CN capability (TAU Request)
UE reporting of Coarse Location Information in TAU Request message, if the TAU Request message is ciphered, and if the network had previously requested the UE to report its Coarse Location Information
MME request of UE Coarse Location reporting in Security Mode Command and UE response in Security Mode Complete (always ciphered)
ESM
Inclusion of Coarse Location Information in Control Plane Service Request, Service Request and PDN connectivity request messages
  NOTE: Partial ciphering of Control Plane Service Request is possible as of today. Partial ciphering of Service request would be necessary (as Initial NAS message)
UE reporting of UE Coarse Location Information to the MME
[1/2]
SP-231594

## Slide 4: Proposal
SA#102 Plenary is invited to recommend the introduction of UE Reporting of Coarse Location Information at NAS in Rel-18 for NB-IoT NTN by:
  Requesting SA2 to define a solution for SA#103/March 2024 approval, using CR23.401 in SP-231595 as a starting point, starting in SA2#160e/January 2024.
[2/2]
SP-231594
There is an undeniably urgent commercial need to address the concerns from the satellite community and introduce UE Coarse Location Reporting at NAS