## Slide 1: Proposal on R19 SA2 Ambient IoT Scope, Work Tasks and TUs
TSG SA Meeting #102 SP-231628
December 11 – 15, 2023
Huawei, HiSilicon

## Slide 2
Rel-19 SA2 Ambient IoT Device Scope Proposal
Success of the Rel-19 Ambient IoT project depends on a properly-focused scope.
As proposed in RP-233880, considering market demands, and competition from other technologies, the sourcing sourcing companies consider that:
  Device A and Device B need to be addressed first, and are in the scope of Rel-19.
  Device C is also important to the 3GPP ecosystem, and can be addressed in a second Release of Ambient IoT.
Rel-19 Ambient IoT is scoped to Device A and Device B
(Background) R18 RAN-level SI (TR 38.848), defined three Devices:
  Device A: No energy storage, no independent signal generation/amplification, i.e. backscattering transmission.
  Device B: Has energy storage, no independent signal generation, i.e. backscattering transmission. Use of stored energy can include amplification for reflected signals.
  NOTE: From the SA2 point of view, Device A and Device B can be considered the same type, i.e. both do NOT support autonomous communication with the network.
  Device C: Has energy storage, has independent signal generation, i.e., active RF components for transmission.

## Slide 3
Rel-19 SA2 Ambient IoT Topology Scope Proposal
Topology 1 is the basic fundamental network topology and must be supported in Rel-19.
The other topologies have a strong relationship with the supported Devices and existing RAN recommendations for work.
Other topologies for indoor and outdoor coverage using intermediate/assisting nodes are only relevant if topology 1 is not supported, do not necessarily offer better coverage depending on circumstance, or could have unpredictable BS interference.
Rel-19 Ambient IoT is scoped to Topology 1
(Background) R18 RAN-level SI (TR 38.848), defined 4 topologies:
  Topology 1: AIoT Device direct to RAN Node.
  Topology 2: Use of an Intermediate Node between the AIoT Device and RAN Node.
  Topology 3: Use of an Assisting Node to transfer either UL or DL traffic to/from the AIoT Device.
  Topology 4: A standalone Reader (already suggested to be down scoped).

## Slide 4
R19 SA2 Ambient IoT Work Tasks and Time Unit Proposal
Work Tasks NOTE 1: Coordination with RAN is required to determine which types of the Ambient IoT devices and which connectivity topologies as defined in TR38.848 will be in the scope of this study for all work tasks. | RAN dependency | Study TU + Normative TU 12 + 12 | TU update based on Device A and Device B, and Topology 1 10 (study TU) +8 (normative TU) 10 + 8
WT#1 Architecture to support Ambient IoT NOTE 2: WT#1 will take into account the RAN study outcome and outcome of WT#3, WT#4 and WT#5. | YES | 1.5 + [1.5] | 1 + 0.25 There is no need to study how to adapt the architecture to support Device C or Intermediate/Assisting Nodes.
WT#3 Identification, Subscription, Registration and Connection management to support Ambient IoT devices WT#3.1 Study whether subscription management, registration management and/or connection management are necessary, and if so identify the necessary state machine(s), procedures and functionality considering the Ambient IoT devices capability and characteristics; WT#3.2 Study whether and how reachability and paging apply to Ambient IoT device(s) considering the Ambient IoT devices capability and characteristics, and if so, what are the impacts. WT#3.3 Study how to identify Ambient IoT device or group of devices and how to format the identifier. NOTE 2a: Network Access Control like functionality e.g. UAC like functionality could be considered. NOTE 2b: NAS based Congestion control is not in the scope of this study. | Maybe (depend on the connectivity topologies) | 5 + [5] | 4.5 + 4 As Device A and Device B cannot autonomously connect to the network there is not need to support aspects like paging strategies, mobility, and whether existing subscriptions, registration or connection management applies to Device C. The normative will be more how to add new features then adapt/merge into existing concepts or features, therefore the normative workload is simplified.
WT#4 Ambient IoT Services WT#4.1 Study how to support information transfer for Ambient IoT services and related system functionality. NOTE 3: including whether there is a need to support session based transfer between Ambient IoT device and the network considering the device types and capabilities. WT#4.2 Study which Ambient IoT services enabled in WT#4.1 to be exposed to AF and how. | Maybe (depend on the connectivity topologies) | 4 + [4] | 4 + 3.5 Many of the services would naturally be applicable to all device types, but overall there will be simplification in the normative phase due to only Device A and Device B
WT#5 Architecture support of the following security related aspects WT#5.1 Study architecture aspects to support security, including validation of the device’s ID. WT#5.2 Study how to securely disable the capability of an Ambient IoT device or a group of Ambient IoT devices to transmit RF signals. NOTE 4: WT#5 requires coordination with SA3. | Maybe | 1.5 + [1.5] | 0.5 + 0.25 Many of the security aspects are have to be simplified for the lower complexity only devices.
NOTE 5: Charging aspects for Ambient IoT will be studied by SA5. | If Rel-19 Device type only considers device A and device B, TU can be reduced accordingly |  | 

## Slide 5
R19 SA2 Ambient IoT Per Meeting Plan
According to the timeline in SP-231629, and the TU proposal in slide 4, per meeting plan is as below
Meetings for study phase (5) |  |  |  | Meeting for normative phase(3) | Meetings for normative phase (4) |  |  | 
Jan 24 | Feb 24 | Apr 24 | May 24 | Aug 24 | Oct 24 | Nov 24 | Jan 25 | Feb25
TDOCs for: Skeleton TR scope Architecture assumption Architecture requirement New Key issues New solutions Target completeness: 20% | TDOCs for: New key issue (last chance) New solutions TR scope updates Architecture assumption & requirement updates Key issues updates Solutions Target completeness: 40% | TDOCs for: New solutions (last chance) Solutions updates Target completeness: 60% | TDOCs for: Solutions updates Solution evaluations Interim conclusion Target completeness: 80% | TDOCs for: Finalize solution evaluation Final TR conclusion WID proposal Target completeness: 100% | TDOCs for: Add solutions to TS (based on TR conclusions). | TDOCs for: Add solutions to TS (based on TR conclusions). Continued TS updates (based on TR conclusions). | TDOCs for: Add solutions to TS (based on TR conclusions). Continued TS updates (based on TR conclusions). | TDOCs for: Continued TS updates (based on TR conclusions). Finalize the normative work.
 | LS exchange with RAN if needed | LS exchange with SA3 if needed | LS exchange with other WG if needed |  | Note 1: 24Q4 may continue with some key issues in the TR Note 2: 24Q4 starts WI for key issues concluded by 24Q3 |  |  | 
NOTE 1: Assuming 2 TU allocated for each meeting.
NOTE 2: Some key issues in SI needs further discussion in 24Q4, e.g. align with RAN progress.

## Slide 6: TU Spreadsheet for RAN1
Annex 1 : RAN Rel-19 Ambient IoT timeline (RP-232745)
Ambient IoT | ~3.5 TUs (TUs budgeted for the entire release, target 12-month for SI completion, check in Dec’24 for conversion to WI or if necessary, continuation of SI)