## Slide 1: Way forward on SNPN Cellular Hotspots (FS_ISN)
Intel, Cisco Systems

## Slide 2: Introduction (1/4)
The study on Interconnect of Standalone Non-Public Networks (FS_ISN) was approved in SA#99 (SP-230236)
The original completion date for FS_ISN was SA#102 (i.e., this meeting)
  Unfortunately, the study is not yet complete
  Exception sheet, agreed by SA1, has been submitted for the FS_ISN study (SP-231400) requesting additional two quarters to finish the study

## Slide 3: Introduction (2/4)
The FS_ISN study includes two different types of use cases
  UC1 for scalable single-hop SNPN interconnect with dynamic connections (now referred to as “SNPN Cellular Hotspots”)
  UC3, UC4 and UC5 for dynamically reconfigurable multi-hop SNPN interconnect
  NOTE 1: In this analysis UC2 is subsumed under UC3/UC4/UC5
  NOTE 2: For details refer to the backup slides

## Slide 4: Introduction (3/4)
The UC1 (SNPN Cellular Hotspots) requirements are not related to the UC3/UC4/UC5 requirements
  Large number of SNPNs vs 5-6 ships (SNPNs)
  SNPN participants generally unknown to each other in advance vs SNPN participants well known and locked down well in advance (in addition to being few in number)
  Single-hop vs multi-hop SNPN interconnect
  Static SNPN interconnect vs dynamically reconfigurable SNPN interconnect topology
  NOTE: In this analysis UC2 is subsumed under UC3/UC4/UC5

## Slide 5: Introduction (4/x)
In SA#104 (Nov 2023) the potential requirements corresponding to UC1(SNPN Cellular Hotspots) have been consolidated and agreed by SA1 (S1-233480)
The companies driving the work on SNPN Cellular Hotspots also brought a set of documents for approval in SA#104 as follows:
  Conclusion in TR 22.848 related to SNPN Cellular Hotspots (S1-233476)
  A mini-WID related to SNPN Cellular Hotspots (S1-233477)
  A TS 22.261 CR (S1-233478) related to SNPN Cellular Hotspots
Unfortunately, the proposal for interim conclusions related to UC1 (S1-233476) were not agreed on the grounds that SA1 working practices do not allow partial conclusions
  As a consequence, the related mini-WID and CR were not handled

## Slide 6: Request for SA#102 (1/2)
Given that…
  The UC1 (SNPN Cellular Hotspots) requirements are not related to the UC3/UC4/UC5 requirements
  The technical discussion in SA1#104 indicated that the study on SNPN Cellular Hotspots (UC1) is ripe for conclusion, but the conclusion proper (S1-233476) was blocked on procedural grounds related to SA1 WG working practices, and
  The companies driving the work on SNPN Cellular Hotspots would like to complete the normative work as part of Rel-19
The companies driving the work on SNPN Cellular Hotspots are seeking approval from SA#102 on the following companion documents submitted for this meeting
  A mini-WID related to SNPN Cellular Hotspots (SP-231656)
  A TS 22.261 CR (SP-231657) related to SNPN Cellular Hotspots

## Slide 7: Request for SA#102 (2/2)
If the request on the previous slide cannot be fully addressed by SA#102, the requesting companies are seeking guidance from SA#102 on how to proceed in order to complete the normative work on SNPN Cellular Hotspots stage-1 requirements as part of Rel-19
We hope the entire study can be completed by March 2024; however, if this is not possible, there should be no objection to concluding only the mature parts of SA1 SID and moving forward with WID/CRs for Rel-19 on the concluded items in SA2 and/or SA3 SID

## Slide 8: BACKUP SLIDES (from S1-233063)

## Slide 9: UC1: Scalable SNPN Interconnect with dynamic connections
Salient features:
Static SNPNs and single-hop connectivity (between SNPN and SNPN Credential Provider)
Focus on scalability
  large number of SNPN Credential Providers with which the SNPN might not have preconfigured information detailing the IP addresses used by these SNPN Credential Providers to interconnect with the SNPN
  large number of SNPNs with which the SNPN Credential Provider might not have preconfigured information detailing the IP addresses used by these SNPNs to interconnect with the SNPN Credential Provider
Focus on security
  How the SNPN determines how to connect to a SNPN Credential Provider capable of verifying the identity presented by a user attempting to connect to that SNPN
  How the SNPN can securely interconnect with a SNPN Credential Provider in deployments where the required security information is not preconfigured
  How the SNPN Credential Provider can securely notify events (e.g., a user’s subscription ending) to the SNPN
UC1: Scalable SNPN interconnect with dynamic connections

## Slide 10: UC2: Interconnect between SNPNs
Focus on interconnect topologies without other considerations
  Point-to-point connectivity supported today
  Hub & Spoke connectivity implies two-hop connectivity and can be considered addressed under the UC3/UC4/UC5 scenarios (see next slides)
  Gateway connectivity seems to be entirely within the transport network and is outside of 3GPP scope
NOTE: The considerations above are based on the descriptive UC2 text. The UC2 potential requirements (see backup slides) are high-level and do not refer to a specific interconnect topology.
Gateway connectivity
Point-to-point connectivity
Hub & Spoke connectivity

## Slide 11: UC3: Interconnection of standalone naval non-public networks
User A on-board ship A and attached to the on-board SNPN A establishes a PDU session to access service B.
In the process of establishing the PDU session, the 5G system identifies that communication with service B shall be routed from SNPN A to SNPN B through SNPN D to fulfil the quality of service required by service B. The 5G system configures all resources on this path according to service B quality of service requirements.
Later on, ships have moved relatively from each other’s, based on metrics collected on the wireless interconnection links, the 5G system now identifies that the communication with service B shall be routed through SNPN C. The call is handed over to the new path without the user A even noticing it.
Later on, unfortunately, SNPN C is no more available (or goes out of reach) and is replaced by a helicopter embedding an ad hoc SNPN. As part of a discovery process, the new SNPN in the helicopter identifies and authenticates itself to those SNPNs in range. The new route now comprising the SNPN on board the helicopter is evaluated against quality of service requirements and eventually selected by the 5G system for user A PDU session.
Meanwhile, while the helicopter is being launched, the 5G system realizes that the communication path using SNPN C is no more available and, as a result, User A communication to service B is reconfigured to the initial communication path through SNPN D. The communication is experiencing quality issues until the communication path is switched over to the one involving the SNPN on board the helicopter.
The communication with service B is terminated by user A and all resources used for the communication between SNPN A and SNPN B are released.
UC3: Interconnection of standalone naval non-public networks

## Slide 12: Use case #4: Mobility in a group of interconnected standalone naval non-public networks
User A on-board ship A and attached to the on-board SNPN A establishes a PDU session to access service B.
User A takes a speed boat, equipped with necessary communication equipment to deploy locally SNPN around the speed boat and to enable connectivity with any vessels in the fleet through wireless links. Once it is deployed, the on-board SNPN selects the SNPNs in range, identifies and authenticates itself to those SNPNs. The SNPN on board the speed boat is then added in the group of interconnected SNPNs through wireless links.
As the speed boat moves away from ship A, radio measurements made by user A terminal trigger the 5G system to handover the ongoing communication from SNPN A to the SNPN on-board the speed boat.
At this point, user A terminal, although under radio coverage of the SNPN in the speed boat, keeps consuming service B through a communication path made of speed boat SNPN + SNPN A + SNPN D + SNPN B.
Somewhere along the path from ship A to ship B, as radio conditions on the 5G link to ship A worsen and as the speedboat approaches ship D, the SNPN on-board the speed boat selects SNPN D as a new anchoring point to the group of interconnected standalone non-public networks. Based on the new resulting topology, the 5G system then seamlessly reconfigures the communication path from user A’s UE to service B so that it can still continue to fulfil QoS required by service B. The communication path is now made of speed boat SNPN + SNPN D + SNPN B.
Later on, as the speedboat approaches ship B, the on-board SNPN directly connects to SNPN B in the same anchoring point selection and communication path switching process as previously described to reduce communication latency.
From the point in time user A gets on board the speedboat and gets to ship B, his communication with service B is maintained. There is no noticeable alteration of the communication along the path from ship A to ship B.
When user A arrives at his destination on ship B, his communication is seamlessly handed over from the SNPN on-board the speedboat to one of the cells on SNPN B. Once connected to SNPN B, he can still access to service B and other local services according to authorizations he’s entrusted with.
UC4: Mobility in a group of interconnected standalone naval non-public networks

## Slide 13: Use case #5: QoS differentiation and resource prioritization in a group of interconnected standalone naval non-public networks
User A requests a real time video streaming involving a MCX server located onboard ship A to users B and D respectively located on ship B and D.
If the requested quality of service can be reached, users A, B, D on-board ships A, B, D, and attached to the on-board SNPNs A, B, D, can establish a PDU session to access the video streaming service provided by the MCX server on ship A.
While establishing the user B’s PDU session, the 5G system identifies that communication shall be routed from SNPN A to SNPN B through SNPN C to fulfil the quality of service required by the MCX service A. The 5G system configures all resources on this path according to MCX service A’s quality of service requirements.
While establishing the user D’s PDU session, the 5G system identifies that communication can be directly routed from SNPN A to SNPN D. The 5G system configures all resources on this path according to MCX service A’s quality of service requirements.
At this point in time, users A, B, D consume the real time video service hosted by the MCX server A and the 5G system constantly monitors the achieved end to end quality of service with regards to the application known requirements.
The delivered end to end quality of service changes (due to e.g. path loss increase on the interconnection links), thus triggering a notification from the 5G system to the MCX application which decides to lower the video resolution to match the end to end connection capacity and maintain an acceptable experience for the users.
Meanwhile, lower priority communications are setup inside the fleet and start to heavily load all the interconnection links.
The 5G system ensure that the critical video streaming communication between users A, B, D has higher priority related to the other ongoing data exchanges which results in user A, B, D continuing experiencing a good quality MCX service A.
UC5: QoS differentiation and resource prioritization in a group of interconnected standalone naval non-public networks

## Slide 14: Use cases #3, #4 and #5: Salient features
Limited number of interconnected SNPNs
  5 or 6 ships (according to TR 22.848 clause 5.3.1)
Wireless SNPN interconnect
Self-organized SNPN interconnect topology
Dynamically reconfigurable SNPN interconnect topology
  Due to SNPN mobility
  Due to changes in the quality of interconnection links
Multi-hop SNPN interconnect
Dynamic route selection in the SNPN interconnect based on the QoS requirement of the service

## Slide 15: Summary
The UC1 requirements stand in stark contrast compared to the UC3/UC4/UC5 requirements
  Large number of SNPNs vs 5-6 ships (SNPNs)
  SNPN participants generally unknown to each other in advance vs SNPN participants well known and locked down well in advance (in addition to being few in number)
  Single-hop vs multi-hop SNPN interconnect
  Static SNPN interconnect vs dynamically reconfigurable SNPN interconnect topology
  NOTE: In this analysis UC2 is subsumed under UC3/UC4/UC5
Based on the observations above it is proposed to:
  Proceed with two distinct 6.X clauses in TR 22.848 for consolidation of requirements (S1-233060)
  Agree the mini-WID (S1-233061) and related TS 22.261 CR (S1-233062) related to UC1