## Slide 1: Way forwards for Release 19 AI/ML work in SA2
Lenovo

## Slide 2: Status of SID on Core Network Enhanced Support for Artificial Intelligence (AI)/Machine Learning (ML)
Study was endorsed at SA2 #158 (S2-2310034). Study is composed of three work tasks
  WT1: AI/ML cross-domain (Core-RAN) coordination aspects
  WT2: Enable 5G system to assist collaborative AI/ML operation involving 5GC/NWDAF or AF for “Vertical Federated Learning (VFL)”.
  WT3: Support NWDAF-assisted policy control and address network abnormal behaviour (signalling storm)
Further iterations of the SID (i.e. TUs estimation) were discussed at SA #101 and SA2 meetings #159 #160 but were postponed
WT1 is controversial given related AI/ML work in RAN groups while WT2 and WT3 are stable

## Slide 3: Status of AI/ML related work in RAN – general aspects
A general AI/ML framework
  Include model training, model management, data collection, model inference and model storage
Network-UE collaboration levels
  Level x: No collaboration
  Level y: Signaling-based collaboration without model transfer
  Level z: Signaling-based collaboration with model transfer
Life-cycle management (LCM) principles
  Functionality-based and Model-ID-based LCM
    Different manageable granularity for UE-side or UE-part of two-sided models, based on identified configurations.
  Relevant operations and functions
    Performance monitoring, activation/deactivation, selection, switching, updating and fallback.
Data collection
Inference
Management
Training data
Output for Monitoring
Selection/(de)activation
/switching/fallback
Model Training
Performance feedback/
Retraining Request
Trained/updated model
Monitoring Data
Inference data
Model Storage
Model transfer/delivery request
Model transfer/delivery

## Slide 4: Status of AI/ML related work in RAN – RAN1 use cases
CSI feedback enhancement
  CSI compression using two-sided AI model
  CSI prediction using UE-sided model
Beam management (BM)
  BM-Case1: Spatial-domain DL Tx beam or beam pair prediction using NW and/or UE-side AI model
  BM-Case2: Temporal DL Tx beam or beam pair prediction using NW and/or UE-side AI model
Positioning accuracy enhancement
  Direct AI/ML positioning
  AI/ML assisted positioning
Conclusions from RAN WG1:
  Recommendation for normative work for:
    BM-Case1
    BM-Case2
    Direct AI/ML positioning
    AI/ML assisted positioning
  No consensus for normative work recommendation:
    CSI compression
    One-sided CSI prediction use-case

## Slide 5: Status of AI/ML related work in RAN – Data Collection aspects
Network-side data collection mechanisms
  gNB-centric data collection  Data used for model training at gNB
  OAM-centric data collection (using MDT)  gNB is a consumer of data from OAM for model training at gNB
  LMF-centric data collection  Data used for training AI/ML models used at LMF
UE-side data collection mechanisms
  UE collects and directly transfers training data to the Over-The-Top (OTT) server
  UE collects training data and transfers it to Core Network. Core Network transfers the training data to the OTT server.
  UE collects training data and transfers it to OAM. OAM transfers the needed data to the OTT server.
  RAN2 did not study or analyse these proposals and did not agree to requirements or recommendations.
  Observation 1: WT1.1 focuses on UE-side data collection and WT1.5 on LMF-centric data collection
  Observation 2: SA2 can study further UE-side data collection, given that RAN will not further work on this topic
  Observation 3: LMF-centric data collection options can be further studied at SA2
  Observation 4: No common data collection framework has been defined in RAN. SA2 can further study if a common data collection framework can be defined

## Slide 6: Status of AI/ML related work in RAN – Model transfer/delivery to UE
Solution 1a | gNB can transfer/deliver AI/ML model(s) to UE via RRC signalling.
Solution 2a | Core Network (except LMF) can transfer/deliver AI/ML model(s) to UE via NAS signalling.
Solution 3a | LMF can transfer/deliver AI/ML model(s) to UE via LPP signalling.
Solution 1b | gNB can transfer/deliver AI/ML model(s) to UE via UP data.
Solution 2b | Core Network (except LMF) can transfer/deliver AI/ML model(s) to UE via User Plane (UP) data.
Solution 3b | LMF can transfer/deliver AI/ML model(s) to UE via UP data.
Solution 4a | OTT server can transfer/deliver AI/ML model(s) to UE (e.g., transparent to 3GPP).
Solution 4b | OAM can transfer/deliver AI/ML model(s) to UE.
  Observation 5: WT1.2 studies model/transfer delivery options. Model/Transfer delivery options (for UE-side models) involving the CN can be further studied and evaluated by SA2
  Observation 6: WT1.3 studies model identification. Use case for UE-side model identification at CN for delivering models to UE can be further studied and evaluated by SA2
Model transfer/delivery options in TR 38883

## Slide 7: Way forwards proposal for WT1
SA2 to work on Work Task 1 (and sub work-tasks) but only as a study (i.e. no normative work in Release 19). Focus on the following use cases
  UE data collection procedure for UE-side related AI/ML model use cases describing the framework to support data collection from the UE with UE-side model training carried out at 3rd party (e.g. AF/OTT).
  Model/Transfer Delivery to the UE from core network/AF/OTT server (includes model identification between UE and AF/OTT server).
  AI/ML positioning enhancements (data collection/model training) with main assumption model training is carried out and used at LMF.
Any SA2 conclusions to WT1 in Release 19 should be taken into account by RAN during Release 19+ normative work
SA2 to continue normative work for WT1 in Release 20 taking into account any Release 19 conclusions
*WT1 additional TUs allocated for the study phase
*WT2 and WT3 TUs unchanged for both study and normative phase