## Slide 1: Rel-18 Ranging Controversial issue and way forward.
Sony, Philips International B.V.

## Slide 2: Introduction
The feature “Service exposure to SL Positioning Client UE via Control plane” (i.e., expose Ranging/SL Positioning information to a different UE not participating in the Ranging/SL positioning) is missing important information on the UE Privacy checking.
Different views in SA2 and SA3 are creating a deadlock situation.
This relates to document S2-2400120 (CR0466R1 to TS 23.273)

## Slide 3: Introduction (ctd.)
S2-2400120 proposes to extend legacy LCS privacy profiles with list of Client UEs that are trusted.
  Information stored in UDM, similar to list of trusted LCS Clients or AFs.
  Such list is very useful e.g. for deployment in factories in which a pre-configured list of “trusted” UEs may exists.
  Without such Client UE list, UEs would need to be requested every time to confirm (leading to lots of overhead and user unfriendly experience) or prevent exposure completely. For more technical information see back-up slides.
  This CR is based on LS S2-2400027 from SA3 to SA2. (i.e. refers to SA3 specification stating that: “the GMLC shall perform the privacy check for the Target/Reference UEs…”)
S2-2400120 was agreed during SA2#160AHe in January 2024.

## Slide 4: Introduction (ctd.)
Issue is that in August 2023 an LS was sent from SA2 to SA3 in which SA2 expects SA3 to develop a ranging/sidelink positioning privacy profile. This profile could potentially replace the legacy LCS privacy profile in case of ranging/sidelink positioning.
During SA3#115 in February 2024, proposal S3‑240751 for ranging/sidelink positioning privacy profile was discussed. However, this privacy profile was not aligned with S2-2400120, because some companies in SA3 expressed concerns with the architectural decision of having list of Client UEs stored in UDM.
The SA3 ranging/privacy profile was not accepted in SA3. At the same time in SA2#161 some companies objected to S2-2400120 being sent to plenary, leading to the current deadlock situation.

## Slide 5: Way Forward proposal
Endorse S2-2400120 (company contribution CR in SP-240332), based on the grounds that SA2 accepted the proposal in January and SA3 did not align with SA2’s decision by stating architectural concerns, not security related concerns.
SA#103 to send LS to SA2 and SA3 to ask either SA2 or SA3 (not both) to address further clarifications that have been requested (thus far):
  Exposure to Client UEs only applies to ranging/sidelink positioning procedures
  Word “location” in the LCS privacy profile also applies to ranging/sidelink positioning results (not only absolute and relative location)
  Number of client UEs in the client UE list may be restricted by the operator
  or endorse these as well in SA#103.
Consequences if not approved: Feature “Service exposure to SL Positioning Client UE via Control plane” needs to be removed from Rel-18.

## Slide 6: Technical background/analysis
(backup slides)

## Slide 7: Technical background
Legacy Exposure service specified for AF(s) or LCS client(s) uses LCS privacy profile.
Privacy check can be done in three ways
  Allow or disallow exposure to any/all AF or LCS client.
  Allow with notification: Page the UE and check local privacy rule (UE/User interaction).
  Check list of approved AF(s) or LCS client(s) in the UE Privacy Profile.
  This information is stored in the UDM

## Slide 8: Proposal 1 (S2-2400120)
Add a list of approved UEs (Client UE/Requesting UE) in the UE Privacy Profile.
GMLC can perform Privacy check without interaction/notification with UE1 to UEn. (equivalent to Check list of approved AFs in the Privacy Profile)
No need to page these UEs!

## Slide 9: Proposal 2 (S3-240751/S3-240949)
No list of approved UEs (Client UE/Requesting UE) in the Privacy Profile
GMLC must interact/notify UE1 to UEn to check local Privacy rule. (equivalent to Allow with notification)
All these UEs must be paged and exchange NAS level msg.

## Slide 10: Issue related to UE Privacy check
Exposure service for a SL Positioning Client UE (Requesting UE)
Privacy check could be done in three ways (same as for AF/LCS Client)
  Check Privacy Indicator: Allow (or disallow) exposure to any UE (Client UE)
    Issue: It is not acceptable to allow every UE registered in the network to get access to a UEs ranging/location information (either relative or absolute location).
  Allow with notification: Page the UEs (UE1-UEn) and check local privacy rule (UE/User interaction)
    Issue: On every request the network will need to page and interact with the UE1-UEn which creates significant UE and network inefficiency. This approach will not be practical in e.g. a factory when many UEs are involved.
  Check list of approved Client UE(s) in the Privacy Profile.
    Issue: A new list of approved Client UEs (GPSIs) needs to be added to the UE Privacy Profile. Concern is that the list may become long (1000 GPSIs is less than 10kByte).

## Slide 11: Ranging to follow after Privacy Check
After Privacy Check, the GMLC will trigger LMF to perform Ranging between Target UE and UE1 to UEn
LMF will trigger the AMF/RAN to page the Target UE to deliver the Ranging request.
Target UE will discover UE1 to UEn over Sidelink and perform Ranging
Target UE will report result back to LMF
LMF will send Ranging result to GMLC
GMLC will send result to Client UE (Requesting UE).