## Slide 1: Ranging/SL Positioning service exposure to SL Positioning Client UE through 5GC
Xiaomi
SP-240449

## Slide 2: Background
Procedures for Ranging/SL Positioning service exposure
  Procedures for service exposure to SL Positioning Client UE
    Procedures for Ranging/SL Positioning service exposure through PC5
    Procedure for Ranging/SL Positioning service exposure through 5GC network
      Procedure for Ranging/SL Positioning service exposure through 5GC network via NEF
      Procedure for Ranging/SL Positioning service exposure through 5GC network via control plane
  Procedures for Service Exposure to the AF
Privacy profile solutions are dependent on SA3 decision for all the Ranging/SL Positioning service exposure procedures
  Ranging_SL WID (SP-230106): Privacy protection and other security aspects will be tasked to SA3, and the related impacts to architecture enhancement will be based on SA3 conclusion.
NOTE: Procedures for Ranging/SL Positioning service exposure through PC5 does not use a Privacy Profile in the network. (Agreed in SA3#115)

## Slide 3: Status
SA3 is tasked to develop content of UE Ranging/SL Positioning privacy profile based on LS to SA3 (S2-2309830/S3-234480)
Regarding to UE Ranging/SL Positioning privacy profile, SA2 agrees with SA3 that it is used, among others, to indicate whether the Ranging/SL positioning service exposure to 5GC NF, AFs, and SL Positioning Client is allowed. SA2 believes the content of UE Ranging/SL Positioning privacy profile will be developed by SA3 in TS 33.533, which will be referenced by SA2 in the corresponding Ranging/SL Positioning specifications.
S2-2400120 proposes to extend legacy LCS privacy profiles with list of Client UEs that are trusted.
  agreed on SA2#160AHe, objected on SA2#161 (due to un-alignment with SA2 LS out (S2-2309830/S3-234480)): The originally agreed CR at SA2#160AH-e (S2-2400120) was marked as revised to S2-2402147 and will not be presented by MCC to TSG SA.
On SA2#161/SA3#115, how to handle SL Positioning Client UE privacy check for Ranging/SL Positioning service exposure through 5GC was discussed in both SA2 and SA3, several options were proposed; however, consensus could not be reached in either SA2 or SA3.

## Slide 4: Proposed way fwd
Option 1
Proposal: Remove Procedure for Ranging/SL Positioning service exposure to Client UE through 5GC network to avoid the contentious issue for Client UE privacy checking
SA#103 Tdocs related to Ranging/SL Positioning service exposure to Client UE through 5GC
SP-240405: Discussion on removing Ranging/SL Positioning service exposure to Client UE through 5GC
SP-240406: [DRAFT] LS on removing Ranging/SL Positioning service exposure to Client UE through 5GC
SP-240403: 23.586 CR0129 (Rel-18, 'F'): Remove Ranging/SL Positioning service exposure to Client UE through 5GC
SP-240404: 33.533 CR0067 (Rel-18, 'F'): Remove authorization procedure for Ranging/SL Positioning service exposure through 5GC

## Slide 5: Proposed way fwd
Option 2
Proposal: The legacy LCS privacy profile also applies to ranging/sidelink positioning results.
SA#103 Tdocs related to Ranging/SL Positioning service exposure to Client UE through 5GC
SP-240332: 23.273 CR0466R6 (Rel-18, 'F'): LCS UE Privacy profile updated with a list of allowed UE(s)
SA#103 Tdocs related to UE Ranging/SL Positioning privacy profile
SP-240425 (to be noted): 33.533 CR0055R2 (Rel-18, 'F'): Clarification on the UE Ranging/SL Positioning privacy profile
Option 3
Proposal: Add a new UE Ranging/SL Position Privacy Profile in SA3 specification with Client UE list. (remove the updates in TS 23.273 UE LCS Privacy Profile but approve the provisioning changes of the new indicator and Client UE list)
SA#103 Tdocs related to Ranging/SL Positioning service exposure to Client UE through 5GC
Revision of SP-240332: 23.273 CR0466R6 (Rel-18, 'F'): LCS UE Privacy profile updated with a list of allowed UE(s)
SA#103 Tdocs related to UE Ranging/SL Positioning privacy profile
Revision of SP-240425: 33.533 CR0055R2 (Rel-18, 'F'): Clarification on the UE Ranging/SL Positioning privacy profile