## Slide 1: Need for a consistent e2e AI/ML framework (ref. RP-233796)
Deutsche Telekom, AT&T, BT, China Mobile, KT Corp., MTN Group, Orange, Spark NZ, Telecom Italia, T-Mobile US, Verizon, Vodafone,…
SP-240292

## Slide 2: Observations
What has been done/agreed
  SA WGs 1 - 5, CT WGs 3 – 4, and RAN WGs 1 - 3 have already performed SIs and/or WIs on the AI/ML topic.
  They addressed use cases from their own perspective (e.g. NWDAF usage in the CN, MDAS in OAM, AI/ML for NG-RAN and for air interface in the RAN domain), but a consolidated E2E framework, especially from a LifeCycle Management (LCM) perspective for AI/ML models, is still missing: TS 28.105 (SA5) may act as a basis for further discussions.
  AI/ML models are certainly implementation specific and therefore out of scope of 3GPP, but MNOs see the need to have a common LCM framework at least for those models that have impact on the network and E2E performance.

## Slide 3: Requirements on LCM for AI/ML models in the 5GS from an MNO’s perspective
The LCM should be supported by a full E2E AI/ML architectural framework.
  The framework should in addition also address the data layer(s) where data for online/offline training and inference functions are stored/collected.
The LCM should be consistent across the different NW domains (RAN, CN, OAM) and should cover also the UE part if AI/ML models to be applied have direct interrelation with the NW side (e.g., two-sided models or training of UE-sided models in a NW-sided domain).
  Consistency of terminology (e.g., definitions), processes, responsibilities, …
  Consistency how models are trained, validated, and tested; how deployment of models to inference machines (as part of logical NW nodes or functions) is handled; how models are updated, replaced and/or finally released; how model inference output is ensured not to negatively impact the NW and E2E performance, … (note: use case specific adaptations could be considered)
Usage of AI/ML models within the 5GS and data generated (to be used for training and inference purposes) should be under control of the NW, i.e., MNO; at least the NW should have the knowledge about which models are applied (e.g., via model ID) and should be in a position to manage them in case of negative impact on performance.

## Slide 4: Urgent proposal for way forward
As TSG SA is responsible for the E2E architecture, the common E2E LCM framework should be defined or described by related SA WGs (e.g., SA2 in collaboration with SA5) taking into account the status of existing and ongoing work in other SA, CT, and RAN WGs (continuous LS exchange would be appreciated).