## Slide 1: Discussion on MINT_Ph2_EPS
China Telecom
SP-240577

## Slide 2: SA1 MINT_Ph2
The following requirement was introduced to TS 22.261 by R19 MINT_Ph2, approved in SA#97E:
  Subject to regulatory requirements, operator's policy or UE capabilities, the 3GPP system shall be able to support a UE, with 5G-only national roaming access to a VPLMN, to obtain 4G connectivity service (e.g. voice call, mobile data service) from that VPLMN in the area where a Disaster Condition applies.
HPLMN has no 4/5G coverage in the impacted area.
Before Disaster Condition applies, the UE obtains 5G service from a 5G VPLMN, while the UE cannot access 4G from that VPLMN.
When Disaster Condition applies to 5G VPLMN due to RAN failure, the UE shall be able to perform Disaster Roaming in the 4G of that VPLMN, to obtain 4G service.

## Slide 3: CT1 MINT_Ph2_EPS Proposal
In CT1#148, a WID for MINT support in EPS (MINT_Ph2_EPS) was proposed to support the requirement (C1-242486).
The objectives of MINT_Ph2_EPS are:
define 4G PLMN selection for Disaster Roaming,
reuse UE configuration and provisioning for Disaster Roaming by 5G to activate Disaster Roaming and prevent signaling overload, including 5G provision of "disaster roaming is enabled in the UE" and registration wait range,
enhance NAS protocol regarding attach procedure after selection of a Disaster Roaming 4G PLMN, including updates for unified access control, notification of information related to Disaster Roaming.
NOTE:
The scope of Disaster Condition is limited to RAN failure, same as R17 MINT.
The MINT_Ph2_EPS solutions should be similar to Disaster Roaming mechanisms defined for 5G in R17 MINT.

## Slide 4: Incoming LS (1/2)
Incoming LS from CT1 for action (SP-240538 / C1-242675)
With limited system level impacts, R17 MINT started with a study item in CT1, a work item in CT1, and then a work item for alignment in SA2. SA2 reviews were provided before CT1 normative work.
MINT_Ph2_EPS is the 4G version of R17 MINT. Similar to R17 MINT, MINT_Ph2_EPS includes both stage-2 and stage-3 aspects, and the stage 2 aspects regarding 4G network selection and access control are under CT1 responsibility.
CT1 would like to ask TSG SA if CT1 could conduct normative work for MINT_Ph2_EPS.

## Slide 5: Incoming LS (2/2)
Incoming LS from SA2 for information (SP-240558/ S2-2407313)
To provide SA2 reviews before CT1 normative work, SA2 recommends to follow R17 MINT working procedure: a study should be performed for MINT_Ph2_EPS. When the study is completed, then CT1 should consult with SA and SA2 on how to proceed with the normative work for MINT_Ph2_EPS.
SA2 kindly asks TSG SA to take above information into consideration.

## Slide 6: Conclusions and Way forward
Conclusions
MINT_Ph2_EPS is the 4G version of R17 MINT. It intends to support the requirement in TS 22.261, by allowing the UE to perform Disaster Roaming in 4G VPLMN under 5G RAN failure.
The scope of MINT_Ph2_EPS work is under CT1 responsibility, similar to R17 MINT.
To receive SA2 reviews before CT1 normative work, it is reasonable to follow R17 MINT working procedure.
Proposed Way forward
In the reply LS to CT1, TSG SA kindly asks CT1 to have a study item for MINT_Ph2_EPS, and consult with SA and SA2 on how to proceed with the normative work when the study is completed.