## Slide 1
Samsung, Lenovo, CATT, China Mobile, ETRI, Hisillicon, Huawei, Intel, InterDigital, KPN, KT Corp., LG Uplus, MediaTek, NEC, NTT DOCOMO, OPPO, ORANGE, Rakuten Mobile, SK Telecom, Toyota, Vivo, ZTE
Way forward
for SA2 EnergySys

## Slide 2: Summary of Issue
SA2 discussion on new functionality for EnergySys
  FS_EnergySys in SA2 discussed functionality to support the feature for energy saving and energy efficiency in 5GC
  Specifying a new functionality in 5GC was supported by majority of companies
    There was a clear need to collect and calculate energy related information in 5GC to support the SA1 defined requirements for energy saving as service criteria, for which the existing functionalities do not support
  Few companies presented different preference to enhance the CHF defined by SA5 for the purpose
  SA2 could not confirm the majority’s view due to the sustained objections from companies

## Slide 3: SA2 Majority View
Rel-19 SA2 FS_EnergySys identified enhancements which needs a new functionality in 5GC to support energy efficiency and saving, e.g.:
  Energy Information exposure to the 3rd party consumer regarding energy consumption per UE, and per UE per AF
    Different from what are being studied for OAM based on NF and slice granularity in SA5
  In addition, following procedures can consider energy related information:
    PCF making policy decision for a UE/PDU Session/Network Slice
    NF discovery and (re-)selection
    UP path adjustment for a PDU session(s)
  And more…

## Slide 4: Proposed Way-Forward
The decision for architectural enhancements and a new functionality for supporting energy related information to be used during UE related control procedures should be defined in SA2.
  SA2 EnergySys is focused on UE related control procedures, such as the UE subscription, policy control and NF discovery & selection and UP path selection.
  Proponents for CHF claims that CHF can support the required use cases. However, it is unclear how the existing mechanism defined for CHF can be enhanced to support such use cases for energy saving and energy efficiency. Note that there is no related work in SA5 charging to make such enhancement.

## Slide 5: Proposed Way-Forward
Possible work distribution regarding energy related information handling:
SA2
SA5 (OAM)
SA5 (charging)
Monitor the data volume of overall UPF traffic and UE’s QoS Flow traffic
Calculate energy related information
per-UE-per-QoS-Flow
Aggregate for various granularities (e.g. per UE, per application, …)
Policy decision, analytics and prediction, NW optimization (e.g. NF discovery/selection and UP path selection), Exposure to AF
Spending Limit control enforcement
UE charging and credit (spending) control
- Receive energy related record, e.g., per-UE-QoS-Flow, and aggregate per UE for charging
- Trigger spending
Collect energy related information per NF, per Network Slice
(EC & EE in R18, Carbon Emission and Renewable Energy in R19)

## Slide 6: Annex

## Slide 7: Consideration
OAM is handling different granularities for calculating energy related information (network element, network domain, cross-domain, communication service)
  These are irrelevant to support SA2 defined scenarios
CHF does not support information exposure
  Functionality of CHF is not defined for exposure to 3rd party
SA2 is responsible for UE granularity, policy and path adjustments
  These are not related to CHF or SA5

## Slide 8: Consideration
SA2 proposal (New functionality)
  Achieves scalability to support finer granularities required in SA2, i.e. per QoS Flow / per application flow
  Ensures future-proof extensibility: addition of control plane contribution on energy consumption, network sharing, roaming, ATSSS, etc.)
  Can reuse the existing control procedures: exposure via NEF, AF influence, BDT, PDTQ, …
  Cons: increased complexity of implementation in case of defining the new functionality on the existing NF
CHF proposal (alternative)
  May need small enhancements for SMF only to support energy-related Charging information
  Cons: Complexity in evaluation of energy related information for UE granularity from charging information
  Needs a new exposure framework for CHF
  Allows limited extensibility: any new info needs to go into the Charging information
  Charging System belongs to different business unit of operator, may come from specialized vendor and has different life cycle