## Slide 1: Summary on E2E AIML Framework in SA2
vivo

## Slide 2
Summary of AI/ML Activity in 3GPP SA2
(AI for Network)
1) Introduce the concept of NWDAF(Network Data Analytics Function) to produce data analytics for network automation.
2) Only one network data analytics is supported i.e. slice specific network data analytics
1)Define general framework for data collection and data analytics exposure. NWDAF consist of data collection/model training and model inference
2) 9 more network data analytics supported e.g.
Observed Service Experience
R15: Analytics Concept
R16: monolithic Arch
1) Decompose monolithic NWDAF into Model Training logical function/Analytics logical function and Analytics Data Repository Function
2) Data collection framework enhancement via DCCF (Data collection coordination Function)
3) 5 More network data analytics supported
R17: distributed Arch
1) Architecture enhancement e.g. model performance monitoring/multi-Vendor ML Model sharing/Horizontal FL/ /data analytics in roaming 2) Data collection framework enhancement via UPF data exposure/DCCF relocation
3) 6 More network data analytics supported
R18: Arch enhancement
R15~R18 eNA(enablers for Network Automation) are to study the architecture level enhancements to support AI/ML in Core network including AIML architecture and corresponding use cases
  Focus on data collection and data analytics to the network and AI/ML algorithm is not in the scope
  Good coordination with SA5/SA3 however no coordination with RAN due to no RAN dependency
R19 SA2 FS_AIML_CN is to further identify potential architecture enhancements to support AI/ML
  Part1: AI/ML cross-domain coordination aspects (RAN related, high dependency with R19 AIML over air interface)
  Part2: Core network topics Vertical Federated Learning, NWDAF-assisted policy control, signaling storm mitigation
NWDAF
1 UC
NWDAF
10 UCs
AnLF
MTLF
DCCF
15 UCs
ADRF
model
AnLF
MTLF
DCCF
21 UCs
ADRF
model
Perfo. Monitor
Model sharing
Horizontal FL
Roaming Enh.
UPF
Data

## Slide 3
General AI/ML Framework in Core Network
The NWDAF(Network Data Analytics Function) provides analytics to 5GC NFs and OAM.
An NWDAF may contain the following logical functions:
  Analytics logical function (AnLF): A logical function in NWDAF, which performs inference, derives analytics information and exposes analytics service
  Model Training logical function (MTLF): A logical function in NWDAF, which trains Machine Learning (ML) models and exposes new training services (e.g. providing trained ML model)
NEF
NWDAF
AF
PCF
AMF
SMF
UPF
Nnef
Nnwdaf
Naf
Npcf
Namf
Nsmf
N4
UDR
Nudr
CHF
Nchf
OAM
RAN
UE

## Slide 4
Data Collection Architecture in
Core Network
Fig2: Network Data Analytics Exposure architecture
Fig1: Data storage architecture for Analytics and Collected Data
DCCF: Data Collection Coordination Function
ADRF: Analytics Data Repository Function

## Slide 5
AI/ML Model Sharing within Core Network
In R18, introduce ML model Interoperability information to support Model delivery within 5GC NWDAFs among multi-vendors;
ML Model Interoperability Information, this is vendor-specific information that conveys, e.g., requested model file format, model execution environment, etc.

## Slide 6
FL(Federated Learning) in Core network
  Enhance 5GC to support horizontal/vertical federated learning (VFL), i.e. a federated learning technique without exchanging/sharing local data set or ML Models
5GC Support for Horizontal FL in R18
5GC Support for Vertical FL in R18

## Slide 7
AI/ML Model Performance Monitoring
In R18, define Model/Analytics Accuracy for classification in TS23.288, which is the number of correct predictions out of all predictions.

## Slide 8
Observations
Identify AI/ML related activities of all working groups of Pre18/ Rel-18 features and Rel-19 studies.
  First identify AI/ML related Activities of Pre-R18 and Rel-18 features as they are already frozen and stable
  Secondly identify AI/ML related Activities of R19 studies once it is stable e.g. by end of 2024 when R19 is expected to finished
In addition to AI/ML LCM, AI/ML E2E framework should also include other parts e.g. models and data collection/storage, performance evaluation and accuracy monitoring