## Slide 1: Interworking Support within NextGen Study Timeline
Samsung, Intel
TSG SA Meeting #SP-73
New Orleans USA, Sep 21-23 2016
SP-160683

## Slide 2: Motivation (1/2)
  Regardless of migration options listed from TSG#72 [’16.06 SA/RAN Plenary], partial 5G system deployment requires interworking solution between the legacy LTE/EPC and the NG-RAN/NG Core
    UE may frequently move across the 4G/5G boundaries
LTE
NR
EPC
Nextgen Core
Attach to LTE
Attach to 5G
5G Partial
Deployment
Service Disruption
IWK solution should be investigated for reducing service interruption in 5G Partial Deployment Case

## Slide 3: Motivation (2/2)
A solution that can minimize the service disruption in NextGen / EPS interworking scenarios is needed
A solution with minimum impacts on both NG Core and EPC is needed
Work prioritization to support early deployment of NextGen system should be considered

## Slide 4: Observations
5G migration scenarios have been discussed at SA2#116bis meeting
  Only migration scenarios were discussed
  No interworking solutions were reviewed
Based on the SA2 discussion, the following points are observed
  Partial deployment of NextGen system requires NextGen / EPS interworking
  It is desirable to reduce service interruption during UE mobility between NextGen system and EPS
SA2 should prioritise loose interworking solutions that provide:
  Seamless NextGen / EPS HO by simply preserving the IP address of UE, while avoiding unnecessary complexity (e.g. handover preparation, in-flight data forwarding, etc.)
  Less impact on the legacy EPS and the NextGen system, which makes interworking standardization process move forward fast
  Further reduced HO interruption by using Dual Radio/Dual Attach

## Slide 5: Proposal
SA Plenary to task SA WG2 to
  Accelerate the development of NextGen / EPS interworking solutions within NextGen SI while keeping the timeline for the standalone specification.
  Prioritize discussion on loose interworking solutions (e.g. Common IP anchor, Dual Radio/Dual Attach, etc.) to facilitate early deployment of NextGen systems, while continuing studying on more sophisticated, tight interworking solutions