## Slide 1
Frank Mademann, SA2 Chairman (Huawei)
Maurice Pope, SA2 Support (MCC)
TSG SA WG2 Report and Questions for Advice at TSG SA#81 (agenda item 7.2)

## Slide 2: Contents
1) General aspects (events since SA#80, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work and Work
  2.3) Rel-16 and later Work
  2.4) New and Updated WIDs/SIDs and Exceptions
  2.5) IETF Dependency Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
Explicit requests for TSG SA are highlighted in RED

## Slide 3: Contents
1) General aspects (events since SA#80, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs/SIDs and Exceptions
  2.5) IETF Dependency Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 4: 1) General Aspects (1/8)
SA2 meetings held since SA#80
  SA2#128: Jul 2018, Vilnius, LT
  SA2#128bis: Aug 2018, Sophia Antipolis, FR
Future SA2 meetings
  SA2#129: Oct 2018, Dongguan, CN
  SA2#129bis: Nov 2018, West Palm Beach, US

## Slide 5: 1) General Aspects (2/8)
SA2 WG Officials
  Chairman: Frank Mademann (Huawei)
  Vice Chairmen: Puneet Jain (Intel), Krisztian Kiss (Apple)
  Secretary: Maurice Pope (MCC)
Parallel sessions held in the last plenary cycle
  Many thanks to Maurice Pope and the parallel session chairs Puneet Jain, Krisztian Kiss, LaeYoung Kim and Irfan Ali for their outstanding support!

## Slide 6: 1) General Aspects (3/8)
No changes in SA2 leadership, elected during SA2#121 before SA#76.

## Slide 7: 1) General Aspects (4/8)
Statistics at SA WG2 #128:
152 delegates ‘attended’ (checked-in) SA WG2 #128
  1269 documents, 1154 handled (including revisions), including
    487 CRs (including revisions)
    42 Incoming LSs, of which 6 were postponed
    30 Outgoing LSs Approved
  145 Tdocs postponed / not handled
Total CRs agreed: 117 (+16 revised at SA WG2#128BIS)
Statistics at SA WG2 #128BIS:
149 delegates ‘attended’ (checked-in) SA WG2 #128BIS
  1364 documents, 1204 Tdocs handled (including revisions), including
    545 CRs (including revisions)
    40 Incoming LSs, of which 9 were postponed
    14 Outgoing LSs Approved
  181 Tdocs postponed / not handled
Total CRs agreed: 169
926 people registered on the SA WG2 e-mail reflector on 28 August 2018

## Slide 8: 1) General Aspects (5/8)
Chart: SA2 meeting attendance
| 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 113AH | 114 | 115 | 116 | 116bis | 117 | 118 | 118bis | 119 | 120 | 121 | 122 | 122bis | 123 | 124 | 125 | 126 | 127 | 127bis | 128 | 128bis
attended | 157 | 139 | 133 | 162 | 135 | 142 | 139 | 173 | 181 | 165 | 158 | 153 | 189 | 146 | 133 | 145 | 142 | 144 | 195 | 159 | 175 | 182 | 113 | 137 | 200 | 137 | 107 | 157 | 168 | 169 | 143 | 157 | 233 | 182 | 175 | 191 | 188 | 156 | 154 | 156 | 222 | 196 | 174 | 149 | 140 | 152 | 149

## Slide 9: 1) General Aspects (6/8) Resource usage
SA2 meetings
Number of Sessions
Chart: 
| #118bis Jan | #119 Feb | #120 Mar | #121 May | #122 Jun | #122bis Aug | #123 Oct | #124 Nov | #125 Jan | #126 Feb | #127 Apr | #127bis May | #128 Jul | #128bis Aug
maintenance | 5 | 6 | 6.7 | 6.5 | 6 | 3.4 | 5 | 3 | 4.5 | 3.8 | 4 | 4 | 1.7 | 1.2
R15 5GS / maintenance | 18 | 23 | 24 | 27 | 31 | 32.5 | 36 | 37 | 24 | 25 | 19 | 19 | 15 | 15
R15 other | 2.5 | 8.5 | 12.3 | 11.5 | 8.3 | 6.3 | 4 | 3
R16 studies | 3.7 | 13.5 | 12 | 19.5 | 20 | 26.4 | 28.6
R15 exceptions | 1 | 1.3 | 1 | 0.2

## Slide 10: 1) General Aspects (7/8) Document Handling / Meeting
Number of Tdocs
Rel-12
Rel-11
Rel-13
Rel-14
Rel-15
Chart: 
| 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 101b | 102 | 103 | 104 | 105 | 106 | 107+E | 108 | 109 | 110 | 110AH | 111 | 112 | 113 | 113AH | 114 | 115 | 116 | 116bis | 117 | 118 | 118bis | 119 | 120 | 121 | 122 | 122bis | 122e | 123 | 124 | 125 | 126 | 127 | 127bis | 128 | 128bis
#approved/endorsed/merged (total) | 210 | 209 | 154 | 207 | 192 | 148 | 166 | 140 | 144 | 108 | 117 | 115 | 134 | 147 | 170 | 168 | 165 | 134 | 123 | 56 | 145 | 150 | 130 | 212 | 198 | 162 | 162 | 168 | 161 | 61 | 151 | 175 | 180 | 87 | 86 | 224 | 278 | 317 | 158 | 210 | 151 | 224 | 269 | 264 | 311 | 368 | 67 | 414 | 467 | 399 | 516 | 483 | 434 | 364 | 423
#not handled, postponed | 199 | 170 | 90 | 98 | 101 | 140 | 97 | 132 | 151 | 77 | 149 | 91 | 138 | 144 | 124 | 101 | 131 | 117 | 23 | 3 | 49 | 63 | 72 | 70 | 66 | 73 | 74 | 65 | 27 | 34 | 145 | 112 | 120 | 35 | 120 | 90 | 53 | 52 | 166 | 108 | 122 | 178 | 254 | 254 | 188 | 200 | 2 | 148 | 85 | 176 | 154 | 186 | 189 | 170 | 185
#noted | 170 | 150 | 135 | 165 | 185 | 179 | 137 | 157 | 137 | 120 | 139 | 155 | 131 | 123 | 121 | 110 | 165 | 172 | 141 | 62 | 95 | 137 | 143 | 143 | 143 | 141 | 120 | 77 | 65 | 38 | 103 | 78 | 124 | 43 | 112 | 137 | 119 | 131 | 70 | 97 | 95 | 101 | 138 | 142 | 119 | 109 | 7 | 163 | 137 | 142 | 137 | 132 | 183 | 113 | 90
Rel-16

## Slide 11: 1) General Aspects (8/8) SA2 Agreed CRs by Release / Meeting
Rel-12
Rel-11
Rel-14
Number of CRs
Rel-13
Note: for 5GS (draft) TSs agreed pCRs and for #125 also agreed/endorsed draft CRs are shown
Rel-15
Rel-16
Chart: 
| 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107+E | 108 | 109 | 110 | 110AH | 111 | 112 | 113 | 113AH | 114 | 115 | 116 | 116bis | 117 | 118 | 118bis | 119 | 120 | 121 | 122 | 122bis | 122e | 123 | 124 | 125 | 126 | 127 | 127bis | 128 | 128bis
r10 CR | 52 | 41 | 54 | 38 | 38 | 21 | 21 | 17 | 3 | 3 | 9 | 1 | 6 | 2 | 3 | 3 | 4 | 0 | 0 | 2 | 3 | 6 | 3 | 1 | 3 | 1 | 0 | 1 | 1 | 1
r11 CR | 2 | 3 | 12 | 16 | 7 | 31 | 26 | 23 | 105 | 71 | 53 | 45 | 18 | 27 | 20 | 20 | 19 | 17 | 10 | 7 | 4 | 5 | 5 | 0 | 6 | 3 | 1 | 1 | 1
r12 CR | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 2 | 2 | 4 | 11 | 8 | 19 | 21 | 35 | 50 | 38 | 64 | 55 | 39 | 35 | 34 | 21 | 11 | 10 | 9 | 1 | 9 | 3 | 3 | 3 | 1
r13 CR | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 10 | 19 | 13 | 14 | 6 | 9 | 56 | 25 | 58 | 73 | 41 | 11 | 35 | 29 | 25 | 25 | 9 | 11 | 2 | 5 | 2 | 4 | 2 | 5 | 3 | 1 | 1 | 1 | 1
r14 CR | 4 | 21 | 69 | 81 | 33 | 56 | 23 | 13 | 17 | 18 | 20 | 10 | 8 | 10 | 8 | 1 | 7 | 2 | 1 | 2
r15 PCR/draftCR | 63 | 126 | 117 | 121 | 171 | 214 | 62 | 287 | 328 | 182
r15 CR | 19 | 19 | 27 | 27 | 12 | 351 | 201 | 213 | 119 | 159
r16 CR | 2

## Slide 12: Contents
1) General aspects (events since SA#80, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs/SIDs and Exceptions
  2.5) IETF Dependency Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 13: 2.1) Rel-14 and before Maintenance (1/1)
Work Progress on Corrections (Category A CRs are not counted)
  R12: none
  R13: none
  R14: 1 CRs on SDCI, 1 CR on SEW2, 1 CR TEI14 / CIoT

## Slide 14: Contents
1) General aspects (events since SA#80, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2 Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs/SIDs and Exceptions
  2.5) IETF Dependency Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 15: 2.2) Rel-15 Maintenance and Work (1/3)
WI | Work Item | WP | CRs approved
VoWLAN | Complementary Features for Voice services over WLAN | 100% | 
ProSe_WLAN_DD_Stage2 | Inclusion of WLAN direct discovery technologies as an alternative for ProSe direct discovery | 100% | 
NAPS | Northbound APIs for SCEF – SCS/AS Interworking | 100% | 1
eVoLP | enhanced VoLTE performance | 100% | 
USOS | Unlicensed spectrum offloading system enhancements | 100% | 
EDCE5 | EPC enhancements to support 5G New Radio via Dual Connectivity | 100% | 1
PS_Data_Off_Phase2 | PS Data Off Feature Phase 2 | 100% | 
EPS_URLLC | EPC support for E-UTRAN Ultra Reliable Low Latency Comm. | 100% | 1
TEI15 | Maintenance for pre-Rel-15 features in Rel-15 |  | 7
TEI15 | Rel-15 Cat B/C alignments with other WGs or specifically required (one of those with objections) |  | 8

## Slide 16: 2.2) Rel-15 Maintenance and Work (2/3)
Progress since SA#80
  CRs agreed for TS 23.501 (42+49 CRs), TS 23.502 (60+81 CRs), TS 23.503 (5+18 CRs)
  5 CRs agreed for TSs 23.167, 23.228
  3 CRs are WG-approved with a single objection each, see CR packages
  Some resolution may be needed in following areas:
    Unresolved Editor’s note in TS 23.501 due to RAN(2) dependency on resolving UE support for RRC_INACTIVE indication
    Potential updates related to RAN2 LSs on handling NSSAI in AS (show of hands in SA2: 14 vs. 11)
    Potential updates related to RAN2 LSs on wait timer in AS (show of hands in SA2: 10 vs. 10)
    Some aspects of handling multiple PDU Sessions towards the same DNN for Interworking.
    potential impact on 5GS due to late RAN R15 drop, none identified yet within SA2
Next steps:
  Essential corrections, resolving remaining issues, further aligning with the work from other WGs
WI | Work Item | WP |  | 
5GS_Ph1 | 5G System – Phase 1 | 100 > 100% |  | 

## Slide 17: 2.2) Rel-15 - local RRM policy specific UE differentiation (3/3)
Progress since SA#80 regarding „ local RRM policy specific UE differentiation“
In SA2 the following LSs from RAN2/3 were discussed:
  S2-184659, LS from RAN WG2: LS on UE differentiation in NB-IoT
  S2-184667, LS from RAN WG2: Reply LS to Reply LS on UE differentiation for Rel-15 NB-IoT
  S2-184703, LS from RAN WG3: LS on UE differentiation in NB-IoT
LS S2-184703 enclosed a CR from RAN3 including 2 main parts (IEs):
  1) Subscription Based UE Differentiation Information IE: New subscription based parameters for UE differentiation in NB-IOT provided from MME to eNB
  2) Local RRM Policy Specific UE Differentiation Information IE: Introduction for “local RRM container” IE provided from eNB to MME and stored in MME while UE is in IDLE mode
The status in SA2 is:
  For 1) SA2 approved four CRs on NB-IoT UE Uu operation optimization.
  For 2) Regarding the Local RRM Policy Specific UE Differentiation Information, no consensus was reached in the SA2#127bis, SA2#128 and SA2#128BIS meetings.
TSG RAN and/or SA are asked to provide guidance or to resolve it

## Slide 18: Contents
1) General aspects (events since SA#80, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs/SIDs and Exceptions
  2.5) IETF Dependency Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 19: 2.3) Rel-16 and later Work and Maint. (1/23)
WI | Work Item | WP |  | 
FS_PARLOS_SA2 | Study on System enhancements for Provision of Access to Restricted Local Operator Services by Unauthenticated UEs | 70 > 100% |  | 
Progress since SA#80
  Study concluded
  A WID is provided for approval
RAN impacts or dependencies
  addition of RLOS broadcast information, addition of RRC establishment cause for RLOS for congestion control and MME selection
Next steps:
  Conducting related normative work

## Slide 20: 2.3) Rel-16 and later Work and Maint. (2/23)
WI | Work Item | WP |  | 
FS_5WWC | Study on the Wireless and Wireline Convergence for the 5G system architecture | 35 > 60% |  | 
Progress since SA#80
  Support of Trusted Non-3GPP access considered reasonably mature.
  interim agreement on solution for Fixed Wireless Access and support of BBF TR-069 management connection on 5G-RG (sent to BBF for feedback)
  Progress with solutions for several Key issues
  BBF informs about progress and provides proposals for consideration and feedback
  TR provided for information
RAN impact/dependency
  None identified
Next steps:
  Analyse BBF proposals and provide feedback
  Work on solutions, evaluations, conclusions

## Slide 21: 2.3) Rel-16 and later Work and Maint. (3/23)
WI | Work Item | WP |  | 
FS_ATSSS | Study on Access Traffic Steering, Switch and Splitting support in the 5G system architecture | 40 > 70% |  | 
Progress since SA#80
  All Key Issues have corresponding solutions documented
  Agreement reached on ATSSS solution framework, which includes the support of MPTCP as an option
  TR provided for information, SID update provided for approval
RAN impacts or dependencies
  None identified
Next steps
  Solution clean-up and possibly merge of solutions
  Evaluation and down-selection for concluding on solution(s) for ATSSS phase-1 multi-access support for 3GPP and Untrusted N3GPP traffic

## Slide 22: 2.3) Rel-16 and later Work and Maint. (4/23)
WI | Work Item | WP |  | 
FS_eV2XARC | Study on architecture enhancements for 3GPP support of advanced V2X services (FS_eV2XARC) | 35 > 58% |  | 
Progress since SA#80
  Three new key issues and seven new solutions agreed for inclusion in TR 23.786
  Solutions for "broadcast/multicast/group delivery over Uu" including solutions for FS_CIoT_5G are captured in Annex B of TR 23.786. Also those from FS_CIoT_5G to ensure consistency.
  Key Issue #7 (Network Slicing for eV2X Services) concluded.
  SID update provided for approval to extend the timeline to Dec 2018
RAN impacts or dependencies
  So far identified: per PC5 RAT operation (NR/LTE), PC5 unicast/multicast, QoS for PC5/Uu
Next steps
  Study continues. Intends to conclude.

## Slide 23: 2.3) Rel-16 and later Work and Maint. (5/23)
WI | Work Item | WP |  | 
FS_eNA | Study of enablers for Network Automation for 5G | 30 > 50% |  | 
Progress since SA#80
  SID is updated to clarify the boundaries towards SA5 and RAN3. Submitted to TSG SA.
  14 key issues and 18 solutions are captured in the TR
RAN impacts or dependences:
  Alignments for obtaining information that RAN OAM already collects
Next steps:
  Work on solutions for existing key issues
  No further use cases and key issues unless there is wider multi-company support

## Slide 24: 2.3) Rel-16 and later Work and Maint. (6/23)
WI | Work Item | WP |  | 
FS_CIoT_5G | Study on Cellular IoT support and evolution for the 5G System | 50 > 70% |  | 
Progress since SA#80
  Good progress for all key issues, TR is provided to TSG SA for information
  Some key issues have already been partially or fully concluded
  Support of broadcast / group communication is in scope of both FS_CIoT_5G and FS_eV2XARC. To ensure consistency it has been agreed to document any broadcast / group communication solutions in the FS_eV2XARC TR
RAN impacts or dependencies
  Potential ng-eNB impacts (depends on solutions chosen during conclusion) for small data transfer; UE power saving enhancements (eDRX, enhanced MICO mode); CIoT feature support-based CN selection; overload control; UE differentiation; group communication
Next steps
  In Q4 focus will be on finalizing solutions and evaluations/conclusions

## Slide 25: 2.3) Rel-16 and later Work and Maint. (7/23)
WI | Work Item | WP |  | 
FS_ETSUN | Study on Enhancing Topology of SMF and UPF in 5G Networks | 40 > 66% |  | 
Progress since SA#80
  8 Key issues and 20 solutions are now documented.
  Solutions have been added and clarified
  TR presented for information. SID update to push study conclusion to December (keeping the same overall SA2 meeting time unit budget)
RAN impacts or dependencies
  None identified
Next steps:
  Evaluate the solutions and conclude.
  No new use cases / key issues / solutions unless there is wider multi-company support

## Slide 26: 2.3) Rel-16 and later Work and Maint. (8/23)
WI | Work Item | WP |  | 
FS_eLCS | Study on Enhancement to Service Based Architecture for Location Services | 45 > 55% |  | 
Progress since SA#80
  2 new key issue and 5 new solutions captured
  6 existing solutions updated
  Interim agreement for 4 key issues (#1, #4, #12, #14)
  SID update provided for approval, extending to December
RAN impacts or dependencies:
  System architecture to support NR positioning method defined by RAN
  Potentially a new positioning architecture affecting RAN
Next steps:
  In Q4/2018: Conclude the first part of the study
  Next year: Continuing with the second part of the study

## Slide 27: 2.3) Rel-16 and later Work and Maint. (9/23)
WI | Work Item | WP |  | 
FS_5G-SRVCC | Study for single radio voice continuity from 5GS to 3G | 80 > 100% |  | 
Progress since SA#80
  5 solutions have been documented
  Evaluation and conclusion for all the 4 key issues completed
  TR 23.756 is concluded and provided for approval
  A WID is provided for approval
RAN impacts or dependencies
  NG-RAN support by measurements for SRVCC from 5GS to 3G
Next steps:
  Conducting related normative work

## Slide 28: 2.3) Rel-16 and later Work and Maint. (10/23)
WI | Work Item | WP |  | 
FS_RACS | Study on optimisations on UE radio capability signalling | 0 > 40% |  | 
Progress since SA#80
  3 key issues agreed
  8 solutions for these key issues documented
RAN impacts or dependencies
  Format of efficient representation of UE radio capabilities
  Maximum expected size of UE radio capabilities (LSs exchanged)
  Access Stratum signalling impacts e.g. in RRC
Next steps:
  Study continues, intends to conclude by SA#82

## Slide 29: 2.3) Rel-16 and later Work and Maint. (11/23)
WI | Work Item | WP |  | 
FS_Vertical_LAN | Study on 5GS Enhanced support of Vertical and LAN Services | 0 > 25% |  | 
Progress since SA#80
  6 key issues agreed (3 on type-a and type-b networks, 1 on Time Sensitive Networking (TSN), 2 on 5G LAN)
  12 Solutions being discussed and documented for all the Key issues
  Note: SA2 is facing a moving target in terms of type-a/type-b network definition. Lack of clarity with the definition in stage 1 hinders progress with stage 2 work
RAN impacts or dependencies
  So far identified: Integration of 5G System with TSN has dependency on NG-RAN. A related LS is sent to RAN1/2/3.
Next steps:
  Study continues, intends to conclude by SA#82

## Slide 30: 2.3) Rel-16 and later Work and Maint. (12/23)
WI | Work Item | WP |  | 
FS_5G_URLLC | Study on enhancement of URLLC supporting in 5GC | 15 > 60% |  | 
Progress since SA#80
  2 new KIs added (low latency for UE in RRC_inactive and PDB division). Now 6 in total.
  13 solutions documented for various key issues. TR provided to TSG SA for information.
RAN impacts or dependencies (following items may lead to impacts/dependencies)
  KI#1: High reliability by redundant transmission in UP between UE/RAN and CN
  KI#2: Low latency and low jitter during handover procedure
  KI#4: QoS Monitoring for the QoS Flow to assist URLLC service
  KI#5: Low latency without requiring the UE to always be in RRC_Connected mode
Next steps
  Develop further solutions, evaluation and interim conclusions.
  Initiate exchange with RAN on aspects that may require coordination or alignment.

## Slide 31: 2.3) Rel-16 and later Work and Maint. (13/23)
WI | Work Item | WP |  | 
FS_eSBA | Study on Enhancements to the Service-Based 5G System Architecture | 15 > 60% |  | 
Progress since SA#80
  7 Key issues identified and captured in the TR
  Solutions developed for most of the key issues
  Principles developed for evaluating backward compatibility of solutions
  TR is provided to TSG SA for information
RAN impacts or dependencies
  None identified
Next steps:
  Continue developing solutions for key issues that are not yet well addressed
  Refine solutions and evaluate solutions for key issues 3 (framework) and 4 (reliability)
  Interim agreements

## Slide 32: 2.3) Rel-16 and later Work and Maint. (14/23)
WI | Work Item | WP |  | 
FS_eNS | Study on Enhancement of Network Slicing | 10 > 50% |  | 
Progress since SA#80
  All 3 main key issues have corresponding solutions documented
RAN impacts or dependencies
  None identified
Next steps:
  Solutions clean-up and possibly merge of solutions
  Evaluation and down-selection for concluding on solution(s) for each key issue

## Slide 33: 2.3) Rel-16 and later Work and Maint. (15/23)
WI | Work Item | WP |  | 
FS_UDICoM | Study on User data interworking, Coexistence and Migration | 0 > 30% |  | 
Progress since SA#80
  Work started
  2 key issues and 3 solutions are documented
  SID updated and provided for approval
RAN impacts or dependencies
  None identified
Next steps:
  Work on solutions, evaluations and conclusions

## Slide 34: 2.3) Rel-16 and later Work and Maint. (16/23)
WI | Work Item | WP |  | 
FS_5GSAT_ARCH | Study on architecture aspects for using satellite access in 5G | 2 > 15% |  | 
Progress since SA#80
  TR Skeleton defined
  Two Information Annexes introduced on satellite characteristics
  4 Reference scenarios defined as well as 3 Key issues documented
RAN impacts or dependencies:
  Some potential effects on QoS (delay) from the satellite backhauling scenario.
Next steps:
  Introduce possibly additional key issues.
  Work on solutions for key issues that have been defined
· ·

## Slide 35: 2.3) Rel-16 and later Work and Maint. (17/23)
WI | Work Item | WP |  | 
FS_ENTRADE | Study on encrypted traffic detection and verification | 70 > 70% |  | 
Progress since SA#80
  No work conducted as not determined as focus area by TSG SA
Next steps:
  To be determined by TSG SA

## Slide 36: 2.3) Rel-16 and later Work and Maint. (18/23)
WI | Work Item | WP |  | 
FS_eIMS5G | Study on Enhanced IMS to 5GC Integration | 40 > 40% |  | 
Progress since SA#80
  No work conducted as not determined as focus area by TSG SA
  The SID is updated with an approval date of June 2019 and submitted for approval
Next steps:
  To be determined by TSG SA

## Slide 37: 2.3) Rel-16 and later Work and Maint. (19/23)
WI | Work Item | WP |  | 
FS_LLC_Mob | Study on EPC support for Mobility with Low Latency Communication | 75 > 75% |  | 
Progress since SA#80
  No work conducted as not determined as focus area by TSG SA
RAN impacts or dependencies
  None identified
Next steps:
  To be determined by TSG SA

## Slide 38: 2.3) Rel-16 and later Work and Maint. (20/23)
WI | Work Item | WP |  | 
FS_AAI_LTE_NR | Study on Application Awareness Interworking between LTE and NR | 30 > 30% |  | 
Progress since SA#80
  No work conducted as not determined as focus area by TSG SA
Next steps:
  To be determined by TSG SA

## Slide 39: 2.3) Rel-16 and later Work and Maint. (21/23)
WI | Work Item | WP |  | 
FS_EPS_URACE | Study on enhancement of systems using EPS for Ultra Reliability and Availability using commodity equipment | 10 > 10% |  | 
Progress since SA#80
  No work conducted as not determined as focus area by TSG SA
RAN impacts or dependencies
  High availability by redundant transmission in UP between UE/RAN and CN (may impact cell reselection and handover target selection)
  Notification control for GBR bearers
Next steps:
  To be determined by TSG SA

## Slide 40: 2.3) Rel-16 and later Work and Maint. (22/23)
WI | Work Item | WP |  | 
TEI16 | Technical Enhancements and Improvements Rel-16 | n.a. |  | 
Progress since SA#80
  2 CRs for Enhancement of network event reporting
Next steps:

## Slide 41: 2.3) Rel-16 and later Work and Maint. (23/23)
WI | Work Item | WP | CRs approved
TEI16 | Maintenance for pre-Rel-16 features in Rel-16 specs only |  | 

## Slide 42: Contents
1) General aspects (events since SA#80, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs/SIDs and Exceptions
  2.5) IETF Dependency Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 43: 2.4) New and Updated WIDs/SIDs and Exceptions
New WID:
  SP-180737, New WID on Single Radio Voice Continuity from 5GS to 3G
  SP-180738, New WID on System enhancements for Provision of Access to Restricted Local Operator Services by Unauthenticated UEs
REVISED WID:
  SP-180731, Revised SID: Study on Enhancing Topology of SMF and UPF in 5G Networks (FS_ETSUN)
  SP-180732, Revised SID: Study on Access Traffic Steering, Switch and Splitting support in the 5G system architecture (FS_ATSSS)
  SP-180733, Revised SID: Study on architecture enhancements for 3GPP support of advanced V2X services (FS_eV2XARC)
  SP-180734, Revised SID: Study on Enhancement to Service Based Architecture for Location Services (FS_eLCS)
  SP-180735, Revised SID: Study on User Data Interworking, Coexistence and Migration (FS_UDICoM)
  SP-180736, Revised SID: Study on Enhanced IMS to 5GC Integration (FS_eIMS5G)
  SP-180792, Revised SID: Study of enablers for Network Automation (FS_eNA)

## Slide 44: Contents
1) General aspects (events since SA#80, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs and SIDs
  2.5) IETF and External SDO Normative Reference Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 45: 2.5) IETF and External SDO Normative Reference Update (1/1)
none

## Slide 46: Contents
1) General aspects (events since SA#80, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs and SIDs
  2.5) IETF Dependency Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 47: Contents
1) General aspects (events since SA#80, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs and SIDs
  2.5) IETF Dependency Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 48: 4) Documents for Information and Approval
Presentation for Information
  SP-180739, Presentation of TR 23.726 to TSG SA for information (FS_ETSUN)
  SP-180740, Presentation of TR 23.716 to TSG SA for information (FS_5WWC)
  SP-180741, Presentation of TR 23.791 to TSG SA for information (FS_ATSSS)
  SP-180744, Presentation of TR 23.742 to TSG SA for information (FS_eSBA)
  SP-180745, Presentation of TR 23.725 to TSG SA for information (FS_5G_URLLC)
  SP-180793, Presentation of TR 23.724 to TSG SA for information (FS_CIoT_5G)
For Approval
  SP-180742, Presentation of TR 23.715 to TSG SA for approval (FS_PARLOS_SA2)
  SP-180743, Presentation of TR 23.756 to TSG SA for approval (FS_5G-SRVCC)

## Slide 49: Contents
1) General aspects (events since SA#80, statistics, next meetings)
2) SA Work Report
  2.1) Rel-14 and before Maintenance
  2.2) Rel-15 Maintenance and Work
  2.3) Rel-16 and later Work and Maintenance
  2.4) New and Updated WIDs and SIDs
  2.5) IETF Dependency Update
3) Action Items
4) Documents for Information and Approval
5) Collected Items requiring action from SA
è

## Slide 50: 5) Collected Items requiring action from SA
    Approval of proposed/updated WIDs
  SP-180731, Revised SID: Study on Enhancing Topology of SMF and UPF in 5G Networks (FS_ETSUN)
  SP-180732, Revised SID: Study on Access Traffic Steering, Switch and Splitting support in the 5G system architecture (FS_ATSSS)
  SP-180733, Revised SID: Study on architecture enhancements for 3GPP support of advanced V2X services (FS_eV2XARC)
  SP-180734, Revised SID: Study on Enhancement to Service Based Architecture for Location Services (FS_eLCS)
  SP-180735, Revised SID: Study on User Data Interworking, Coexistence and Migration (FS_UDICoM)
  SP-180736, Revised SID: Study on Enhanced IMS to 5GC Integration (FS_eIMS5G)
  SP-180737, New WID on single radio voice continuity from 5GS to 3G
  SP-180738, New WID: System enhancements for Provision of Access to Restricted Local Operator Services by Unauthenticated UEs

## Slide 51
Thank You!

## Slide 52
Annex: SA2 work planning sheet
    SA2#128bis endorsed the budgets shown for Oct and Nov. (embedded excel, open with MS Excel)
    Some studies increased budgets compared to what was input to TSG SA#80 for planning/decision. There is a slight overload that will be managed by reducing endorsed budgets slightly based on amount of submitted tdocs.
    R16 studies with some backlog. Handled tdocs per study: V2X-60%, 5WWC-50%, ATSSS-55%, CIoT-40%, eNA-50%, vLAN-65%, URLLC-70%, RACS-55%