## Slide 1: 5GC enhancement for Satellite access in Rel18 (presentation slides for SP-210986)
Source:
Thales, Xiaomi
Supporting companies:
ESA, SES, Sateliot, Gatehouse, Intelsat, TNO, Hispasat, Novamint, Hughes Network System, Gilat Satelite networks Ltd
SP-210988

## Slide 2: 5GC enhancement for satellite access in Rel18
Where we are:
  Following study (TR23.737) Work Item for Integration of satellite components in the 5G architecture (5GSAT_ARCH) (R17) is now completed, with first normative step enabling satellite is R17.
  We are in the selection process for R18 content, for RAN and SA TSGs, ending in December 2021.
Where we want to go:
  To the definition of a consolidated R18 Study Item for satellite access in Q4, to be able to enhance and complete the 5GC architecture.
  in accordance with RAN feature selection.
  The present slideware is a short list of candidate features we consider as first stones in such R18 satellite SID:

## Slide 3: 5GC enhancement for satellite access in Rel18
#1 Discontinuous coverage
#2 Store and forward (regenerative payload)
#3 Broadcast/multicast
#4 Network based UE location determination
#5 Support of Performance Enhancement Proxy
#6 Service continuity
#7 Relay based architecture including satellite

## Slide 4: #1 Discontinuous coverage
Justification:
  Dynamic support of discontinuous coverage is required for initial NGSO constellation deployment but as well to support evolution of the constellations such as loss of satellites, different releases supported in a given constellation…).
  There is an important aspect of discontinuous coverage related to dynamic GEO systems where beams/cells are intermittent due to use of dynamic beam configuration
5GC areas for study:
  Mobility Enhancement (Paging…)
  Prediction, awareness & notification of UE wake-up time, power saving optimizations.
Problem Statement:
  UE under satellite coverage only at specific time and places due to spares constellation.
  Paging to be synchronized with UE and satellite motion.
  UE should not always stay awake for the sake of power efficiency, especially for MIoT UE

## Slide 5: #2 Store and forward (regenerative payload)
Justification:
  The support of an store-and-forward capabilities will allow providing service coverage with NGSO satellites to areas where NTN-GWs cannot be deployed (e.g. deep-sea maritime areas). Moreover, the support of store-and-forward capabilities would allow for a reduced network of NTN-GWs and still achieve global service coverage for delay-tolerant/non-real-time IoT NTN services.
5GC areas for study:
  Session and Mobility management enhancements for the use case.
  User plane enhancements for the use case.
Problem statement:
  The satellite need to embark eNB function and storage capability (plus, potentially, some core network functionality) in order to harvest data from IoT devices along its orbit and forward it to a core network when it encounters a NTN-GW and the feeder link can be activated. Conversely, the satellite uploads data from core network when connected to a NTN-GW and delivers it to the relevant IoT-devices when covering the targeted service area.

## Slide 6: #3 Broadcast/multicast
Justification:
  To meet for example public safety needs, software upgrades and multimedia content distribution.
  Also for IoT (type of) applications that require e.g. triggering or distribution of messages.
5GC areas for study:
  Location and MBS Service Area determination for content transfer
  Supporting differentiated QoS for MBS.
  Content transfer for UEs temporarily out of coverage due to discontinuous coverage or regenerative payload
  User plane path selection between satellite path and terrestrial path for efficient content transfer
Problem statement:
  UE Location dependent content transfer and MBS Service Area requires accurate location; however, the coverage of one cell over satellite access may include multiple countries or across country boarders
  Different UE or UE category which join in multicast service may have different QoS requirement(e.g. 5GC Individual MBS traffic delivery or 5GC shared MBS traffic delivery with PTP/PTM method), to efficient usage of network resources, especially limited satellite resources, differentiate QoS should be supported by satellite access
  When UEs are temporarily out of coverage due to discontinuous coverage or regenerative payload, store and forward may be needed in the network
  When both satellite path and terrestrial path are available, the performance of each path may be different

## Slide 7: #4 Network based UE location determination
Justification:
  For regulatory services (e.g. lawful intercept, emergency communications, public warning service) as well as handling of extraterritoriality requirements where Law enforcement apply, the network shall be able to provide a “reliable” UE location (either network verified or network provided).
5GC areas for study:
  Refine triggering conditions after LCS framework new method definition .
  Check compliancy with regulated service requirements (network provided or verified)(TS 22.261).
  Check compliancy with extraterritoriality requirements (See SA1 extra-territoriality 5GET study)
  Possible architectural enhancement to meet location services requirements as defined in TS 22.261.
Problem statement:
  The Core Network shall be capable of making efficient use of this method according R17 UE localization mechanisms.

## Slide 8: #5 Support of Performance Enhancement Proxy
Justification:
  In case of GEO satellite access for Uu interface, any connected protocol (TCP, QUIC, SCTP…) will be degraded at performance and user quality of experience levels in case of long delay.
5GC areas for study:
  Investigate if solution can be endorsed by 3GPP to enhance user quality of experience for connected protocols in case of PEP long delay.
  Investigate where PEP can be placed in 5GC architecture (SA2).
  Investigate how PEP can be integrated in security architecture (SA3).
Problem statement:
  To cope with GEO delay, a widely used solution is to make use of PEPs (performance Enhancement Proxies).
  If IP level security layer is used over satellite access, such PEPs cannot be used.

## Slide 9: #6 Service continuity
Justification:
  Service continuity when switching between terrestrial and satellite access networks is key to the user experience.
  When both 5G terrestrial access network and 5G satellite access are available, the performance of each access shall be considered for some specific applications for the handover, see use case defined in clause 5.7 of TR 22.822
5GC areas for study:
  Hand Over based application preference: enhance architecture (new mobility triggers) such like application would have choice between satellite access for the benefits of service continuity, and terrestrial access taking advantage of the short delay, large bandwidth and strong reliability.
  Service continuity in case of shared satellite RAN, with multiple CN (e.g.: autonomous ships near coastal areas )
Problem statement:
  To cope for an ongoing service application, e.g. VoNR emergency call, the service continuity has to be guaranteed:
    Case A: If it is running over satellite access, when UE moves into an area with 5G terrestrial coverage, it may handover to the gNB providing 5G terrestrial coverage.
    Case B: If it is running over terrestrial 5G NR, when UE moves into an area of no terrestrial 5G NR coverage but under the satellite coverage, it may handover to the gNB with satellite access.

## Slide 10: #7 Relay based architecture including satellite
Justification:
  (SA1) 5G system shall be able to support mobile base station relays using 3GPP satellite NG-RAN
  (SA2 R17) 5G system shall be able to support UE to NW relay with Uu by satellite
  Store and forward relay will strongly enhance applicability of store and forward scheme (see #2), e.g.: IoT devices needing relay that would use store and forwarding on dedicated satellite system.
5GC areas for study:
  Applicability of existing solutions for satellite?
  Store and forward relay architecture and procedures
Problem statement:
  In IoT use cases, the satellite coverage deployment scheme will most probably request store and forward support at the relay level.
  Modification of existing solutions for satellite
  Opportunistic relay connectivity of the relay Base Station to 5GC via Terrestrial or Satellite.

## Slide 11: Thank you!