## Slide 1: Facilitating roaming/ interworking adoption across 3GPP NPN deployments (related to the incoming LS from WBA OpenRoaming in SP-220730)
Intel, Cisco
SA#97E, Electronic meeting, 13 – 19 Sep 2022
SP-220955

## Slide 2: Introduction
In June 2020, WBA announced the launch of a new roaming federation to lower the barriers to adoption of roaming functionality by access network providers and identity providers.
  The OpenRoaming federation comprises a technical framework and a legal framework that was originally conceived of to facilitate the adoption of roaming by the significant number of private enterprises that have deployed Wi-Fi systems to support inbound roaming for guests that use credentials managed by third party identity providers.
  In May 2022, WBA announced that over 1 million hotspots had been connected to the OpenRoaming federation.
In 2021, WBA approved the formation of the “OpenRoaming for 5G” project that was tasked with examining the opportunity of re-using OpenRoaming concepts to accelerate the adoption of roaming across non-public 3GPP networks.
  WBA have recently completed the first deliverable from this project that identifies several key issues that may be pertinent to facilitating roaming onto non-public networks.
  While the WBA deliverable is attached to the incoming LS in SP-220730, the LS text points to key aspects of the analysis as it relates to the specification of NPN systems by 3GPP and asks questions to SA3, SA and CT6

## Slide 3: Questions to SA3
The LS in SP-220730 (S3-221740) identified specific issues for SA3 as follows:
  Potential scalability issue for the N32 reference points (SEPP to SEPP) due to the persistence of the N32 connection
  Potential issue related to firewall traversal on N32
In response to this LS, there was a study proposal in SA3#108E (S3-222039; Study on enhancements to facilitate N32 adoption by Standalone Non-Public Networks) proposing to study solutions for the N32 scalability and firewall traversal issues identified by WBA in SP-220730
  The proposal was noted on the grounds that supporting NPN/PLMN interworking with Open Roaming has impacts beyond SA3 and that these requirements for interworking/roaming should be first considered by other groups such as 3GPP SA/SA2
  The draft reply LS from SA3 to WBA (S3-222040) was postponed awaiting a reply to the LS by SA

## Slide 4: Seeking guidance from SA
The proponents of this study expect that 3GPP will support the WBA request for facilitating roaming/ interworking adoption across 3GPP NPN deployments and are seeking guidance from SA on how to accommodate this request
  One possibility (Option A) could be for SA plenary to task SA3 WG to further work on an agreeable revision of S3-222039
    The advantage of this approach is that the study would be conducted as part of Rel-18 (it is noted that the Rel-18 door in SA2 is closed for new work, unless it can be handled as alignment work)
  Another possibility (Option B) could be for SA plenary to identify the relevant WG where this work should be initiated
    E.g. should the proponents bring a SID or WID on facilitating roaming/interworking adoption across 3GPP NPN deployments in SA1 WG?
    With this approach the work will certainly be pushed into Rel-19. According to the SA1 WG Chair’s report in SP-220661, the Rel-19 door in SA1 is still open:
      “This does not preclude, whenever there will be consensus, to later introduce “exceptional studies” and small “delta” normative work (such as work not needing prior study).”

## Slide 5: Proposals
1) The authors of this contribution request SA to provide guidance on the best way for addressing the WBA’s request for facilitating roaming/ interworking adoption across 3GPP NPN deployments
2) Also proposed is to convey the agreed SA guidance to WBA in a reply LS
  A draft reply LS to the incoming LS in SP-220730 is available in SP-220906, currently focusing only on the WBA question to SA on devices with multiple credentials.
  Any agreed SA guidance related to the questions to SA3 can be piggybacked on this reply LS