## Slide 1: On misalignment between SA3 and CT4 on the usage of OAuth 2.0 in NRF APIs
Source: Nokia
3GPP TSG SA Meeting #92e 15 - 21 June 2021, Electronic meeting
SP-210555

## Slide 2: History and details on misalignments
SA3/CT4 LS exchange in 2018, CT4 answering that Oauth client registration is out of scope of 3GPP Rel-15 (C4-185505).
However, SA3 mandated Oauth 2.0 client registration using the NRF NF Register service operation, w/o notifying so to CT4.
Thus, misalignments between SA3 and SA2/CT4 specs exist:
Oauth2 client registration:
  TS 33.501 mandates Oauth clients to register to NRF (using NF Register) prior to requesting access tokens
  TS 23.502 / TS 29.510: NF Register is used by NF producers to register the services they expose to other NFs.
Use of Oauth for NF Register and NF Discovery requests:
  TS 33.501 contains an informative note saying that Oauth is not needed for these requests
  TS 29.510: this is an option (per operator policy)
These misalignments can cause interoperability issues, if some implementations follow TS 33.501, others TS 29.510.

## Slide 3: Views from the authors why it is recommended to align with CT4 specification
NFs only behaving as consumers (e.g., CBCF, S-CSCF, I-CSCF, AS) are not expected to register an NF profile to NRF.
PLMN with multiple NRFs:
  NF producers may register services in one NRF and consume services discovered from other NRFs.
  Different deployment models can exist, e.g. AMF sending access token requests always via its local NRF, or directly to a slice specific NRF configured locally or discovered from NSSF.
Recent slice attack reported by GSMA: using NF Register as OAuth 2.0 client registration allows a malicious/compromise NF to register non-authorized slice and obtain access tokens to access services of that slice.
RFC 6749 / RFC 7591: registration of a client with an authorization server can be (typically) performed w/o interactions between the client and Oauth server.
It is proposed to update TS 33.501 to no longer mandate NF Register for Oauth client registration.

## Slide 4: CT4/SA3 alignment status (1/2) (CP-211017)
CT4 chairman notes on a way forward after SA3/CT4 telco (31 March 2021)
On misalignment on access token request requirement between TS 29.510 and 33.501 Status:
  A conference call was held with participants from SA3 and CT4 and as a way forward :
  It was proposed to discuss separation of Oauth2.0 Authorization and NRF registration. This would be a possible discussion in SA3 for Rel-17. We need to find a pragmatic solution for Rel-15 and Rel-16.
  We agreed to work first on the two open issues:
  Correct the stage-2 (TS 33.501), clauses 13.4.1.1 and 13.4.1.2, for the definition of the Oauth2 Client Registration process by defining for Rel-15/16 a kind of Static Authorization/O&M configuration process.
  The NOTE in TS 33.501 clause 13.3.1.3 should be changed to normative text clarifying that the usage of Oauth2 in the NRF APIs (NFManagement and NFDiscovery) is optional.
  No progress was made in last SA3 meeting, so no discussion took place in CT4 on this topic.

## Slide 5: CT4/SA3 alignment status (2/2)
Summary of compromise proposed by Nokia in SA3:
Cover all 3 releases in one step, but we can continue to analyse Rel-17.
Keep in stage 3 the option to use Oauth for NF Register and NF Discovery requests but discourage its usage in R15/R16. Align accordingly in stage 2 spec.
Specify the potential use of OAuth for accessing NRF APIs in Rel-17.
Make the NF Service registration procedure (NF Register) optional (and NOT mandatory) to register the OAuth 2.0 client (NF Service Consumer) with the OAuth 2.0 Authorization server (NRF)
… provided it is further specified that this NF service registration (NF Register) – as OAuth client registration - shall NOT be a pre-requisite for any NF to issue Access Token requests and obtain access tokens from the NRF, i.e in other words, an NF that does NOT implement the option shall still be able to get Access tokens (and NRF services).

## Slide 6: Proposal
We propose to consider the compromise (draft_S3-211752-r4).
We suggest SA#92 tasks SA3 to prioritize the resolution of the misalignments in Q3 2021.

## Slide 7: Background material
The following slides contain background material. They were part of a slide set presented at the CT4/SA3 conf call on March 31th 2021.

## Slide 8: Latest LS from SA3 to CT4
Last year, SA3 sent LS to CT4 (S3-203495 / C4-211156) with following information:
  TS 29.510 contains provisions allowing, optionally, the NRF APIs (NFManagement and NFDiscovery) to be authorized by means of Oauth2.
    SA3 questions whether such usage of Oauth2 is independent of the usage of Oauth2 in the rest of 5GC APIs
  TS 33.501, clause 13.3.1.3, contains an informative NOTE indicating that the usage of Oauth2 for the NRF APIs is not needed

## Slide 9: Quick feedback from the authors on the SA3 sent LS to CT4 (S3-203495 / C4-211156)
The usage of Oauth2 in the NRF APIs (NFManagement and NFDiscovery) is optional and entirely independent of the usage of Oauth2 in the rest of the APIs in 5GC
  The principle is that each service of any NF in the 5GC (including the NRF APIs) can enforce Oauth2-based authorization independently
  From Rel-16 onwards, as a general feature in 5GC APIs, such granularity goes beyond the service level, and it could enforce the authorization on a per resource/operation level
The NOTE in TS 33.501 is a known issue by both SA3 and CT4, since there has been several attempts in the past to align both specs, without success
  This NOTE, per 3GPP working methods, is non-normative; as such, misalignment with the contents of the NOTE per-se does not constitute a non-compliance against TS 33.501
  The NOTE was added by SA3 (in TS 33.501, v15.2.0, Sept. 2018) after CT4 had specified the optional usage of Oauth2 in the NRF APIs (in TS 29.510, v0.7.0, May 2018)

## Slide 10: Usage of Oauth2 in the NRF APIs (1 of 3)
CT4 added Oauth2-based authorization to the NRF-specific APIs (NFManagement and NFDiscovery) in the very first versions of TS 29.510 (TS version 0.7.0, May 2018)
  It is optional to be used (based on operator’s deployment choice)
  Its usage is independent for each API (NFManagement / NFDiscovery)
  It is not used in Access Token Request API or in Bootstrapping API

## Slide 11: Usage of Oauth2 in the NRF APIs (2 of 3)
It was seen by CT4 as beneficial to employ the same authorization principles used for all other APIs, based on Oauth2, but applied to the NRF-specific APIs as well. It allows to apply policies such as:
  Certain consumers of the NRF APIs may be allowed to invoke NFDiscovery but not allowed to invoke NFManagement (and vice versa)
  Certain consumers of the NRF APIs may be allowed to invoke certain operations of NFManagement (e.g., subscribe to changes of discovered NF profiles), but not others (e.g., not allowed to register, or to query the NRF catalog of NF Instances)
  It allows easy evolution, consistent with all other APIs in 5GC, to apply this same Oauth2-based authorization mechanism when more NRF services/resources/operations are added in the future

## Slide 12: Usage of Oauth2 in the NRF APIs (3 of 3)
When this potential misalignment between TS 33.501 and TS 29.510 was discussed in SA3 and CT4, it was argued by some companies:
  Oauth2 cannot be used in NFManagement API because that’s the mechanism used for Oauth2 Client Registration (NFManagement_Register service operation)
  It would lead to a chicken-and-egg problem, since an Oauth2 Access Token must be obtained in order to be registered as an Oauth2 client
This leads to another major deviation and misalignment:
  How to perform the Oauth2 Client Registration in NRF

## Slide 13: Oauth2 Client Registration (1 of 4)
Oauth2 Client Registration is the process by which an entity is “enrolled” in an authorization server as a potential consumer of the Access Token Request service
  This is something essentially applicable to an NF Service Consumer, with views to obtaining an access token, and later invoke services on an NF Service Producer
  As indicated in IETF RFC 6749 “The OAuth 2.0 Authorization Framework”, clause 2:
      “Client registration does not require a direct interaction between the client and the authorization server”
TS 33.501 specifies that the Oauth2 client registration shall be done by invoking the NFManagement_Register service operation
  This approach is not consistent; e.g., in roaming scenarios:
    The NF Service Consumer in VPLMN does not register in the H-NRF
    Still, the H-NRF issues access tokens for those NF Service Consumers
  Also, not consistent in scenarios with multiple slices. E.g., UE registration with AMF Reallocation:
    AMF1 in Slice1 may have to discover a different AMF2 in Slice2 using the slice-specific NRF2 provided from NSSF. It would be very awkward if, in order to consume services from AMF2, AMF1 would have to first Register to NRF2 in Slice2 (a slice that AMF1 does not even support/belong to…)

## Slide 14: Oauth2 Client Registration (2 of 4)
Using NFManagement _Register for Oauth2 Client Registration does not fit at all with how the NRF services have been conceived and designed (both at stage-2 and stage-3 levels, in SA2 and CT4)
  The NRF is a repository where NF Instances register to advertise their availability, and to expose how to discover and consume their services (if any); it is meant for NF Service Producers
  The NRF keeps track of the status of each NF Instance
  The NF Service Producers maintain such status by invoking periodically a Heart-Beat
    NF Instances not sending those heart-beats are marked as unavailable and may eventually be removed from NRF

## Slide 15: Oauth2 client registration (3 of 4)
The Oauth2 client registration, on the other hand, is something applicable to NF Service Consumers. In general, service consumers:
  Should not need to make themselves available and discoverable to others
  Should not be required to provide an “NF profile” in the same way as NF Service Producers are required to do so
    In any case, such “profile” should be an “Oauth2 client profile”, which might be totally different to the existing “NF Profile” of NF Service Producers
  Should not be required to send heart-beats or to maintain a “status” in NRF
  Should not even be required to be “always-up”
Oauth2 client registration is typically done by O&M configuration
  See IETF RFC 7591 “OAuth 2.0 Dynamic Client Registration Protocol”:
      “Traditionally, registration of a client with an authorization server is performed manually”
  In the future, it is FFS whether 3GPP might consider using a standard protocol for Oauth2 Client Registration

## Slide 16: Oauth2 client registration (4 of 4)
TS 33.501, clause 13.4.1.1, indicates:
    OAuth 2.0 client (NF Service Consumer) registration with the OAuth 2.0 authorization server (NRF)
    The NF Service registration procedure, as defined in clause 4.17.1 of TS 23.502 [8], shall be used to register the OAuth 2.0 client (NF Service Consumer) with the OAuth 2.0 Authorization server (NRF), as described in clause 2.0 of RFC 6749 [43]. The client id, used during OAuth 2.0 registration, shall be the NF Instance Id of the NF.
Examples of NFs that are purely NF Service Consumers, for which it makes no sense to be required to register in NRF with NFManagement_Register:
  From Rel-15 onwards; CBCF, possibly GMLC, possibly NEF (Standard Rel-15 NEF just offers one interface within the network, towards the PCF; if this interface is not deployed, there is no need for NEF to register)
  From Rel-16 onwards: I-CSCF, S-CSCF, TAS, and SCC-AS are service consumers, but not service producers; a Rel-16 P-CSCF may also consume N5 services before supporting service registration
Examples of NFs that produce / register services in one NRF and may consume services discovered from different NRFs:
  Scenarios where an NF registers its services to an NRF X but need to discover other NF services from an NRF Y, e.g., AMF registering to a PLMN-level NRF but performing discovery requests to network slice specific NRFs (e.g., to discover an SMF/PCF).
In the scenarios above, an NF Service Consumer SHALL NOT be forced to issue an NFManagement_Register operation simply to be able to issue an NFDiscovery_Request operation