## Slide 1: 5G common Core Applying 5G QoS Concepts to Wireline Access
AT&T
3BF-170008
Agenda Item: 3

## Slide 2: 5G QoS Concepts
QoS Profile comprises of User plane marking referred to as a 5G QoS indicator (5QI) and corresponding 5G QoS characteristics
  5QI values can be standard or non standard. When non standard values are used, QoS characteristics will have to be sent out of band to the AN
QoS Rule consists of QoS profile, packet filters and precedence order.
  The QoS rules are provided to the AN via out of band signalling, provided at session establishment and when a session is re-activated.
  For non-3GPP accesses such as wireline it is possible to pre provision the AN and the devices with QoS Rules to avoid support for out of band QoS signalling provided these rules are static
QoS Enforcement
  User plane performs per session Aggregate Maximum Bit Rate enforcement and also performs packet counting for support of charging

## Slide 3: 5G QoS Concepts
Uses a Flow Based QoS Model
  All traffic for a UE session with a packet data network that requires the same forwarding treatment is considered to constitute a QoS Flow
  A UE session with a packet data network is encapsulated in a single tunnel and packet marking within header of this tunnel identifies the QoS Flow
  Access Network maps downlink packets from 5G QoS flows to access-specific resources based on the QoS information provided by the 5G core inband through tunnel headers and also where needed additional information provided by the 5G core via out of band signalling
  Uses “Reflective QoS” to allow uplink traffic to get same QoS treatment as downlink. Reflective QoS can be enabled / disabled via inband indication using tunnel header marking or via explicit out of band signaling
Supports both GBR and Non-GBR type flows
Model can be applied to packets with different types of payload, i.e. IP packets, non-IP packets (e.g. unstructured data) and Ethernet frames

## Slide 4: QoS related Questions for BBF
Is there a need for dynamic set up of Guaranteed Bit Rate sessions in wireline 5G Networks?
  This would require support of out of band signaling to the wireline access network to communicate GBR parameter
Is there a need for support of dynamic set up of sessions with non standard QoS types?
  This would require support of out of band signaling to communicate non standard QoS characteristics
Are there other wireline QoS related scenarios that would require out of band QoS signaling?
Can wireline access networks and devices be expected to support out of band QoS related signaling via 3GPP defined interfaces NG2 and NG1?
  QoS can be supported without these interfaces but without support for the first two bullets

## Slide 5: Appendix: 5G System Architecture