## Slide 1: Operator Use Cases and Architectural requirements for convergence SA2/BBF workshop (18th Feb 2017)
British Telecom, Deutsche Telekom, Orange, Vodafone, Telefonica, TIM, KT
3BF-170015

## Slide 2: Definition of Terms used in this presentation “Trusted”, “Untrusted” & “Managed”
Rather than define all possible scenarios, this presentation focuses on network integration and implementation that are likely to be deployed in the real world
“Managed by the NextGen Core operator” implies for the Access Network (AN) that it is technically and administratively integrated with the NextGen Core Network (CN)
  the AN may be owned by the NGC operator or by another entity having a business relationship with the NGC operator
“Trusted by the NextGen Core operator” means that there is a well-defined business relationship between the NGC operator and the AN operator, including the mutual agreement on used / enforced security associations between the UE and the (access and/or core) network
  this covers both the case where AN and CN are owned by NGC operator or by different entities
“Untrusted” access network is an AN where the NGC operator makes no assumptions of ownership, administration or technical features of the AN (other than enabling IP connectivity towards the NGC)
  this implies, by definition, that untrusted AN is also unmanaged
 | Trusted | Untrusted
AN managed by the NextGen operator | In scope – “Trusted and managed” | In scope – “Untrusted”
AN not managed by the NextGen operator | Out of scope & not considered | 
Network Implementation
AN/CN Relationship

## Slide 3: Overview of Use Cases
NG UE connects to wireline and/or cellular
1: NG UE connects to wireline or cellular radio access (trusted and managed)
2: NG UE connects to wireline and cellular radio access simultaneously (trusted and managed)
NG UE connects to independent WLAN and/or cellular radio access network
3a: NG UE connects to independent WLAN or cellular radio access networks (trusted and managed)
3b: NG UE connects to independent WLAN or cellular radio access networks (untrusted)
4a: NG UE connects to independent WLAN and cellular radio access networks (trusted and managed) simultaneously
4b: NG UE connects to independent WLAN and cellular radio access networks (untrusted) simultaneously
NG UE connects to WLAN and/or cellular radio access network that uses wireline access network as backhaul
5a: NG UE connects to WLAN or cellular radio access that uses the wireline access network as backhaul (trusted and managed)
5b: NG UE connects to WLAN or cellular radio access that uses the wireline access network as backhaul (untrusted)
6a: NG UE connects to WLAN and cellular radio access that uses the wireline access network as backhaul (trusted and managed) simultaneously
6b: NG UE connects to WLAN and cellular radio access that uses the wireline access network as backhaul (untrusted) simultaneously
Notes:
Blue text represents use cases where a NG UE uses a single connection in the user plane over the chosen access network
Red text represents use cases where a NG UE uses parallel connections in the user plane over multiple access networks

## Slide 4: Use Case 1: NG UE connects to wireline or cellular radio access (trusted and managed)
Description
A multi-access capable Gateway (acting as a NG UE) can obtain Fixed Broadband services via either cellular radio (e.g. NR radio) or wireline (e.g. fibre) network, where both ANs are trusted and managed by the NextGen Core operator
  The multi-access Gateway can be a residential gateway (for residential market segment) or a business customer premises gateway (for business market segment)
  When the Gateway is online on one AN, use of network or Gateway resources on the other AN link shall be minimized
The set of services that the NextGen Core operator provides to the Gateway is (as much as possible) the same over wireline and cellular radio access
The NextGen Core identifies and authenticates the Gateway as a single subscriber independent of the access network used
Locally connected devices connected to the Gateway must not be visible to the NextGen Core
When the Gateway goes online (i.e. service communication is activated), the used access network is selected under control of the NextGen Core operator, e.g. based on subscription parameters, operator policies, network conditions and service requirements
While the Gateway is online, a change of access networks can occur if network conditions can’t meet service requirements (including that the UE reaches end of coverage for the current AN), or relevant subscription parameters or operator policies are changed
  In case of an access network change during ongoing sessions, customer services shall be continued with the least possible service impact
Gateway
(NG UE)
Wireline AN
(e.g. fibre)
Cellular Radio AN
(e.g. NR)
Subscriber ID(s) and credentials
Service scenarios / features
Recovery from Fixed Broadband failover (e.g. fibre downtime or cellular downtime due to maintenance or failure)
Rapid service activation via cellular AN prior to physical wireline access being available
“Nomadic” fixed broadband access – e.g. take your home broadband to your holiday home (use any available access network type)
Ability to switch over all traffic to an alternative access network when network conditions can’t meet service requirements
Consistent delivery of Value Added Services, charging, traffic policies etc., regardless of used access network
OR
Locally connected device
Locally connected device
Private LAN/WLAN
OR
e.g. fibre
e.g. NR
Control plane
Data plane
NextGen Core

## Slide 5: Use Case 2: NG UE connects to wireline and cellular radio access simultaneously (trusted and managed)
Description
This use case covers all the properties and features of use case 1, with the additional capability of obtaining Fixed Broadband services simultaneously via cellular radio (e.g. NR radio) and wireline (e.g. fibre) network
To optimize user experience as well as access network utilization, the NextGen Core and Gateway (NG UE) both natively support dynamic traffic combining, splitting & steering in the DL and UL direction respectively over multiple ANs, on a per-service flow and/or per-traffic type basis according to a set of policies defined by the NextGen Core operator to meet the needs of different traffic types or services
Service scenarios / features
All the features of use case 1 plus the following
  Ability to cost-effectively deliver higher data speeds to fixed broadband customers via simultaneous use of fixed and mobile access networks
  Best user experience - traffic routing decisions based on access network availability and application traffic type requirements (e.g. traffic splitting with fibre as primary, NR as overflow, traffic steering with 4K HDTV over fibre, other traffic over NR)
  Consistent delivery of Value Added Services, charging, traffic policies etc. when combining, splitting or steering traffic across the two access networks
NextGen Core
Wireline AN
(e.g. fibre)
Cellular Radio AN
(e.g. NR)
AND
Private LAN/WLAN
Traffic combining, splitting and steering
Traffic combining, splitting and steering
AND
e.g. NR
Control plane
Data plane
Gateway
(NG UE)
subscriber ID(s)
and credentials
e.g. fibre
Locally connected device
Locally connected device

## Slide 6: Use Case 3a: NG UE connects to independent WLAN or cellular radio access networks (trusted and managed)
Description
A single, multi-access capable NG UE (in this use case, assumed to be “mobile”) can obtain Mobile BB services via either cellular radio (e.g. NR radio) or wireline (e.g. fibre) network, where both ANs are trusted and managed by the NextGen Core operator
    the NG UE accesses the wireline AN by using a WLAN access on the Gateway
The set of services that the NextGen Core operator provides to the NG UE is (as much as possible) the same over wireline and cellular radio access
The NextGen Core identifies and authenticates the NG UE as a single subscriber independent of the used access network
  WiFi authentication may be performed locally by the Residential Gateway in the Wireline AN OR by the NextGen Core
When the NG UE goes online (i.e. service communication is activated), the used access network is selected under control of the NextGen Core operator, e.g. based on subscription parameters, operator policies, network conditions and service requirements
While the NG UE is online, a change of access networks can occur if network conditions can’t meet service requirements (including that the UE reaches end of coverage for the current AN), or relevant subscription parameters or operator policies are changed
  In case of an access network change during ongoing sessions, customer services shall be continued with the least possible service impact
Service scenarios / features
Ability to use wireline or cellular radio access network seamlessly to the end user to deliver the best and most cost-effective customer experience
Ability to switch over all traffic to an alternative access network when network conditions can’t meet service requirements
Consistent delivery of Value Added Services, charging, traffic policies etc., regardless of used access network
NextGen Core
NG UE
Wireline AN
(e.g. fibre)
Cellular Radio AN
(e.g. NR)
NG UE subscriber identity and credentials, and mobility & session management stack
OR
OR
Gateway
NOTE 1,2
NOTE 1: how the Gateway in this use case is connected to the NextGen Core, authenticated etc. is described in Use Cases 1 and 2. This use case does not include the option of using a third party wireline AN , which is use case 3b.
NOTE 2: from the perspective of the NG UE, the Gateway is the access node rather than a node in the wireline AN.
e.g. WiFi
Local WiFi Auth credentials
(Optional)
Control plane
Data plane
e.g. NR

## Slide 7: Use Case 3b: NG UE connects to independent WLAN or cellular radio access networks (untrusted)
Description
This use case covers all the properties and features of use case 3a, with the differences that
  a single, multi-access capable NG UE (in this use case, assumed to be “mobile”) can obtain Mobile BB services via either cellular radio (e.g. NR radio) or an untrusted wireline (e.g. fibre) access network from a single NextGen Core, where
  the cellular radio is trusted and managed by the NextGen core operator
  the wireline AN is an untrusted AN, owned and managed by a by a 3rd party (marked in green colour in diagram below)
  Note: There is a possibility that the trusted AN is the wireline AN and the untrusted AN is the cellular radio AN (not shown in the diagram below). In this scenario, the feature set should remain the same.
  The set of services that the NextGen Core operator provides to the NG UE is (as much as possible) the same over wireline and cellular radio access.
  NOTE: Compared to use case 3a there may be limitations in the level of QoS that can be provided, due to the use of an untrusted access network.
There may be limitations, regarding the level of service (including QoS) provided by the untrusted wireline access network
Service scenarios / features
Same as in use case 3a, but subject to the level of QoS supported by the untrusted AN, which may impact the NextGen core operator’s AN selection policies.
Control plane
Data plane
NextGen Core
NG UE
Wireline AN
(e.g. third party fibre)
Cellular Radio AN
(e.g. NR)
OR
OR
Gateway
NOTE 1, 2
e.g. WiFi
e.g. NR
Core
Local WiFi Auth credentials
NG UE subscriber identity and credentials, and mobility & session management stack
NOTE 1: how the Gateway in this use case is connected, authenticated etc. is outside of the scope of this use case since it is performed by a third party which does not own the NextGen Core.
NOTE 2: from the perspective of the NG UE, the Gateway is the access node rather than a node in the wireline AN.

## Slide 8: Use Case 4a: NG UE connects to independent WLAN and cellular radio access networks (trusted and managed) simultaneously
Description
This use case covers all the properties and features of use case 3a, with the additional capability that
  NG UE is able to obtain Mobile Broadband services simultaneously via cellular radio (e.g. NR radio) and wireline (e.g. fibre) network
To optimize user experience as well as access network utilization, the NextGen Core and NG UE both natively support dynamic traffic combining, splitting & steering in the DL and UL direction respectively over multiple ANs, on a per-service flow and/or per-traffic type basis according to a set of policies defined by the NextGen Core operator to meet the needs of different traffic types or services.
User experience should be seamless when moving between access networks
Service scenarios / features
Ability to cost-effectively deliver higher data speeds to mobile broadband customers via simultaneous use of fixed and mobile access networks
Best user experience - traffic routing decisions based on access network availability and application traffic type requirements (e.g. Traffic splitting with fibre as primary, NR as overflow, Traffic steering with 4K HDTV over fibre, other traffic over NR)
Consistent delivery of Value Added Services, charging, traffic policies etc. when combining, splitting or steering traffic across the two access networks
Control plane
Data plane
NOTE 1: how the Gateway in this use case is connected to the NextGen Core, authenticated etc. is described in Use Cases 1 and 2. This use case does not include the option of using a third party wireline AN , which is use case 4b.
NOTE 2: from the perspective of the NG UE, the Gateway is the access node rather than a node in the wireline AN.
NextGen Core
NG UE
Wireline AN
(e.g. fibre)
Cellular Radio AN
(e.g. NR)
AND
AND
Gateway
NOTE 1, 2
e.g. WiFi
e.g. NR
Traffic combining, splitting and steering
Traffic combining, splitting and steering
NG UE subscriber identity and credentials, and mobility & session management stack
Local WiFi Auth credentials
(Optional)

## Slide 9: Use Case 4b: NG UE connects to independent WLAN and cellular radio fixed access networks (untrusted) simultaneously
Description
This use case covers all the properties and features of use case 3b, with the additional capability that
NG UE is able to obtain Mobile Broadband services simultaneously via cellular radio (e.g. NR radio) and an untrusted wireline (e.g. fibre) network.
To optimize user experience as well as access network utilization, the NextGen Core and NG UE both natively support dynamic traffic combining, splitting & steering in the DL and UL direction respectively over multiple ANs, on a per-service flow and/or per-traffic type basis according to a set of policies defined by the NextGen Core operator to meet the needs of different traffic types or services
User experience should be seamless when moving between access networks
Service scenarios / features
Same as in use case 4a, but subject to the level of QoS supported by the untrusted AN, which may impact the NextGen core operator’s AN selection policies.
Control plane
Data plane
NOTE 1: how the Gateway in this use case is connected, authenticated etc. is outside of the scope of this use case since it is performed by a third party which does not own the NextGen Core.
NOTE 2: from the perspective of the NG UE, the Gateway is the access node rather than a node in the wireline AN.
NextGen Core
NG UE
Wireline AN
(e.g. third party fibre)
Cellular Radio AN
(e.g. NR)
AND
AND
Gateway
NOTE 1, 2
e.g. WiFi
e.g. NR
Traffic, combining, splitting and steering
Traffic combining, splitting and steering
Core
Local WiFi Auth credentials
NG UE subscriber identity and credentials, and mobility & session management stack

## Slide 10: Use Case 5a: NG UE connects to WLAN or cellular radio access that uses the wireline access network as backhaul (trusted and managed)
Description
Service scenarios / features
Control plane
Data plane
This use case covers all the properties and features of use case 3a, with the additional capability that:-
  The wireline AN act as backhaul to the cellular radio AN that is typically based on radio solution (e.g. small cell) to provide in-building or hotspot cellular coverage
  The wireline AN needs to be able to provide bandwidth management and traffic policing across the two access types (i.e. fixed AN and cellular AN) according to operator policies
Note: This use case can be used concurrently with use case 3a if there is an outage to the small cell cellular radio AN or its backhaul (wireline AN), i.e. NG UE can use the macro coverage provided by cellular radio AN of use case 3a
NOTE 1: how the Gateway in this use case is connected to the NextGen Core, authenticated etc. is described in Use Cases 1 and 2. This use case does not include the option of using a third party wireline AN , which is use case 5b.
NOTE 2: The cellular radio AN uses the Gateway and wireline AN as backhaul.
Ability to use wireline or cellular radio access network seamlessly to the end user to deliver the best and most cost-effective customer experience, including use of small and femtocell in-building coverage solutions connected to the core network via a trusted and managed wireline access network.
Ability to switch over all traffic to an alternative access network when network conditions can’t meet service requirements, however, in case of a single physical connection towards the NG Core there is no additional overall reliability
Consistent delivery of Value Added Services, charging, traffic policies etc., regardless of used access network
NG UE
Wireline AN
(e.g. fibre)
OR
OR
Gateway
NOTE 1
e.g. WiFi
Cellular Radio AN
(e.g. NR)
NG UE subscriber identity and credentials, and mobility & session management stack
Local WiFi Auth credentials
(Optional)
NextGen Core
e.g. NR
NOTE 2

## Slide 11: Use Case 5b: NG UE connects to WLAN or cellular radio that uses the wireline access network as backhaul (untrusted)
Description
Service scenarios / features
Control plane
Data plane
This use case covers all the properties and features of use case 3b, with the additional capability that:-
The 3rd party wireline AN act as backhaul to the cellular radio AN that is typically based on radio solution (e.g. small cell) providing in-building cellular coverage.
Note : There may be limitations in the level of QoS, bandwidth management and traffic policing that can be provided over an untrusted wireline access network
Note: This use case can be used concurrently with use case 3b if there is an outage to the small cell cellular radio AN or its backhaul (wireline AN), i.e. NG UE can use the macro coverage provided by cellular radio AN of use case 3b
Same as in use case 5a, but subject to the level of QoS supported by the untrusted AN, which may impact the NextGen core operator’s AN selection policies.
NOTE 1: how the Gateway in this use case is connected, authenticated etc. is outside of the scope of this use case since it is performed by a third party which does not own the NextGen Core.
NOTE 2: The cellular radio AN uses the third party Gateway and wireline AN as backhaul.
NextGen Core
NG UE
Wireline AN
(e.g. third party fibre)
OR
OR
Gateway
NOTE 1
e.g. WiFi
Cellular Radio AN
(e.g. NR)
Core
Local WiFi Auth credentials
NG UE subscriber identity and credentials, and mobility & session management stack
e.g. NR
NOTE 2

## Slide 12: Use Case 6a: NG UE connects to WLAN and cellular radio access that uses the wireline access network as backhaul (trusted and managed) simultaneously
Description
Service scenarios / features
Control plane
Data plane
This use case covers all the properties and features of use case 4a, with the additional capability that:-
  The wireline AN act as backhaul to the cellular radio AN that is typically based on radio solution (e.g. small cell) to provide in-building cellular coverage
  the wireline AN needs to be able to provide bandwidth management and traffic policing across the two access types (i.e. fixed AN and cellular AN) according to operator policies
Note: This use case can be used concurrently with use case 4a if there is an outage to the small cell cellular radio AN or its backhaul (wireline AN), i.e. NG UE can use the macro coverage provided by cellular radio AN of use case 4a
Ability to cost-effectively deliver higher data speeds and/or an improved quality of experience to mobile broadband customers via simultaneous use of fixed and mobile access networks, including use of small and femtocell in-building coverage solutions connected to the core network via a wireline access network owned by the same operator.
Best user experience - traffic routing decisions based on access network availability and application traffic type requirements (e.g. Traffic splitting with fibre as primary, NR as overflow, Traffic steering with 4K HDTV over fibre, other traffic over NR)
Best user experience - at radio edge, when the combined fixed radio or cellular radio separately offer less bandwidth that the wireline access could support
Consistent Value Added Services, charging, traffic policies etc. when combining, splitting or steering traffic across the two access networks
NOTE 1: how the Gateway in this use case is connected to the NextGen Core, authenticated etc. is described in Use Cases 1 and 2. This use case does not include the option of using a third party wireline AN , which is use case 6b.
NOTE 2: The cellular radio AN uses the Gateway and wireline AN as backhaul.
NextGen Core
NG UE
Wireline AN
(e.g. fibre)
AND
AND
Gateway
NOTE 1
e.g. WiFi
Cellular Radio AN
(e.g. NR)
Traffic combining, splitting and steering
Traffic combining, splitting and steering
NG UE subscriber identity and credentials, and mobility & session management stack
Local WiFi Auth credentials
(Optional)
e.g. NR
NOTE 2

## Slide 13: Use Case 6b: NG UE connects to WLAN and cellular radio access that uses the wireline access network as backhaul (untrusted) simultaneously
Description
Service scenarios / features
Control plane
Data plane
This use case covers all the properties and features of use case 4b, with the additional capability that:-
  The wireline AN act as backhaul to the cellular radio AN that is typically based on radio solution (e.g. small cell) to provide in-building cellular coverage
  the wireline AN needs to be able to provide bandwidth management and traffic policing across the two access types (i.e. fixed AN and cellular AN) according to operator policies
  Note : There may be limitations in the level of QoS, bandwidth management and traffic policing that can be provided over an untrusted wireline access network
  Note: This use case can be used concurrently with use case 4b if there is an outage to the small cell cellular radio AN or its backhaul (wireline AN), i.e. NG UE can use the macro coverage provided by cellular radio AN of use case 4b
Same as in use case 6a, but subject to the level of QoS supported by the untrusted AN, which may impact the NextGen core operator’s AN selection policies.
NOTE 1: how the Gateway in this use case is connected, authenticated etc. is outside of the scope of this use case since it is performed by a third party which does not own the NextGen Core.
NOTE 2: The cellular radio AN uses the third party Gateway and wireline AN as backhaul.
NextGen Core
NG UE
Wireline AN
(e.g. fibre)
AND
AND
Gateway
NOTE 1
e.g. WiFi
Cellular Radio AN
(e.g. NR)
Traffic combining, splitting and steering
Traffic combining, splitting and steering
Core
Local WiFi Auth credentials
NG UE subscriber identity and credentials, and mobility & session management stack
e.g. NR
NOTE 2

## Slide 14: Summary of Use Cases, “Trusted and managed” and “Untrusted” deployment models
 | Trusted | Untrusted
AN managed by the NextGen operator | In scope – “Trusted and managed” Use case 1, 2, 3a, 4a, 5a & 6a | In scope – “Untrusted” Use case 3b, 4b, 5b & 6b
AN not managed by the NextGen operator | Out of scope & not considered | 
Network Implementation
AN/CN Relationship

## Slide 15: Summary of Use Cases and architectural requirements
 | 1 | 2 | 3a | 3b | 4a | 4b | 5a | 5b | 6a | 6b
A single, multi-access capable NG UE can obtain NG services via either cellular radio (e.g. NR radio) or wireline (e.g. fibre) access networks where both ANs are trusted and managed by the NextGen Core operator | x |  | x |  |  |  | x |  |  | 
A single, multi-access capable NG UE can obtains NG services simultaneously via cellular radio (e.g. NR radio) and wireline (e.g. fibre) access network where both ANs are trusted and managed by the NextGen Core operator |  | x |  |  | x |  |  |  | x | 
A single, multi-access capable NG UE can obtain NG services via cellular radio (e.g. NR radio) or wireline (e.g. fibre) access network owned and managed by an untrusted third party operator from a single NextGen Core. |  |  |  | x |  |  |  | x |  | 
A single, multi-access capable NG UE can obtain NG services simultaneously via cellular radio (e.g. NR radio) and wireline (e.g. fibre) access network owned and managed by an untrusted third party operator from a single NextGen Core. |  |  |  |  |  | x |  |  |  | x
The set of services available to the NG UE will be the same over wireline and cellular radio access | x |  | x | x |  |  | x | x |  | 
There may be limitations in the level of QoS that can be provided over an untrusted wireline access network |  |  |  | x |  | x |  | x |  | x
NG UE Authentication / authorization to use a particular access network type (wireline or cellular radio) via trusted and managed access network is granted to the NG UE by the NextGen Core, using the same credentials | x | x | x |  | x |  | x |  | x | 
NG UE Authentication and authorisation to access NG network services via a third party network needs to be performed by the Next Gen core and use the same credentials used for the Radio AN. |  |  |  | x |  | x |  | x |  | x
WiFi authentication MAY be performed locally by the Residential Gateway in the Wireline AN OR by the NextGen Core |  |  | x |  | x |  | x |  | x | 
The NG UE needs to select the right access network to attach to before communication starts - based on operator policies, network conditions and service requirements | x |  | x | x |  |  | x | x |  | 
The NG UE may also decide to change access networks during a session if network conditions can’t meet traffic requirements or if the UE reaches end of coverage for the current AN – user experience should be seamless when moving between access networks. | x |  | x | x |  |  | x | x |  | 
User experience should be seamless when moving between access networks |  |  |  |  | x | x |  |  | x | x
To optimize user experience as well as access network utilization, the NextGen Core and NG UE should both support dynamic traffic splitting over multiple ANs, on a per-flow and/or per-packet basis, following a set of policies defined by the operator to meet the needs of different traffic types. |  | x |  |  | x | x |  |  | x | x
When the wireline AN is acting as both fixed access as well as backhaul to the cellular radio, it needs to be able to perform bandwidth management and traffic policing across the two access types (i.e. fixed and cellular) according to operator policies |  |  |  |  |  |  | x | x | x | x