## Slide 1: Release 18 Key focus areas Lenovo, Motorola Mobility
SA Release 18 Workshop
SP-210609

## Slide 2: Lenovo’s Key Focus Areas for Release 18
System enhancements to improve existing features
  Enhancements to multi-access communication (ATSSS)
  Edge computing improvements
  Enhancements to network analytics
  Improve integration with verticals
  Enhancements to network slicing
  UPF enhancements for control and SBA
  UE policy enhancements
System enhancements to support additional features
  Enhancements to support XR and media services

## Slide 3: Multi-Access Communication (ATSSS)
The ATSSS feature was introduced in Rel-16 & enhanced in Rel-17.
Enables policy-based multi-access communication between UE and UPF using one 3GPP access path and one non-3GPP access path.
ATSSS has attracted the interest of several industry sectors and new use cases have emerged.
We believe that in Rel-18 it is important to:
  Streamline the ATSSS solution to support streering of non-TCP traffic based on well-known and widely deployed IETF protocols with readily available implementations, e.g., QUIC and/or DCCP.
  Enable new use cases, which require two Non-3GPP access paths (e.g. NWu+NWt), or two 3GPP access paths (NTN NR+TN NR), or three access paths.
  Support ATSSS for traffic to Local Area Data Networks (LADNs)
  Support ATSSS when the user plane contains a Branching Point (BP) or UL Classifier (ULCL)

## Slide 4: Edge Computing
Enhance network exposure to include RAN related information to Edge Application Server
  Additional network exposure information can be used by the Edge Application Server to adapt edge application service according to current RAN status
Improve the EAS server selection by leveraging network analytics
  Identify how network analytics (i.e. DN performance analytics from NWDAF) can be leveraged to support the 5GC selecting an optimal EAS server for a UE.
Supporting consecutive traffic steering in different N6-LAN (R17 leftover)
Enhance the PSA-UPF and EAS (re)location for the following scenarios:
  Scenario 1: A collection of UE(s) that use the same application service (i.e. multi-use gaming) but are not part of pre-defined group (existing SID discussion)
  Scenario 2: Consider enhancements to support diversified EAS deployment for different UE(s) and/or different application(s), e.g. according to UE subscription/SLA agreements

## Slide 5: Network Analytics
Currently each NF decides an action based on network analytics. It has not been studied how actions from each NF can be coordinated.
  Goal: Achieve a fully coordinated 5GC network where there are no conflicting actions between NF(s)
Enhanced support for ML enabled analytics (e.g. federated learning, transfer learning, model sharing)
  Supports data privacy in case data are collected from isolated networks (e.g. different PLMNs)
  Reduces signalling required for data collection for model training
  Improves confidence of analytics
Interaction/Coordination between NWDAF and MDAS/MDAF and enablement layer for better analytics generation
  Potential coordination between SA2/SA5/SA6
  New analytic(s) output at the enablement layer for supporting the application specific layer to receive useful stats/predictions/prescriptions for the application service
Leverage analytics to support network automation
Analytics at the enablement layer

## Slide 6: Support of verticals
Deterministic networks
  Enhance architecture to support IEEE TSN distributed networks
    e.g. supporting IEEE related protocols for QoS reservation
  Support integration with additional deterministic networks (e.g. IETF DetNet)
  Support for device-to-device based time sensitive communication (RAN dependency)
  Coordination with 5G-ACIA to support additional features from IoT verticals (5G-ACIA has provided first set of requirements in S2-2105229).
    Enhanced exposure functionality to support group management of industrial devices, exposure of connectivity information
NPN
  Support new service (SA1) requirement:
    5G Networks Providing Access to Localized Services. (Lenovo supports the SID proposed in SA2 in S2-2106802)
  Key focus areas for SA2:
    Support of non-3GPP access for SNPN (included in S2-2106802);
    Study what enhancements are needed to enable (S)NPN to support:
      5G Proximity Services;
      5G System Enhancements for Edge Computing.

## Slide 7: Network Slicing
Support new service (SA1) requirement:
  In roaming, providing the UE with prioritization information of the VPLMNs which may offer a network slice required by the UE;
SA2 internal requirements:
  Providing priority information for the S-NSSAIs subscribed/used by a UE;
  Enable a UE to initiate a registration for a rejected S-NSSAI due to non-support in a first TA of the RA but may be available in another TA of the RA
  Minimize the impact on applications when a currently used slice cannot be any longer offered (due to mobility or slice switching).
  Enable seamless switch between Independent (i.e. Disjoint) Network Slices where strict slice isolation is required (SA3 dependency)

## Slide 8: Enhancements to Wireline and Non-3GPP access
Many capabilities are still missing
New BBF requirements, e.g. scenarios with multiple RGs (see S2-2105345)
The selection of a non-3GPP access node does not take slice information into account (in Rel-17 a non-3GPP access node can support only specific slices – see the N3SLICE WID)
The N3IWF/TNGF/W5GAN selection should be extended to consider slice information
Intra-TNGF and inter-TNGF mobility is still not supported so deployments with multiple TNGFs are not efficiently supported
Multiple simultaneous registrations via non-3GPP access are not supported, e.g. multiple registrations via different N3IWFs supported different slices, or registations using Nwu and NWt
MPS support when the access to the EPC/5GC is non-3GPP access

## Slide 9: Support for XR and media services
Network exposure enhancements
  Identify further enhancements in network exposure information to support XR and media applications
QoS enhancement
  Layered QoS for different frame types (i.e. I/P frame) or importance of different packets within one frame
  Coordination with QoS flow based QoS scheme

## Slide 10: UE Policy Enhancements
Investigate URSP rule enhancements to support GSMA requirement on standardized and operator specific traffic categories
Investigate enhancements to allow a UE to have consistent traffic routing policies across 5GC and EPC
Enhancements for URSP rules provisioning when the UE is roaming (involving the V-PCF)
Investigate how the URSP rules can be extended so that the UE can apply the URSP rules only for the traffic of the intended applications, e.g. avoid applying URSP rules for malicious apps that present fake app-id (SA3 dependency)

## Slide 11: Additional topics
Additional network exposure enhancements
  Potential exposure enhancements for verticals to manage/configure telco communication services (SA5)
  Exposure enhancements to support a 3rd party to indicate in a 5G network a routing policy for steering traffic to an N6-LAN networks
D2D enhancements
  Proximity Services
    Support of service continuity when switching between indirect/direct paths
    Support of Inter-gNB mobility for UE-to-Network Relay.
UPF enhancement for control and SBA
  support better integration of UPF into the 5GC SBA
    Study UPF services registration/deregistration, and discovery with NRF
    Study UPF event exposure service (s) to SMF services, PCF services, NWDAF services, CHF services, NEF services, Trusted AF services
    Study and evaluate usage of event exposure service(s) and potential architectural impacts