## Slide 1: 3GPP SA Proposal c Exploring Disaggregation for 5G Advanced Source: IIT Bombay India Cosignees: IIT Madras India, CEWiT India, Tejas Networks, Saankhya Labs, IIT Kanpur India
SP-210623

## Slide 2
Further possibilities of Disaggregation??
Disaggregation
Disaggregation brings many advantages such as Modularity, Enabling multi-vendor ecosystem …
DU
DU
CU
RU
RU
RU
RU

## Slide 3: Disaggregation in Control Plane
3GPP Network has separate Control Plane and User Plane Functions
User Plane Primarily Responsible for Transfer of Data
Control Plane Functions in 5G performs two types of control tasks
  #1 – Control/Manage User Plane (Network) Functions – Can be Categorized as “Network Control”
    RAN Control Plane (Part of gNB-CU-CP)
      Controls gNB-DU (F1AP) and gNB-CU-UP (E1AP)
      Session Management
      Resource Management: Radio Bearer Control, Admission Control
      QoS Flow management and Mapping to Data Radio Bearers
    CN Control Plane (AMF/SMF/PCF…)
      SMF Controls UPF through PFCP Protocol
      AMF+SMF Controls RAN (gNB) via NGAP protocol
      Hierarchical Control Structure
  #2 - Perform UE Control & State Mgmt, Exchange Signalling Messages with UE - Can be Categorized as “UE Control”
    RAN Control Plane (Part of gNB-CU-CP)
      Exchanges Signalling (RRC) Messages with UEs
      Maintains UE’s Radio Connection State (RRC States)
      Measurement Control & Mobility Control (Though part of Mobility Control deals with Network Control - Session Management)
      …
    CN Control Plane (AMF/SMF/AUSF…)
      Exchanges Signalling (NAS) Messages with UEs
      Maintains UE’s State (MM/SM states)
      Authenticates UE
      …

## Slide 4
gNB-CU Control Plane
Disaggregation in RAN Control Plane - Example
Should We Separate UE Control and Network Control (User Plane Control) functionalities?
  UE RRC Control
    Exchanges Signaling (RRC) Messages with UEs
    Maintains UE’s Radio Connection State (RRC States)
    Measurement Control & Mobility Control
    We can call the function “gNB CU UE RRC”
  Access Network Control (gNB Bearer & Session Control)
    Controls gNB-DU (F1AP) and gNB-CU-UP (E1AP)
    Session Management, Radio Bearer Control
    QoS Flow management
    …
    We can call it gNB CU BSC (gNB CU Bearer & Session Control)
Advantages
  Simplified Network Architecture
    Enhanced Modularity
    Simpler Protocols – e.g., Simpler F1-C’, F1AP need not carry RRC messages
  Easy to support Use case specific variants of UE signalling (RRC) Protocols and associated state machines
  UE Signalling can be treated as data
    Flexibility in Placement of “gNB CU UE RRC” Function
  Improved Load Management in Control Plane
gNB-CU
Control Plane
gNB-CU
User Plane
gNB-DU
gNB-DU
gNB
F1-C
Carries UE specific RRC messages also
F1-U
E1
gNB CU BSC
gNB-CU
User Plane
gNB-DU
gNB-DU
gNB
New Interface
(Carries UE specific RRC messages)
(can be similar to F1-U)
F1-U
E1
gNB CU UE RRC
F1-C’
(Modified F1-C)
New Interface
Existing
Disaggregated RAN Control
gNB CU UE RRC can be taken out of gNB-CU-CP and placed in the data plane also

## Slide 5
Disaggregation in RAN Control Plane
gNB-CU Control Plane
gNB CU BSC
gNB-CU
User Plane
gNB-DU
gNB-DU
gNB
New Interface
(Carries UE specific RRC messages)
(can be similar to F1-U or N3)
F1-U
E1
gNB CU UE RRC
F1-C’
(Modified F1-C)
New (Standardized) Interface
RRC Carrier Path - Option 2
RRC Carrier Path - Option 1
F1-U’
N3’
Flexible Placement of Functions

## Slide 6
Disaggregation in Control Plane
gNB-CU Control Plane
gNB CU BSC
gNB-CU
User Plane
gNB-DU
gNB-DU
gNB
F1-U
E1
gNB CU UE RRC
(eMBB Use Case)
F1-C’
(Modified F1-C)
New (Standardized) Interface
Use case specific Deployment of UE Control
gNB CU UE RRC
(URLLC Use Case)

## Slide 7
Disaggregation in CN Control Plane - Example
Can this approach be followed for Core Network?
  Separate UE Control from Network Control in Core?
    In a way it is already done in the existing 5G System - Partially though
      AMF, AUSF ... - Primarily UE Control
      SMF, PCF … - Primarily Network (User Plane) Control
    Can be clearly defined
  UE CN Control (AMF’+AUSF+SMF’…)
    Exchanges Signalling (NAS) Messages with UEs
    Authenticates UE
    Maintains UE’s State (MM/SM states)
    Can be divided into multiple smaller modular Functions
  CN Network Control Plane (SMF’’+AMF’’+ PCF+…)
    Controls User Plane Functions – SMF’’ Controls UPF through PFCP Protocol
    Controls RAN (gNB) - AMF’’+SMF’’ via Modified NGAP’ protocol
    Can be divided into multiple smaller modular Network Functions

## Slide 8
Disaggregation in RAN + CN Control Plane
gNB-CU-CP
gNB CU BSC
gNB-CU
User Plane
gNB-DU
gNB-DU
gNB
F1-U
E1
gNB CU UE RRC
F1-C’
(Modified F1-C)
New Interface
(Can be
Service based)
CN Network Control
UPF
Data Network
N4 (PFCP)
NG-C’
(Modified NG-C Interface)
UE CN Control
New Interface
(Can be
Service based)
Core
RAN
F1-U’
New Interface
N3
AMF””
SMF””
PCF
…
AMF”
SMF”
AUSF
…

## Slide 9
Disaggregation in RAN + CN Control Plane - Simpler Service Based Architecture
gNB-CU-CP
gNB CU BSC
gNB-CU
User Plane
gNB-DU
gNB-DU
gNB
F1-U
E1
UE (RRC + CN) Control
F1-C’
(Modified F1-C)
New Interface
(Can be service based interface)
CN NW Control
UPF
Data Network
N4-PFCP
NG-C’
N6

## Slide 10
Advantages of the Proposal
Decoupled UE Control and Network Control Functions
Modular Architecture
Simpler Protocols
Easy to Deploy Use Case Specific Variants of UE Control Function and UE Signalling Protocols (RRC/NAS) Protocols
Flexible Function Placements
  UE control can flexibly be placed, either in access or in core or beyond Core (in DN)
UE Signalling exchange also treated as data by the Mobile Network
UE Control Placed in Data Plane as a Service Function
  Providing Service to UEs
Improved Load Management in Control Plane

## Slide 11: Thanks