## Slide 1: 3GPP SA Proposal c Interworking of Non-3GPP Broadcast Networks with 3GPP 5G System Source: Saankhya Labs Cosignees: One Media, Ligado Networks, Fraunhofer IIS, CEWiT, Tejas Networks, IIT Bombay, IIT Kanpur, IIT Madras, IIT Hyderabad, IIT Kharagpur

## Slide 2
Motivation
Increased Video Traffic in Cellular Networks
  Congestion in Cellular Networks
Non-3GPP Digital Terrestrial Broadcasting Technologies and Non-3GPP Satellite Broadcasting Technologies, which may be introduced to 3GPP/NTN for standardization
  Support for Multi Frequency as well as Single Frequency Network
  Large Coverage Area Support (Example - Rural)
  High Spectral Efficiency - Higher Mod-Cod support like 1K-QAM (ATSC3)
  Improved Mobility Support
Convergence of Cellular and Non-3GPP Digital Terrestrial Broadcast Network (DTT)/Non-3GPP Satellite Broadcasting Technologies
  To utilize Non-3GPP DTT for Video Traffic (Multicast/Broadcast Delivery)
    Improves Resource Utilization across non-3GPP DTT and 3GPP 5G NG-RAN
  Reduces Load on Cellular Network
  Interfacing to Legacy and New Broadcasting Networks opens business opportunities in conjunction with 5GS
    ATSC3 Deployed in USA, Korea & DVB-T2 is deployed in 144 countries

## Slide 3
Convergence Support in 5G System
Converged Core in 3GPP 5G System
  Support for both 3GPP and Non-3GPP Access Networks with a common AN-CN Interface
    Allows Interworking with Non-3GPP Access (Trusted/Untrusted WLAN, Wireline)
  Support for Multicast/Broadcast Services Enabled (TS 23.247)
Interworking of Non-3GPP DTT/Satellite Broadcasting Technologies with 5G Core
  As another type of Non-3GPP Access Network supporting Multicast/Broadcast Services
  Aligned with 5G System Architectural Principles

## Slide 4: Backup

## Slide 5: System Architecture (Non-3GPP MB Network Integrated with 5G Core)
Multicast Broadcast System
(MBS)
UE
3GPP 5G Network
Non 3GPP Multicast/Broadcast Network
Content Provider
(AF)
3GPP Unicast or Multicast/Broadcast Flow
Non-3GPP Multicast/Broadcast Flow

## Slide 6: System Architecture - (Contd.)
UE
N3GPP Broadcast-NW (DTT/NTN)
NG-RAN
AMF
UPF
SMF
MB-UPF
MB-SMF
Non-3GPP Broadcast-IWF
MB-STF
AF/AS
PCF
NEF
MBSF
N2
N3
N4
N11
N11
N15
N7mb
N16mb
N19mb
N4mb
N33
N30
Nmb1
Nmb9
Nmb2
Nmb8/
X-MB-U/MB2-U
Nmb5
N6mb
N3mb
N3mb
N2
Nmb10
X-MB-C/MB2-C
Nmb13
MBS

## Slide 7
System Architecture – Salient Points
5G System
  Availability of Multicast/Broadcast Service Delivery Framework (23.247)
  Converged Core Network - Supports both 3GPP and Non-3GPP Access through a common AN-CN Interface
Easy to Integrate Non-3GPP Multicast/Broadcast NW as N3GPP Access with 5G Core
  With the Multicast/Broadcast Framework in 5G Core
    Limited Changes Expected in Existing Interfaces (N2/N3)
  No Impact on AF+MBSF+MBSTF
  Aligned with 5G System Architectural Principles
Unified MB Session Management across 3GPP NG-RAN and non-3GPP DTT/Satellite Network
  5G Core to manage data Flow through both Non-3GPP DTT/Satellite Network and 5G NG-RAN
  Use Non-3GPP DTT/Satellite Network for Multicast/Broadcast Transmission
  Easy to Switch between Non-3GPP DTT/Satellite Network and 3GPP 5G NG-RAN (Unicast)
    Reuse the Inbuilt Unicast – Multicast Switching Mechanism of 5G Core
  Improved Resource Utilization across non-3GPP DTT/Satellite Network and 3GPP 5G NG-RAN
  Synchronization across the two access networks in case of User Mobility

## Slide 8: Thanks