## Slide 1: Passive IoT
Shanghai Quanray Electronics
Notes: 1

## Slide 2: Quanray: Connecting Things Secure
文档翻译
文档翻译
Shanghai Quanray Electronic Technology Co., Ltd. — a leading one-stop RFID hardware solution provider. The company is committed to the research and development of innovative IoT products. The passive wireless sensor products transmit object information using 4G/5G network to the cloud, make the global awareness of the objects possible to interested parties.
Identity
Temperature
4G
5G
Identify
Identity
Pressure
Identity
Identity
Position
Everything in the Cloud

## Slide 3
Why we are here?
Problem of existing RFID technology
Short read distance (up to 15m)
Complex and high cost of read coverage because of reader to reader interference
Unguaranteed QoS because of unregulated radio band
Very low level of security because of simple protocol
Difficult to extend to for smart sensor application because the current protocol is based on dumb memory access
Expecting 5G Passive IoT
As far as we know, 3GPP is discussing to support passive technology called passive IoT. We expect it can solve the problem of RFID technology. So we propose to study Passive IoT in 3GPP as soon as possible.

## Slide 4
Proposed Features of Passive IoT
Reliable communication range: up to 100 ~ 200m
Backscatter communication for low cost low power user terminal
Low power consumption: powered by energy harvesting with reasonable footprint, extreme low power consumption for wake-up
Massive user terminal: tens of thousands simultaneously
Low cost: ~1/10 of NB-IoT
Frequency: compatible to both regulated band and ISM band

## Slide 5
Scenario of Passive IoT
In electricity power grid, battery is dangerous as it may explode
For construction health management, battery replacement cost is high
Loading
Transport
Outbound
Choosing
Inbound
Receiving
Inventory
Location Management
Picking
Transfer warehouse
Replenish
In a distribution center, 100% coverage is very difficult
In animal farming, identification, sensing, locating, etc. in large area is essential

## Slide 6
Thanks!