## Slide 1: Requirements to perception for automotive industry-Passive IoT
BMW Brilliance Automotive
3GPP TSG SA Rel-18 workshop
Electronic Meeting, Sep 09 - Sep 10, 2021

## Slide 2
Passive IoT enabled Perception--Motivation
We have considered RFID technology, but RFID is not good.
Bad performance: Based on our test, RFID can only read labels in case the labels are not blocked. On the other words, in case the label attached on the bin is blocked, e.g. by another metal bin, RFID always fail to read it.
High Cost: The transmission distance for RFID readers is short, about 8 meters based on test. We need to deploy a lot of RFID readers to cover the whole warehouse(about 5000m2) and the network cost is very high.
Bin management at the Gate of the warehouse
Scenario: unique identify the bins for logistic management. E.g.
Identify which bins move in or out of the warehouse, at the Gate of the warehouse.
Identify the bins in a specific area inside the warehouse.
Currently, bins are manually managed via scanning the barcode attached on each bin.
Causes：
High OPEX: OPEX of warehouse management is very high for us;
Manual error: Manual work often cause errors and many bins lost;
We are considering Automatic bin Management in the warehouse with a quite low cost.
Use cases and Motivation
Bin management inside the warehouse

## Slide 3
Passive IoT enabled Perception--Requirement
Coverage capability: communication distance should be enhanced to 30 meters to construct a feasible network coverage in the 5000 m2 warehouse.
UE power consumption: <0.1mW to support working without battery.
UE cost: <0.1￥(~0.02$) to meet cost-sensitive applications.
Positioning accuracy： 3~5m(Horizontal&Vertical) @ 90% for positioning .
There is no battery in the terminal and the terminal accumulate the energy from radio signaling. Additionally, the terminal may also accumulate energy from solar energy as supplement.
Requirement to support Passive IoT
What is Passive IoT
From BMW Brilliance Automotive perspective, we hope we can take use of Passive IoT as soon as possible (around 2024~2025) and hope 3GPP can study Passive IoT soon.
Urgency for Passive IoT

## Slide 4
Thank You

## Slide 5
Annex:
Introduction of a New 3GPP member: BMW Brilliance Automotive (BBA)
  Founded in May 2003, BMW Brilliance Automotive Ltd. (BBA) is a joint venture between the BMW Group and Brilliance China Automotive Holdings Ltd. Business operations of BBA include production, sales and after-sales services of BMW automobiles in China. BBA has a state-of-the-art production base in Shenyang, a branch company in Beijing and an extensive national sales and service network. The joint venture employees around 20,000 people and has a network of nearly 400 local suppliers.
  BMW Brilliance’s production base in Shenyang is the BMW Group’s largest production base worldwide. It currently manufactures six BMW models: BMW 5 Series (long wheelbase), BMW 3 Series (long wheelbase and standard wheelbase), BMW X3, BMW X2, BMW X1 (long wheelbase) and BMW 1 Series Sedan.
  BBA’s production system applies innovative technologies, sustainable production and the latest Industry 4.0 manufacturing technologies, and it continues to promote these initiatives with its partners.
Please find more at: http://www.bmw-brilliance.cn/cn/en/index.html