## Slide 1: SA1 Rel-18 Normative Work -Status update-
SP-210654

## Slide 2: Introduction
This presentation aims to give an outline of the work done in SA1 in the context of Rel-18.
Rel-18 Stage 1 freeze will be done in Dec 2021. As of today, all work items but one have been completed to a minimum of 80%.
The work presented in these slides has been categorized into:
    New Features
    Enhancements
    Verticals +NTN focused

## Slide 3: SA1 Rel-18 Normative work
Evolution of IMS Multimedia Telephony Service
Enhanced Access to and Support of Network Slice
AI/ML Model Transfer in 5GS
5G Timing Resiliency System
Personal IoT and Residential Networks
Ranging Services
Networks Providing Access to Localized Services
Vehicle-Mounted Relays
Tactile and Multi-Modality Communication Services
Subscriber-Aware Northbound API access
Support for Service Function Chaining
Data Integrity in 5GS
Signal Level Enhanced Network Selection
Smart Energy and Infrastructure
FRMCS Evolution
Low Power High Accuracy Positioning for Industrial IoT scenarios
Service Exposure Interfaces for Industry
Sharing Administrative Configuration between Interconnected MCX
Ad Hoc Group Communication in Mission Critical Services
MPS when Access to EPC/5GC is WLAN
5GS with Satellite Backhaul
5GS with Satellite Access to Support Control and/or Video Surveillance
Enhancements (TS 22.261)
New Features (TS 22.261)
Verticals + NTN focused (TS 22.261, TS 22.104, others)

## Slide 4
New Features
AI/ML Model Transfer in 5GS |  |  | 
Rapporteur: | Jia SHEN (OPPO) | Output : | TR 22.874 CRs to TS 22.261 (new clause)
Summary | This work introduces the 5GS to support for AI/ML operations for various applications (e.g. image/speech recognition, media editing/enhancements, robot control, automotive). The work specifies performance requirements (for end-to-end latency, experienced data rate, communication service availability) and service requirements (for AI/ML QoS management, AI/ML model /data distribution/transfer, network performance and resource utilization monitoring/prediction). Different use cases where under study: AI/ML operation splitting between AI/ML endpoints; AI/ML model/data distribution and sharing over 5G system; Distributed/Federated Learning over 5G system. |  | 
5G Timing Resiliency System |  |  | 
Rapporteur: | Betsy Covell (Nokia) | Output : | TR 22.878 CRs to TS 22.261 (new clause)
Summary | The 5G timing resiliency system introduces holdover and frequency stability capabilities enabling the 5G system to receive information from RAN nodes (e.g., GNSS reports) to determine the status of the overall system and influence consistent operation of timing resiliency. With timing resiliency capabilities, the 5G core network can provide a consistent and fault tolerant solution for all or parts of the network. The 5G system can also provide an alternative timing source to verticals currently relying on GNSS timing solutions. |  | 

## Slide 5
New Features
Personal IoT and Residential Networks |  |  | 
Rapporteur: | Adrian Buckley (Vivo) | Output : | TR 22.858 (Resident Study) TR 22.859 (Personal IoT Networks Study) CRs to TS 22.261 (new clause)
Summary | Personal IoT Networks (PINs) and Customer Premises Networks (CPNs) provide both local connectivity and, via a gateway, access to 5G network services. CPNs and PINs have in common that in general they are owned, installed and/or (at least partially) configured by a customer of a public network operator. A Premises Radio Access Station (PRAS) is a base station installed in a CPN to provide in-home 5G coverage. The PRAS provides access to the CPN and/or 5G network services. The PRAS can be configured to use licensed and/or unlicensed frequency bands. A Personal IoT Network (PIN) consists of PIN Elements that communicate using PIN Direct Connection (sidelink) or direct network connection. Examples of PINs include networks of wearables and smart home / smart office equipment. |  | 

## Slide 6
New Features
Ranging Services |  |  | 
Rapporteur: | Xiaowei jiang (Xiaomi) | Output : | TR 22.855 CRs to TS 22.261 (new clause)
Summary | The work specifies the functional and performance requirements for Ranging based services(i.e. applications utilizing angle and direction between UEs). It mainly focuses on commercial use cases, e.g. smart home, smart city, etc. Some example KPIs include distance/angle accuracy, latency, confidence level, availability, ranging interval, effective ranging distance, concurrent ranging operations. |  | 
Networks Providing Access to Localized Services |  |  | 
Rapporteur: | Lola Awoniyi-Oteri (Qualcomm) | Output : | TR 22.844 CRs to TS 22.261 (new clause)
Summary | This work item provides new service (functional) requirements to enhance 5G system support of UEs accessing to a hosting network and local services offered by service providers, the hosting network operator or third parties, at a given time and geographical location. The normative requirements cover UE and hosting network configuration, provisioning, authentication, authorization, discovery, selection and access. They also covers regulatory services and multicast and broadcast services over the hosting network. |  | 

## Slide 7
New Features
Vehicle-Mounted Relays |  |  | 
Rapporteur: | Francesco Pica (Qualcomm) | Output : | TR 22.839 CRs to TS 22.261 (new clause)
Summary | The VMR work introduces service requirements (in TS 22.261) for 5GS support of mobile base station (BS) relays, e.g mounted on moving vehicles, which provide 5G coverage and communication to UEs (inside the vehicle and/or in its vicinity), and are connected wirelessly to the 5G network via RAN nodes. Requirements include support for mobile BS relays configuration & provisioning, UE access control, QoS, charging, Multi-PLMN RAN sharing, mobility, service continuity, multi-link connectivity, roaming, priority/emergency services, security, RAN management. |  | 
Tactile and Multi-modality Communication Services |  |  | 
Rapporteur: | Xiaonan Shi (China Mobile) | Output : | TR 22.847 CRs to TS 22.261 (normative work expected in Nov2021)
Summary | FS_TACMM aiming at identifying new use cases and potential service requirements for 5GS support of tactile and multi-modality communication services. Use cases involve immersive VR, remote control robot, support of skillset sharing for cooperative perception and maneuvering of robots, haptic feedback for a personal exclusion zone in dangerous remote environments, live event selective immersion, support for IEEE P1918.1 architecture and virtual factory. Requirements involves service exposure requirements to enable 5G system support of tactile and multi-modality applications. |  | 

## Slide 8
New Features
Subscriber-Aware Northbound API access |  |  | 
Rapporteur: | Atsushi Minokuchi (NTT Docomo) | Output : | CRs to TS 22.261
Summary | Requirements are specified for a UE (or a UE application) to utilize northbound APIs with appropriate authentication and authorization. This feature could potentially increase the effect of “Enhancements for XR”. |  | 
Support for Service Function Chaining |  |  | 
Rapporteur: | Ellen Liao (Intel) | Output : | CRs to TS 22.261 (clause 6.35)
Summary | This work item enables enhancement of service function chaining for 5G networks beyond the requirements for FMSS in TS 22.101, the network operator defines service function chaining policies for service function chaining to steer the traffic associated to the application and its users on per UE basis to appropriate ordered service functions. The corresponding service support of service function management and charging aspects for 5G network are also specified. |  | 

## Slide 9
New Features
Data Integrity in 5GS |  |  | 
Rapporteur: | Qun Wei (China Unicom) | Output : | CRs to TS 22.261
Summary | Data Integrity adds requirements of data integrity verification service on the 5G system, in order to fulfill the demand such as supply chain finance and insurance, etc., which have strict requirements for services that employ IoT device communication for data integrity. |  | 
Signal Level Enhanced Network Selection |  |  | 
Rapporteur: | Kurt Bischinger (Deutsche Telekom) | Output : | CR to TS 22.011 (clause 3.2.2)
Summary | For certain UEs introducing an Operator controlled signal threshold per access technology on the USIM to enhance the automatic network selection procedures in that way that in case the threshold is set in a first iteration the UE additionally applies the threshold as an additional criterion in each step of the network selection process, and if registration cannot be achieved during the first iteration a second iteration of the process is performed as today, i.e. without applying the Operator controlled signal threshold. |  | 

## Slide 10
Enhancements
Evolution of IMS Multimedia Telephony Service |  |  | 
Rapporteur: | Hu Yue (China Mobile) | Output : | TR 22.873 CRs to TS 22.261
Summary | This work introduces the support for AR telephony communication and support for 3rd parties (e.g. enterprise) to securely demonstrate to the called party that the caller (e.g. employee) is authorized to use or reference specific business information when placing a call. |  | 
Enhanced Access to and Support of Network Slice |  |  | 
Rapporteur: | Ki-Dong Lee (LGE) | Output : | TR 22.835 CRs to TS 22.261
Summary | This work introduces the support for a UE’s access to a network slice when different types of restrictions apply (e.g. related to radio resources, frequency bands), with minimized interruption of services when there is a change of network slices or allocated resources and support for service exposure for 3rd party control/configuration of network slices |  | 

## Slide 11
Verticals + NTN
Smart Energy and Infrastructure |  |  | 
Rapporteur: | Xu Xia (China Telecom) | Output : | TR 22.867 CRs to TS 22.261, 22104
Summary | Smart Grid is a term that refers to enhanced cyber-physical control of electrical grids and to related application. Smart Grid operation can cover power generation, transmission, distribution, and consumption, which may require high communication service availability and communication service reliability, and in some cases a low end-to-end latency with more accurate clock synchronization.The SEI WID introduces the Smart Grid specific service requirements in control, monitoring, availability assurance, service security and isolation for 5G systems. |  | 
FRMCS Evolution |  |  | 
Rapporteur: | Guillaume Gach (UIC) | Output : | TR 22.989
Summary | SA1 has refined existing critical applications related use cases coming from a gap analysis between the newly released set of UIC FRMCS specifications and latest version of TR 22.989 (e.g., Railway emergency communication, Inviting-a-user-to a voice communication), limited to use cases in on-network mode. |  | 

## Slide 12
Verticals + NTN
Low Power High Accuracy Positioning for Industrial IoT scenarios |  |  | 
Rapporteur: | Yuan Wang (Huawei) | Output : | CRs to TS 22.261, TS 22.104
Summary | This work specifies requirements on low power high accuracy positioning service for industrial IoT device. |  | 
Service Exposure Interfaces for Industry |  |  | 
Rapporteur: | Joachim W. Walewski (Siemens) | Output : | CRs to TS 22.261
Summary | This work updates TS 22.261 following the results of the gap analysis done against the updated version of the document “Exposure of 5G Capabilities for Connected Industries and Automation Applications” from 5G Alliance for Connected Industries and Automation (5G-ACIA). |  | 

## Slide 13
Verticals + NTN
Sharing Administrative Configuration between Interconnected MCX |  |  | 
Rapporteur: | Jens Toobe (BDBOS) | Output : | TR 22.881 CRs to TS 22.280
Summary: | Mission Critical Organizations can deploy their own 3GPP standardized mobile, local, countrywide or national broadband mission critical communications systems. In order to grant visiting MCX Service Users access to a Partner MCX Service System and its services, a mechanism is required, which allows the exchange of administrative configuration between connected MCX Service Systems. This work introduces enhancement of architecture and protocols to allow the exchange of administrative information between connected MCX Service systems. |  | 
Ad Hoc Group Communication in Mission Critical Services |  |  | 
Rapporteur: | Erik Guttman (Samsung) | Output : | CRs to TS 22.280
Summary | This work introduce the support for Ad hoc Group communication feature as part of MCX Services and thereby available for MCPTT, MCVideo and MCData. Ad hoc Group communication will be treated as a type of MCX service Group communication and it supports the mechanism of call processing and call termination identical to MCX service Group communication. |  | 
MPS when Access to EPC/5GC is WLAN |  |  | 
Rapporteur: | Ray Singh (Peraton Labs) | Output : | CRs to TS 22.153 (new clause)
Summary | This work introduces support MPS communications when the access to the EPC/5GC is WLAN. Support of MPS when the UE has WLAN access is important during certain disaster scenarios such as when 3GPP access networks (LTE and NR) are not unavailable or degraded. In some cases, WLAN may be the only available access (e.g., inside buildings, hotels, airports, malls and stadiums) and therefore critical for MPS communications. |  | 

## Slide 14
Verticals + NTN
5GS with Satellite Backhaul |  |  | 
Rapporteur: | Hui Xu (CATT) | Output : | CRs to TS 22.261
Summary | This work introduces new requirements on support of multiple wireless backhaul connections (e.g. satellites and/or terrestrial), QoS control considering satellite backhaul characteristics (including dynamically changed latency and/or bandwidth), and differentiation of charging information for traffic over satellite backhaul. The work has been completed in SA1#94E. |  | 
5GS with Satellite Access to Support Control and/or Video Surveillance |  |  | 
Rapporteur: | Dong Chen (Xiaomi) | Output : | CRs to TS 22.261
Summary | Equipment control (includes controlling commands from console to the equipment as well as equipment status data reporting information to the console) and/or video surveillance (picture or video taken by camera installed on the equipment to console) by mobile and stationary UEs are supported with this WI for 5G system with satellite access. Characteristic of the requirement is that UL data rate (3M) is higher than DL data rate (0.5M). |  |