TSG-SA Working Group 1 (Services) meeting #5	TSG S1 (99) 1004

San Diego, USA 29th Nov – 3rd Dec 1999	Agenda Item: 4.3.3

To		R2

# Source: 	S1

# Copy:		S2, SMG2 WPA, CN1

Title: 		Proposed LS to RAN2 on Requirements for Network Selection

S1 received an LS from CN1 (Tdoc N1-99D27) asking for confirmation of S1 requirements for the selection of access systems. S1 has reviewed its requirements in TS 22.101 and has agreed a change request (attached) to the existing requirements to take account of access network type.

CN1 and R2 are requested to take these requirements into consideration when developing procedures for PLMN selection.

| TSG-SA Working Group 1 meeting #6 | TSG S1 | (99)xxx |
| --- | --- | --- |
| San Diego, USA, 29th Nov. – 3rd Dec. 1999 | Agenda: | 4.3.3 |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 22.101 | CR |  | Current Version: | 3.7.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | TSG SA | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM | X | ME | X | UTRAN / Radio | X | Core Network |  |
| (at least one should be marked with an X) |
| Source: | SA1 | Date: | 24th Nov. 99 |
| Subject: | PLMN Selection |
| Work item: |  |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature | X |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  |  | Release 00 |  |
| Reason for change: | To clarify the requirements for PLMN selection in environments with multiple access technologies available |
| Clauses affected: | 18 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

# 18	Network Selection

Three roles may be involved in UMTS network selection: the home environment, the serving network and the user. Services may be available to the user through a choice of several serving networks in a given location, possibly using different types of Radio Access Network, , however it is expected that a user terminal will communicate with one network at a given instant (there may be exceptions such as when an inter-network handover occurs).

All selection schemes make use of information provided by the serving networks, including the network name, the network capabilities and any restrictions. Other information such as terminal capabilities may also be required. This information may change with time but must be accurate and available at the time network selection is being made.

Procedures 1 and 2 below for network selection in UMTS shall be supported by all mobile stations. The user shall be able to choose which procedure to use at any given time.

1. Default Automatic Procedure

A default procedure for network selection shall be defined which selects a network from amongst those available based upon the following criteria in order of importance:

The last network on which the UE was registered;

A list of preferred networks stored on the USIM;

A preferred list of access technologies stored on the USIM;

A list of preferred frequency bands or channels stored on the USIM;

If more than one network using a given technology is available then a random choice from those which provide a defined minimum signal quality should be made.

2. Manual Procedure

The manual procedure consists in presenting to the user the list of all available networks and letting her make the selection. The user shall be able to make use of the manual selection procedure at any time.

3. Home Environment Specific Procedure

Optionally, if provisioned by the MS and selected by the user, the home environment can add the ability to define the behaviour when selecting the required network from those available. A standardised framework for over-the-air transfer of behaviour definition is required. If enabled by the user, it shall be possible for the home environment procedure to instruct the mobile station to search for a network which meets a given set of requirements, indicated by certain parameters or to compile a list of all available networks.

Other procedures may be offered by the MS.

Both automatic and manual network selection schemes are constrained by commercial agreements between the home environments and serving networks. If a roaming agreement does not exist and cannot be established using the procedure for automatic establishment of roaming agreements, then registration on the network will not succeed. Therefore the user must provide sufficient information to allow the serving network to identify the relevant home environment and to allow the home environment to identify the user.

A USIM shall be registered on one and only one serving network at any given time (there may be exceptions such as when preparing for an inter-network handover). Changing the serving network between two calls requires USIM de-registration from the current serving network and USIM re-registration on the newly selected serving network.

If simultaneous access to more than one home environment is required (through a card with multiple USIMs or through several cards in a multi-slot terminal), manual selection shall be invoked.

A procedure for handling network rejections is required, see GSM 02.07 Annex A for an example. During manual selection the user may be allowed to attempt to select any available network (subject to restrictions that may be specified by the home environment). Successful manual network selection shall update the procedure for preventing unnecessary network access attempts. A set of network access rejection causes shall be standardised.

It shall be possible for a network operator to control access to the network. This may be done for example to provide priority to emergency services or to control demand upon the access channel after a network failure, see GSM 02.11 for further details.