3GPP TSG SA S1#6				                            	S1-99 1028

San Diego, November 29- December 3, 1999

To:	3GPP RAN2, RAN3, SA2

Source: 	3GPP SA WG1

Title: 	Liaison statement to on SoLSA support on UTRAN

S1 has started to update the SoLSA stage 1 for 3GPP. However S1 is not fully aware of all the implications of these changes and thus  S1 wishes RAN2/3 and SA2 to study the issue.

S1 has discussed on problems related to soft handover, and definition of LSA area. S1 has noted that there are case where based on used radio network planning and used service, it might be either suitable to allow the active set to include non-LSA cells or to have only the LSA cells included. S1 would like to know if this can be provided as operator option to LSA definition. (See definition chapter at Draft CR)

S1 understanding is that UTRAN SoLSA support can be included at Release '99, if TSG SA agrees to finalise the work on that by March '00.

Attached draft CR to 22.043.

Draft CR. To be reviewed by RAN2.

| TSG-SA Working Group 1 meeting #6 | TSG S1 | (99)935 |
| --- | --- | --- |
| San Diego, 29 Nov – 03 Dec 1999 | Agenda: | 6.0 |

| 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- |
|  | 22.043 | CR |  | Current Version: | 3.0.1 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submision to TSG | SA# | for approval | X | (only one box should |
| list TSG meeting no. here ( | for information |  | be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM | X | ME | X | UTRAN | X | Core Network | X |
| (at least one should be marked with an X) |
| Source: | SMG1/ SA WG1 | Date: |  |
| Subject: | DRAFT Editorial update for GSM/3GPP use. |
| 3G Work item: |  |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature |  |  |  |  |
| shall be marked | C Functional modification of feature | X |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | The transfer of GSM specifications for 3GPP requires an editorial update. Text referring to the GSM system needs to be changed to refer to both the GSM and 3G systems. |
| Clauses affected: | All clauses |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

# 1	Scope

This technical specification, specifies a mechanism, which can be used as a platform for providing special tariffs and/or special set of service features for certain subscribers within a regionally restricted area or areas.

The motivation for this concept is to create means for network operators to build new service and tariff packages, which take into account subscriber groups and their needs.

The localised service area is both an optional network feature and an optional UE feature. Usage and implementation of the different SoLSA service features may vary according to operator's service packages.

This feature is not intended to replace the existing method of cell selection, cell indication and handover.

The standard shall support both GERAN and UTRAN to facilitate SoLSA services.

Note: However certain service features may not be fully supported over UTRAN at rel 99.

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies.

-	A non-specific reference to an ETS shall also be taken to refer to later versions published as an EN with the same number.

-	For this Release 1999 document, references to GSM documents are for Release 1999 versions (version 8.x.y).

## 2.1	Informative references

[1]	TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	GSM 01.04: "Digital cellular telecommunications system (Phase 2+); Abbreviations and acronyms".

# 3	Definitions and abbreviations

3.1	DefinitionsLocalised Service Area (LSA):

A localised service area consists of a cell or a number of cells within a PLMN. Cells being part of different localised service areas may have overlapping coverage areas. The cells constituting a localised service area may not necessarily provide continuous coverage.

Figure 1: Localised Service Area

Subscribed to LSA: Set of LSAs, which the user has subscribed to.

Valid LSA: A LSA, which the user has subscribed to and his UE can receive service.

Current LSA: The LSA where a UE is receiving service. Regarding UTRAN soft handover,  active set of cells must include [TBA].

LSA Priority: Priority of subscriber's LSAs. When the user has several valid LSAs, the current LSA shall be selected by prioritising LSAs in case of overlapping LSAs.

Figure 2: Localised Service Areas

LSA only access: LSA user is allowed to access PLMN within his allowed LSAs. LSA user is not allowed to receive and/or originate a call outside LSA area.

Figure 3: LSA only access

Exclusive Access: Access to  exclusive access cells  is restricted to defined LSA subscribers.

Figure 4: Exclusive Access

Preferential Access:  LSA user shall have preferential access to resources of LSA cells, compared to non-LSA users.

Figure 5: Preferential Access

## 3.3	Abbreviations

For the purposes of the present document, the following abbreviations apply:

LSA	Localised Service Area

Further abbreviations may be found in TR 21.905 [1] and GSM 01.04 [2].

# 4	Description

The localised service area concept shall give the operator the basis to offer subscribers different services (e.g. tariffs or access rights) depending on the location of the subscriber.

## 4.1	Defining subscriber information for localised service area

A subscriber can have up to 20 LSAs per PLMN.

It shall be possible to assign localised service areas to subscribers. Subscriber may have service, which contains several LSAs potentially belonging to different PLMNs. There shall be means to allocate LSA priority to each subscriber independently by operator.

Localised service areas for subscriber(s) may overlap, i.e. one cell may be part of several LSAs belonging to that subscriber.

As an example, within a hierarchical cell structure, cells in different layers can constitute different localised service areas. A localised service area could be defined so that it is possible to establish flexible sized areas, which are applicable to

-	a very small localised service area ("home area" covering one or several cells dedicated e.g. to a residential subscriber or a company); or

-	a large area covering a part of the city (one or several location areas); or

-	a combination of these.

Thus it is possible to use the various radio network configurations.

The definition of location areas and the definition of localised service areas may be independent of each other.

## 4.2	Service Features

Following service features are building blocks for SoLSA based services. It is up to the operator to decide which service features are required for a specific service.

-	Localised service area indication.

-	Localised service area support in idle mode (camping).

-	Localised service area support in handover.

-	LSA only access.

-	Exclusive access.

-	Preferential access.

### 4.2.1	Localised service area indication

It shall be possible to assign a subscriber defined identifier by the operator to each LSA (alphanumeric text up to 10 characters), which can be provided to the user in idle and active mode. As a UE manufacturer option the user may assign an icon or another form of indication to each LSA.

It shall be possible to indicate a change of localised service area during idle and active mode.

The indication is a network option (activated/deactivated by the network).

### 4.2.2	Localised service area support in idle mode (camping)

The PLMN shall determine, which cells, belonging to the LSA, are to be favoured by the UE when camping.

When camping on a cell in idle mode, the subscriber's mobile station shall use the information provided by the PLMN in selecting cells belonging to his localised service area. The mobile station shall have the ability to reselect a cell in a different LSA with higher priority. This favouring shall not degrade the overall service quality.

There should be no extra delay in cell selection procedure.

### 4.2.3	Localised service area support in handover

The PLMN shall determine, which cells, belonging to the LSA, are to be favoured during active mode.

### The cells belonging to users LSAs shall be favoured at call setup and when handovers are carried out. This favouring shall not degrade the overall service quality. 4.2.4	Exclusive access

For a cell belonging to one or more service areas and where only one or more specific subscribers shall have allowed access, other subscriber’s mobile stations shall be prevented from using the cell to obtain any service, other than TS12 (Emergency Calls).

### Handovers into cells belonging to localised service areas where only specific subscribers shall have allowed access, shall be possible to be prevented for other subscribers, if required by a SoLSA application.4.2.5	LSA only access

With access allowed only within one or more localised service areas, it shall be possible to prevent receiving and/or originating activities from non-LSA cells outside LSA.

It shall be possible to prevent handovers to cells not belonging to allowed localised service areas, if required by a SoLSA application.

### 4.2.6	Preferential access

It shall be possible to allocate resources at call setup and during the active mode to LSA users, if required by a SoLSA application.

NOTE: 	An example of a requirement: the last traffic channel is not allocated to non-LSA user or in case of congestion an ongoing call of a non-LSA user is released and replaced with a call of a LSA user.

# 5	Impact on other services

## 5.1	General

SoLSA is not limited to specific services and there are no modifications necessary for existing services. In particular there shall be no impact to Emergency Call (TS12).

LSA should be able to support all tele, bearer and supplementary services .There is no interaction to supplementary services except those specified below.

### 5.3	GPRS

It shall be possible to apply SoLSA services independently to circuit switched services and  to GPRS. LSA support in idle mode shall be specified for GPRS.

The definition of routing areas and the definition of localised service areas shall be independent of each other.

## 5.4	Call Forwarding

No interaction.

NOTE:	Operators should consider using tools such as ODB and CAMEL to control call forwarding functionality provided in conjunction with any SoLSA services.

## 5.5	Completion of Calls to Busy Subscriber (CCBS)

LSA only access restrictions shall apply to CCBS recall.

# 5	Exceptional procedures

None identified.

# 6	Charging aspects

Based on the use of the feature "Support of Localised Service Area" it is possible to establish local tariff applications ("home zone applications").

# 7.	Commercial Role Model for SoLSA

SoLSA shall support LSAs which, do not belong to the Home Environment. To enable this the following commercial role model shall be used:

Figure 6: SoLSA commercial role model

The actors of the SoLSA role model are defined below:

-	Home Environment: The Home Environment of a SoLSA subscriber is the owner of the SIM/USIM for this subscriber. As such, he is responsible for transferring the necessary SoLSA information to the subscriber SIM/USIM. He also holds the SoLSA subscriber information (e.g. in the HLR, CAMEL server, private network node). The Home Environment has a commercial agreement with one or several SoLSA operators. A Home environment can be commercially the same entity as a SoLSA operator.

-	SoLSA operator: An operator is acting as a SoLSA operator for one SoLSA subscriber if he owns at least one Localised Service Area (LSA) for that subscriber. As such, when the user is attached to the SoLSA operator the SoLSA operator will provide the service for the SoLSA. One SoLSA operator can own a multiplicity of LSAs for a given SoLSA subscriber. A SoLSA operator has a commercial agreement with one or a multiplicity of Home operators (but maximum one per subscriber). A SoLSA operator can be commercially the same entity as the Home environment.

-	SoLSA subscriber: A SoLSA subscriber is a subscriber who has subscribed to one Home operator and at least one SoLSA operator (or said differently, who has an authorisation to receive services from at least one LSA). A SoLSA subscriber can have a subscription with a multiplicity of SoLSA operators. A subscriber has always a Home operator, but for example if he is allowed to have services only in LSAs, his Home operator and his SoLSA operator can be commercially the same entity.

-