| TSG-SA Working Group 1 meeting #6 | TSG S1 | (99)1035 |
| --- | --- | --- |
| San Diego, USA, 29th Nov. – 3rd Dec. 1999 | Agenda: | 6.6 |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 22.078 | CR |  | Current Version: | 3.1.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | TSG SA 1 | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio |  | Core Network | X |
| (at least one should be marked with an X) |
| Source: | SIEMENS | Date: | 29th Nov. 99 |
| Subject: | Enhancement of the capabilities of dialled services |
| Work item: | CAMEL Phase 3 |
| Category: | F Correction |  | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature | X |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  |  | Release 00 |  |
| Reason for change: | In order to have a more flexible handling TSG CN WG2 have agreed to enhance the capabilities of dialled services by allowing the CSE to bar the call and to perform charging activities, i.e. to add Free Format Data to the Call Data Record. |
| Clauses affected: | 5.3.2.2, 7.2 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

#### 5.3.2.2	Further processing of the call

When the VPLMN has made contact with the CSE (or reported events to the CSE when contact has already been established), the CSE shall be able to instruct the VPLMN to act as described below by issuing one and only one of the following instructions:

-	allow the call processing to continue unchanged;

-	allow the call processing with modified information. The CSE shall have the possibility to send the information listed in table: A-2 (Call set up request procedure 2) );

- release the call;

- perform charging activities.

Further processing of the call continues as detailed in Sections 5.3 to 5.8, and the CSE contact initiated at this procedure is terminated.

7.2	Further processing of the call

When the serving network has made contact with the CSE, the CSE shall be able to instruct the serving network to act as described below by issuing one and only one of the following instructions:

-	allow the call processing to continue unchanged;

-	allow the call processing with modified information. The CSE shall have the possibility to send the information listed in table: A-2 (Procedures for serving network dialled services 2);

- release the call;

- perform charging activities.

Further processing of the call continues as detailed in Sections 5.3 to 5.8, and the CSE contact initiated at this procedure is terminated.