## Slide 1: Documenting SA1 Requirements for 6G
Source: Apple, MediaTek Inc.
Agenda item: 10
For: Discussion

## Slide 2: On 3GPP working methods (21.900) – Quotes
“Where appropriate, the three-stage methodology defined in ITU T Recommendation I.130 should be employed:
  Stage 1 is an overall service description from the user's standpoint.
  Stage 2 is an overall description of the organization of the network functions to map service requirements into network capabilities.
  Stage 3 is the definition of switching and signalling capabilities needed to support services defined in stage 1.”
“TSG SA is, through SA1, responsible for defining the features and services required in the 3GPP specifications. SA1 is responsible of producing the stage 1 descriptions (requirements) for the relevant features and passing them to SA2. SA1 may also forward their considerations on possible architecture and implementation to SA2, but is not responsible for this part of the work.”
Observation 1: SA1 is not responsible for architecture decisions but can express some considerations on architecture and implementation. Considerations are neither restrictions nor requirements.

## Slide 3: 3GPP System: Definitions from TR 21.905
3GPP system: A telecommunication system conforming to 3GPP specifications, consisting of one or more 3GPP core networks, one or more 3GPP access networks (providing GSM/EDGE, UTRA, E-UTRA, or NR radio access), and/or non-3GPP access networks (such as WLAN), and User Equipment.
3GPP core network
UE
3GPP system
3GPP access network
3rd party
User
Subscriber
Subscriber: A Subscriber is an entity (associated with one or more users) that is engaged in a Subscription with a service provider. The subscriber is allowed to subscribe and unsubscribe services, to register a user or a list of users authorised to enjoy these services, and also to set the limits relative to the use that associated users make of these services.
User: An entity, not part of the 3GPP System , which uses 3GPP System services. Example: a person using a 3GPP System mobile station as a portable telephone.
Non-3GPP access network

## Slide 4: SA1 Requirements Applicability
Now that SA1 is starting to define requirements for a new generation, should we re-visit…
A. Which 3GPP entities SA1 functional / service requirements apply to (excluding KPIs):
3GPP system?
UE?
3GPP network (i.e. (non-)3GPP access and/or 3GPP core)?
Something else?
B. Depending on the service / feature defined, could SA1 requirements also apply to more granular entities?
3GPP core network?
3GPP access network?
Non-3GPP access network?
Other network entities (relays, etc)?
UE
3GPP system
3rd party
User
Subscriber
UE
UE
3GPP network
3GPP network
Observation 2: SA1 requirements may consider more granular entities – however these are considerations (per Obs.1), while Stage 2/3 groups are responsible for setting architectural/implementation requirements .

## Slide 5: Example: Integrated Sensing and Communications (TS 22.137)
For Sensing, SA1 defined the terms ‘sensing transmitter’ and ‘sensing receiver’, and it was clarified in the definitions that:
A Sensing transmitter is part of a RAN node or a UE
A sensing receiver is part of a RAN node or a UE
The requirements in TS 22.137 are on the network or system ‘acting’ or ‘doing’ something with a sensing transmitter / receiver (e.g. collect data, authorise)
Observation 3: A sensing transmitter / receiver can, of course, only be a radio node.

## Slide 6: Example: Mobile Metaverse Services (TS 22.156)
spatial anchor: an association between a location in space (three dimensions) and service information that can be used to identify and access services, e.g., information to access AR media content.
avatar: a digital representation specific to media that encodes facial (possibly body) position, motions and expressions of a person or some software generated entity.
Mobile Metaverse Service defined several related services and ‘entities’, such as ‘spatial anchor’, ‘avatar’ and ‘Spatial Localization Service’
Requirements in TS 22.156 are on the network or the system, but ‘acting’ or ‘doing’ something (third party to retrieve information about, or to authorise / identify) in relation to e.g. avatars, spatial anchors, Spatial Localization Service