## Slide 1
Discussion on Distributed Autonomous Sub-network
Source: China Mobile, China Telecom, Robert Bosch GmbH, Huawei, ZTE, OPPO
Agenta item: 8.1.7
© 3GPP 2024
S1-250120

## Slide 2: Distributed Autonomous Sub-network: addressing the needs of vertical industries
Sub-network per Vertical: have its own Sub-networks with complete and minimal set of network features. Customization and local services provisioning, not just UPF deployment for vertical.
Distributed Deployment: close to the verticals. Sub-network makes collaboration with other nodes and provide services together with other nodes.
Network Autonomy: reduce complexity of configuration and deployment for MNO, high resilience.
New type of networking, different from slicing, NPN, etc..
New coordination mechanisms between Sub-network, e.g., each Sub-network has an agent responsible for topology, capability negotiation, and signaling.
Flexible networking and network function combination, where AMF/SMF/UDM/UPF can be aggregated into a basic NF, but provide open interfaces to support the rapid introduction of new NFs/Services.
Motivation
New mechanisms

## Slide 3
Typical Use case
6GC
music festival
amusement park
Shopping centers, music festival and etc, gather tens of thousands of people in a local zone.
Local network requires concurrent accesses for users, priority for services and local maintenance.
Industry requires for sub-network for staff, vehicle, factory.
Various sub-network is required for different level of autonomy and diverse functionalities.
To Business
To Consumer

## Slide 4
Summary of Typical Use case
 | Scenario | Requirements
CMCC (S1-244115, S1-244120) | Industrial park, disaster zone | Customized capability, e.g. sensing, AI, data service, interwork with PLMN autonomous management, running independently adjacent sub-network cooperative work sub-network/capability deployment flexible and rapid
China Telecom (S1-244256, S1-244661) | live news report in rural area | create a distributed network with customized capability interconnection with PLMN, autonomous operation in a limited period
DT (S1-244665) | System and Operational | cloud native design and modular network functions with open APIs
Huawei (S1-244662) | Local zones, e.g., industrial park, shopping centers, power centers, lifestyle centers, factory outlet centers, and festival marketplaces | rapidly offer the network service with autonomy and diverse functionalities take over users when other sub-network is not available stand-alone operation without PLMN inter-(sub)network direct connectivity
ZTE (S1-244152, S1-244155, S1-244181) | Music festival, Factory | automatically deploy customized sub-network as required lifecycle management without impact on the PLMN user subscription data synchronization between sub-network and the PLMN independent operation and maintenance of sub-network failure detection, alert, network switching
OPPO (S1-244752) | Communication between AI agents (robots) in Smart home | grant a bulk of resources for the on-demand sub-networking member Es communication directly

## Slide 5
Gap analysis with Edge Computing
3GPP TS 22.261 includes the following definition for edge computing:
- Hosted Service: a service containing the operator's own application(s) and/or trusted third-party application(s) in the Service Hosting Environment, which can be accessed by the user.
- Service Hosting Environment: the environment, located inside of 5G network and fully controlled by the operator, where Hosted Services are offered from.
Based on operator policy, application needs, or both, the 5G system shall support an efficient user PLMNe path, modifying the path as needed when the UE moves or application changes location, between a UE in an active communication and:
……
The 5G network shall be able to interact with applications in a Service Hosting Environment for efficient network resource utilization and offloading data traffic to the most suitable Service Hosting Environment, e.g. close to the UE's point of attachment to the access network or based on usage information.
Conclusion:
Edge computing is a service to be hosted close to UE and to deliver service traffic with low E2E latency, by selecting a local UPF to forwards traffic to the local DN via a N6 interface.
Edge computing doesn’t support:
NFs, user data/traffic forwarding under control of PLMN. Doesn’t support self-management and self-recovery while disconnect with PLMN. Limited functions and features (e.g.: only support traffic steering)

## Slide 6
Gap analysis with Slicing
3GPP TS 22.261 includes the following definition for slicing:
Network slicing allows the operator to provide customised networks. For example, there can be different requirements on functionality (e.g. priority, charging, policy control, security, and mobility), differences in performance requirements (e.g. latency, mobility, availability, reliability and data rates), or they can serve only specific users (e.g. MPS users, Public Safety users, corporate customers, roamers, or hosting an MVNO).
A network slice can provide the functionality of a complete network, including radio access network functions, core network functions (e.g. potentially from different vendors) and IMS functions. One network can support one or several network slices.
..........
Conclusion:
Network Slice is a logical network that provides specific network capabilities and network characteristics.

## Slide 7
Gap analysis with Slicing - Differences
Guarantee of network resource: All the UEs within the same slice share the resources in slice. Resources in Sub-network is shared by UEs for vertical.
Configuration: Slice is E2E logical network. Sub-network is local network and doesn’t impact the E2E configuration of network.
Resource Segmentation:
Slicing: logical division of network resources from a service perspective
Distributed autonomous sub-network: physical division of network resources based on location.
High UE reliability:
Slice needs UE to support and has major impact to UE architecture. It is not good enough for UE to support slice feature.

## Slide 8
Gap analysis with NPN
3GPP TS 22.261 includes the following definition for NPN:
3GPP TS 22.261 Clause 6.25 describes NPN as:
Non-public networks are intended for the sole use of a private entity such as an enterprise, and can be deployed in a variety of configurations, utilizing both virtual and physical elements. Specifically, they can be deployed as completely standalone networks, they can be hosted by a PLMN, or they can be offered as a slice of a PLMN.
3GPP TS 23.501 Clause 5.30 describes NPN as:
An NPN is either:
- a Stand-alone Non-Public Network (SNPN), i.e. operated by an NPN operator and not relying on network functions provided by a PLMN, or
- a Public Network Integrated NPN (PNI-NPN), i.e. a non-public network deployed with the support of a PLMN.

## Slide 9
Gap analysis with NPN
NPN still can not satisfy the requirements and use cases:
For SNPN:
N3IWF is not commercialized deployment: Interact with PLMN via N3IWF; for non-3GPP access, there are two layers of N3IWFs
Not resource share: All resources are NOT shared with PLMN or other networks, which is highly cost to deploy
Not friendly for new services: Not supporting potential AI-related capabilities in PLMN
Compatibility issues when updating: Updating NFs may have compatibility issues with PLMN
For PNI-NPN:
Low resilience: Subscriptions are all based on PLMN. when PLMN is broken down, PNI-NPN cannot recovery autonomously.
Long route for message flow: Most signals are sent to PLMN CP, resulting in delays and privacy risks
Not friendly for new services: Lack of local computing resource for potential AI-related capabilities
No physical isolation: faults and failures may spread in PLMN and PNI-NPNs
No rapid deployment

## Slide 10
Gap analysis with PALS
3GPP TS 22.261 includes the following definition for PALS:
Providing access to local services refers to the capability to provide access to a hosting network and a set of services offered by the hosting network provider, and 3rd party service providers including other network operators and 3rd party application providers. The services can be localized (i.e. provided at specific/limited area) and can be bounded in time. The user can become aware of the available access to local services, and the process to gain and terminate access to the hosting network and local services. This process should be efficient, and convenient from a user experience standpoint.
Providing access to local services creates new opportunities for users and service providers. For example, access can be provided in areas where there is no coverage provided by other networks (for example, on a fairground established far from other infrastructure), or the access and local services can be established as needed (on a short-term basis), without the need for long term business relationships, permanently installed equipment, etc
Based on the above information and the requirements in clause 6.41, PALS is a service for local services and has been studied how to be satisfied by NPN in R18 NPN phase_2. However,
PALS focus on providing the access and local services
In PALS, the hosting network is supposed to be built on the home network, while the distributed autonomous sub-network can operate and management independently.
NOTE: details analysis of PALS is in appendix.

## Slide 11
Summary
 | EC | Slicing | PNI-NPN | SNPN | PALS | DAS
Local/independently control and management | ★ | ★★ | ★★ | ★★★★★ | ★★★★★ | ★★★★★
Sufficient resource guarantees | N/A | ★★ | ★★ | ★★★★★ | ★★★★★ | ★★★★★
Minimum impact to other networks | ★★★★ | ★ | ★ | ★★★★★ | ★★★★★ | ★★★★★
Friendly to new services and network features (e.g. AI-related, sensing) | N/A | ★ | ★ | ★★★★★ | ★★★★★ | ★★★★★
Interaction and interworking | N/A | ★ | ★ | ★★★ | ★★★ | ★★★★★
High privacy | ★★★ | ★★★ | ★★★ | ★★★★★ | ★★★★★ | ★★★★★
Rapid deployment | ★★★★★ | ★★★ | ★★★ | ★ | ★★★ | ★★★★★

## Slide 12
Definition & Potential requirements
Distributed Autonomous Sub-network:
a network located in a specific zone/area with simplified functions or customized capabilities as required, with the capabilities to interact with other network, support rapid deployment, autonomous management and independent operation.
NOTE: the concept of 'sub-network' is intended as an enhancement / improvement and not a replacement to the existing 5G features.
1. 6G system shall provide a distributed autonomous sub-network for authorized 3rd party (e.g. vertical industry) with the capability of with customized parameters locally.
2. 6G system shall provide a distributed autonomous sub-network for authorized 3rd party (e.g. vertical industry) with the capability to manage and configure network in real time, e.g.granting permission of sim cards rapidly.
Note: Real time here is referring to real-time within minutes.
3. 6G system shall provide a distributed autonomous sub-network for authorized 3rd party (e.g. vertical industry) to enable locally processing control PLMNe signaling, data of user and product.
4. 6G system shall provide a distributed autonomous sub-network for authorized 3rd party (e.g. vertical industry) which can interconnect with PLMN, also can running locally and independently.
5. 6G system shall provide a distributed autonomous sub-network for authorized 3rd party (e.g. vertical industry) which is able to invoke network function from adjacent sub-network which belong to the same authorized 3rd party.
6. 6G system shall support a mechanism of distributed autonomous sub-network/new capabilities. e.g. AI, sensing, data service that can be deployed in several hours and minimize interruption time of existing service.
7. 6G system shall be able to support autonomous network management in distributed autonomous sub-network.

## Slide 13
Thank you

## Slide 14
Gap analysis: PALS
According to 3GPP TR 23.700-08 Conclusions(8.3-8.6)
Key Issue #3: Enabling NPN as hosting network for providing access to localized services
“Conclusions in Key issue #4 and Key issue #5 are sufficient to cover all necessary interactions between home network and hosting network.”
Key Issue #4: Enabling UE to discover, select and access NPN as hosting network and receive localized services
8.4.1 General
Not satisfied. The keyword Hosting Network has not been explicitly defined. The corresponding requirements are only mentioned in Appendix N2.
8.4.2 Conclusion for the content of the information for accessing localized services
Satisfied. For manual selection, no normative updates are necessary, yet Clause 5.30.2.2 (Broadcast System Information) includes a Note relevant to this aspect. For automatic selection, there are updates in Clause 5.30.2.3 (UE Configuration and Subscription Aspects) regarding selections based on validity conditions and prioritized lists. Appendix N2.1 also includes information on this aspect.
8.4.3 Conclusion for from where and how UE obtains the information for accessing localized service
Partially satisfied. Most methods for obtaining information reuse existing mechanisms specified in Clauses 5.30.2.2 and 5.30.2.3. The detailed version of this aspect is in Appendix N2.1.

## Slide 15
Key Issue #4: Enabling UE to discover, select and access NPN as hosting network and receive localized services
8.4.4 Conclusion for how the localized service information is used by UE
Satisfied. The hosting network selection modes (automatic and manual) are specified in Clauses 5.30.2.4.2 and 5.30.2.4.3, respectively. Clause 5.30.2.4.1 mentions that UE may select an SNPN providing access for Localized Services. Clause 5.30.2.10.4.2 mentions the UE onboarding function enhancements for PALS. The detailed version of this aspect is in Appendices N2.1 and N3.
8.4.5 Conclusion for what credentials are used to access hosting network and how to obtain them
Satisfied. Clause 5.30.2.3 has updated a plenty of information regarding credentials and Credentials Holder. Besides, Clause 5.30.2.9 (SNPN connectivity for Es with credentials owned by Credentials Holder) has no updates but supports the PALS mechanism. Existing methods in Clause 5.30.2.10 (Onboarding of Es for SNPNs) can be reused. Appendix N6 specifies the configuration of CH for determining SNPN selection information for Es.
8.4.6 Conclusion for how localized service is accessed in hosting network per agreed conditions
Partially satisfied. Updates in Clause 5.30.2.5 (Network access control) specify conditions (e.g. subscription data or invalid time for accessing an SNPN) that may result in rejection of access to PALS. Existing methods can also be utilized to restrict UE's access. Appendix N4 also mentions the access control of UE for localized services.
Gap analysis: PALS
According to 3GPP TR 23.700-08 Conclusions(8.3-8.6)

## Slide 16
Key Issue #5: Enabling access to localized services via a specific hosting network
The enhancement of the existing SoR procedure
Satisfied. The Validity information in UE consists of Time validity information and location validity information (optionally), in Clause 5.30.2.3 (UE configuration and subscription aspects). And it’s mentioned that the information “may be updated by the Credentials Holder using the Steering of Roaming (SoR) procedure as defined in Annex C of TS 23.122 ” .
The architecture specified in clause 5.30.2.7 of TS 23.501 is reused for the UE to access both home network services (using the SNPN as underlay network) and localized services (via the SNPN).
Satisfied. As suggested, “a UE in SNPN access mode that has successfully registered with an SNPN may perform another registration via the SNPN User PLMNe with a PLMN (using the credentials of that PLMN) following the same architectural principles as specified in clause 4.2.8 (including the optional support for PDU Session continuity between PLMN and SNPN using the Handover of a PDU Session procedures in clauses 4.9.2.1 and 4.9.2.2 of TS 23.502 [3]) and the SNPN taking the role of "Untrusted non-3GPP access ".” in Clause 5.30.2.7 (Access to PLMN services via stand-alone non-public networks).
Gap analysis: PALS
According to 3GPP TR 23.700-08 Conclusions(8.3-8.6)

## Slide 17
Key Issue #5: Enabling access to localized services via a specific hosting network
Existing mechanisms (e.g. roaming architecture, network slicing, etc.) are reused for the UE to access home network services via PNI-NPN.
Satisfied. The definition of PNI-NPN has satisfied the requirement as “Public Network Integrated NPNs are NPNs made available via PLMNs e.g. by means of dedicated DNNs, or by one (or more) Network Slice instances allocated for the NPN. The existing network slicing functionalities apply as described in clause 5.15.” in Clause 5.30.3.1 (General).
The reuse of URSP and LADN feature.
Not satisfied in the main content. There is no explicit reference in the main content to the reuse of mechanisms such as URSP and LADN in NPN as host network. But the Appendix N4. clearly points to this: “ …After the UE has successfully registered to a PNI-NPN/SNPN providing access to the Localized Service, the UE can be configured with URSP rules using existing principles (see clause 6.6.2.2 of TS 23.503 [45])…The existing LADN feature described in clause 5.6.5 can also be used for enabling the UE access to Localized Service which is defined by a LADN DNN.”
Gap analysis: PALS
According to 3GPP TR 23.700-08 Conclusions(8.3-8.6)

## Slide 18
Key Issue #6: Support for returning to home network
The reuse of existing mechanisms for Control PLMNe Load Control, Congestion and Overload Control
Satisfied. It’s clearly pointed out that “existing mechanisms defined for Control PLMNe load control, congestion and overload control in clause 5.19 can be used, as well as the access control and barring functionality described in clause 5.2.5, or Unified Access Control using the access categories as defined in TS 24.501 [47] can be used.” in Clause 5.30.3.4 (Network and cell (re-)selection and access control.
Additional mechanisms can be implemented to ensure spreading of return of the Es to home network.
Not Sure. This conclusion itself does not require 3GPP to standardize, and it is reflected in the Appendix N5: “ …For further enhancement of mitigation of signalling overload, additional mechanisms can be implemented to ensure spreading of the load that returning Es cause. Such mechanisms are implementation-specific, but some guidelines that can be considered are described below: …”
Gap analysis: PALS
According to 3GPP TR 23.700-08 Conclusions(8.3-8.6)

## Slide 19
Gap analysis: WiFi
1. Inter-factory interworking: achieve by dedicated line or VPN. Dedicated line is expensive. VPN adopts packet encapsulation technology and other mechanisms to ensure security. Mobile network has more safer mechanism than WiFi.
2. Low security: Pre-shared key (PSK) access authentication, 802.1X access authentication and other schemes are used in WIFI. PSK authentication is easy to be brute-force cracked, ARP attacks and DDoS attacks. Production data and sensitive enterprise information may be stolen, or leaked during transmission.
3. Signal interference: WiFi frequency is 2.4GHz, various metal equipment in the factory may reflect, scatter and absorb the signal of this frequency band, resulting in signal attenuation, affecting the quality and stability of wireless communication.
4. Number of connected device restrictions: there is a certain limit on the number of connections of WiFi devices. It may lead to network congestion, unstable connection or inability to connect.