## Slide 1
Discussion Paper on
Network Simplification
China Telecom

## Slide 2: Motivations for Network Simplification
Current 5G：3GPP defined 40+NFs and 80+interfaces, and the network architecture and topology are both very complex
The complexity of the network leads to three main problems:
Problem 1：Deploying network and network management are relatively complex, resulting in high operational and management costs. The network is not optimization enough.
Problem 2: It is difficult to identify which network element the fault occurred in, and the recovery time is long, usually taking several hours to tens of hours. The network is not robust enough.
Problem 3: When upgrading network features, there are multiple network NFs that need to be upgraded, and the cycle time is long, usually taking several weeks to several months. Also the ‘state’ in network elements is problem as well. Because of network state (e.g. data related to subscribers/users/ongoing sessions), you cannot simply switch traffic from one network node to another. This means that you can only do upgrades or changes to your network in non-busy hours. And there are no non-busy hours anymore. The network is not agile enough.
6G requirement: Supports six major scenarios, avoids network complexity through innovation and optimization of network design.

## Slide 3: Definitions & Potential Standard Work
Definition of network simplification
Network Simplification is a simplification of the operation management interface and interoperability with different vendors, not a reduction in user experience
Network Simplification is the functional reconstruction of NF, not the pruning or simple merging of NF functions
Network Simplification MAY reduce the NF types, interfaces, and procedures, but will NOT reduce network and UE functionalities and capabilities
Potential standard work
SA1
Clarify terminology, including definitions of network simplification, network state, network flexibility, and the characteristics they present.
Describe operational scenarios and use cases，clarify Operator's requirements.
SA2
Optimize NF function design to reduce redundancy; Concentrate data and reduce the number of data interactions; Reduce serial processing and increase parallel processing
Support new mechanism to achieve menu based function customization , expand NF like building blocks, and support for hot plug of new feature
Make networks/network elements smarter, simplify through AI methods, support intelligent native and ubiquitous
AI
Control
Data
Policy
Routing
Fundamental Functions
Expanded functions 1
Expanded functions 2
Expanded functions n
NF1
NF4
NF3
NF2
Interface 1
Interface 2
Interface 3
NF1
NF2
Interface n

## Slide 4: Example: from NTN perspective
NTN scenarios urgently require network simplification
The payload on the satellite is limited, and the on-board NFs requires high integration and efficiency.
The topology of satellite networks is dynamically changing, and the interfaces between NFs should be minimized as much as possible.
round-trip time (RTT) between satellites and ground networks is relatively long, and the procedure between NFs should be simplified as much as possible.
For example: The frequent interaction between satellite and ground in the UE SAT-UE scenario has a significant impact on end-to-end latency and may even lead to failure
Reference: S2-2410549“ DP on AGW reallocation”
completing the address reservation and configuration requires 6 interaction rounds between the MT-side P-CSCF and AGW (on the satellite) and 3 rounds between the MO-side P-CSCF and AGW (on the satellite), totaling up to 9 rounds. Delay may range from 270ms (LEO) to 810ms(MEO)
the address reservation and configuration requires 3 interaction rounds between the MT-side P-CSCF and AGW (on the satellite) and 3 rounds between the MO-side P-CSCF and AGW (on the satellite), totaling up to 6 rounds. Delay may range 180ms (LEO) to 540ms (MEO). In this case, 2 AGW (on the satellite) are selected.
5GC
Gateway
gNB+UPF+AGW
UE
UE

## Slide 5
Thank you