## Slide 1: Discussion on UE and (Ambient) IoT device definitions
Philips International B.V

## Slide 2: Background
During discussions on the definition of Ambient IoT device in SA#106 based on discussion paper SP-241876, it was clarified that there are two separate definitions for "UE“:
  Definition in TS 22.261 not mentioning UICC:
    “User Equipment: An equipment that allows a user access to network services via 3GPP and/or non-3GPP accesses.”
  Definition in TR 21.905 mentioning UICC:
    “User Equipment (UE): Allows a user access to network services. … Currently the User Equipment is subdivided into the UICC domain and the ME Domain. ….”
TSG SA asked SA WG1 to review both definitions and to provide the necessary clarification CR(s) to either TS 22.261, TR 21.905 or both.

## Slide 3: Background (ctd.)
During discussions in SA WG1 in relation to Ambient IoT, it was clarified that an Ambient IoT device is defined as a type of IoT device, which in turn is a type of UE:
  “Ambient IoT device: An ambient power-enabled Internet of Things device is an IoT device powered by energy harvesting, being either battery-less or with limited energy storage capability (e.g., using a capacitor).”
  “IoT Device: a type of UE which is dedicated for a set of specific use cases or services and which is allowed to make use of certain features restricted to this type of UEs.
    NOTE 5: An IoT device may be optimized for the specific needs of services and application being executed (e.g. smart home/city, smart utilities, e-Health and smart wearables). Some IoT devices are not intended for human type communications.”
Therefore, by inference an Ambient IoT device can be seen a type of UE according to TS 22.261.

## Slide 4: Background (ctd.)
It was also discussed that the definition in TS 22.261 would take precedence for the requirements in TS 22.261 and the related requirements in TS 22.369. Hence, the definition of Ambient IoT device does not automatically imply that Ambient IoT device has a UICC, even if TR 21.905 mentions otherwise.
Potential issue: downstream working groups (e.g. SA2, SA3) may use the definition of User Equipment of TR 21.905 instead of TS 22.261. Hence, clarification of the definitions is needed.
Clarifying the definitions is important, because SA WG1 did not intend by its Ambient IoT definition to give any guidance on whether a UICC is required for Ambient IoT devices or not.
  Requiring a UICC is problematic for an Ambient IoT device given its extremely low energy characteristics. An Ambient IoT device has special characteristics to be taken into account, which is also why the Ambient IoT requirements are largely documented in a separate TS 22.369.
Anyway, some alignment between the definitions in TS 22.261 and TR 21.905 seems to be needed, since TR 21.905 does not yet contain any definitions for IoT device and Ambient IoT device.

## Slide 5: Proposals
Update TR 21.905 as follows:
  Merge definition of “User Equipment” of TS 22.261 and TR 21.905, whereby any statements about requiring a UICC is removed (or alternatively made informative).
  Copy the definitions of “IoT device” and “Ambient IoT device” from TS 22.261 to TR 21.905
  The detailed proposal can be found in contribution S1-250311