## Slide 1: Discussion on 3GPP interaction with M2M service enablement
Takanori Iwai, NEC, (t-iwai@hx.jp.nec.com)
Joerg Swetina, NEC, (joerg.swetina@neclab.eu)
S1-133059

## Slide 2: Background
Currently oneM2M has started standardization work for M2M service enablement layer (see LS in oneM2M-TP-2013-0251R01).
An M2M service enablement platform needs to interwork with the 3GPP System to communicate with its MTC Devices via 3GPP networks
  Additionally, 3GPP may need to be given additional information on M2M traffic (e.g. to address all devices within a given region, to request specific QoS treatment …)
Allowing for traffic with lower ARPU such as M2M requires adaptation of the 3GPP network - reducing required network resources for such traffic. (= optimize network parameters) depending on the utilization characteristics of a specific M2M device.
  Utilization characteristics depends on M2M Services and can be provided by oneM2M service enablement platform
  Utilization characteristics: Mobility (Frequency, Velocity of movement), Communication characteristics (Frequency of communication establishment, Data Volume, Required Bandwidth, Acceptable Delay).
    For a stationary device(=low mobility), larger value of the Tracking Area Update Timer should be set
    For a chatty device (=communicates frequently), larger value should be set for the Inactivity Timer
3GPP has started to become active on these issues.
  SA2 has prioritized MTCe-SDDTE (Small Data and Device Triggering Enhancements) and MTCe-UEPCOP (UE Power Consumption Optimizations) building blocks for Rel-12
However currently there is no way for a M2M service enablement platform to provide the 3GPP System such additional information

## Slide 3: Some examples for potential optimization in 3GPP
Process to be adjusted (parameter) | Detail | Benefit | Utilization characteristics relevant for tweaking network parameters
UE Inactivity Timer (discussion on-going in SA2) | The timer release the RRC connection expires | signaling load reduced on connection management | Frequency of session-establishment
Paging Area (spec. completed) | The area seeking a User Equipment | Signaling load reduced on paging | moving range and frequency
Location registration interval (spec. completed) | The cycle interval between location (tracking area) Update | signaling load reduced on location registration | moving range and frequency
DRX Timer (discussion on-going in SA2) | The cycle interval between monitoring Paging Occasion for a specific UE | Device battery saved | Acceptable delay, Frequency of session-establishment
Back off Timer (spec. completed) | The timer include some time randomisation to guard against a repeat of a load peak | Network congestion avoided | Acceptable delay, Frequency of session-establishment
Device utilization characteristics may vary dynamically depending on the M2M Service status

## Slide 4: Examples for M2M Services (or Devices) whose behavior (Mobility/Communication Characteristics) can vary
Service | Mobility Characteristics (mobile – high and stationary – low) | Communication Characteristics (Intervals of communication establishment)
ITS | Mobility characteristic of device is Dynamic: Driving (mobile) or Parking (stationary) | Communication characteristic: Dynamic Navigation aids: ON ( short interval) Navigation aids: OFF ( long interval)
Logistics – traceability of cargo | Delivering (mobile) or Loading in a freight distribution center (stationary) | Delivering (short interval) or Loading (long interval)
Healthcare | In the street (mobile) or At home (stationary) | Communication characteristic of device may be Static or Dynamic
Home/Office Security | Out the door (mobile) or At home (stationary) | Communication characteristic of device may be Static or Dynamic
Smart Meter | Mobility characteristic of device is Static (device is not moving) | Normal operation (long interval) or Out of order (short interval)
Agriculture | Mobility characteristic of device may be Static (device is mounted in the field) or Dynamic (device is mounted on vehicle) | Normal operation (long interval) or Out of order (short interval)
Pet Monitoring | Out the door (mobile) or At home (stationary) | Normal operation (long interval) or Out of order (short interval)
colour code: … characteristics are dynamic

## Slide 5: Proposal: 3GPP support by M2M service enablement Platform
ITS
Network dynamic control according to the device characteristic
Behavior change detection of a MTC Device
Electric
power
Transportation
Health care
Crime
prevention
M2M service PF
3GPP Network
(MME, S/P-GW,
HSS, eNB)
Smart
Meter
Car
The M2M service enablement Platform, together with related services, identifies the behavior (or a change of behavior) of a device
The 3GPP Network adapts related parameters. E.g.
・Paging Area
・Inactivity Timer
Burglar alarm
Sensor
INPUT
Truck

## Slide 6: … but also other direction is useful and should be considered
ITS
Network detects congestion in a certain region
M2M Platform delays traffic with devices in that region
Electric
power
Transportation
Health care
Crime
prevention
M2M service PF
3GPP Network
(MME, S/P-GW,
HSS, eNB)
Smart
Meter
Car
The M2M service enablement Platform, together with related services, identifies which traffic can be delayed
The 3GPP Network benefits from temporary reduction of traffic.
Burglar alarm
Sensor
OUTPUT
Truck

## Slide 7: Required action in 3GPP
Interface towards M2M service enablement platform needs to be enhanced to exchange related data
3GPP needs to be able to map such device characteristics into network parameter
Work item on “Support for interworking with M2M service enablement” should be updated in Rel-13 (proposal in S1-133060)