## Slide 1: Discussion on IMS Slicing
HUAWEI, China Mobile, China Telecom
3GPP TSG-SA WG1 Meeting #84 S1-183126
Spokane, WA, USA, 12 - 16 November 2018 (revision of S1-18xxxx)

## Slide 2: IMS challenge in the future is to support services in verticals
Traditional Personal Voice
VR/AR
IP PBX
(Fix/Mobile)
One IMS network
(S-CSCF/I-CSCF/P-CSCF/HSS…; Media plane(IMS-AGW/MRFP))
Fixed AN
AN
IMS enabler
Business Service
MCPTT/MCVIDEO
Mobile AN
V2X ToD
(tele-operated driving)
UE
Notes: IMS can support variety of services, such as VR Tele-presence, MCPTT and MCVIDEO, which differ from the original basic voice services in media processing function and performance, signaling routing, and connection management.
Some verticals, such as V2X ToD (Tele-operated Driving) and e-Health remote surgery have high-quality real-time audio and video communication requirements. These verticals require more openness from IMS, so that it can be extended to provide services for these verticals.
“one IMS enabler provides all services” leads to the enabler being relatively heavy and is not easy to be tailored for different services. Customization of IMS functions on demand needs increase flexibility, to quickly support new services and meet vertical openness requirements.

## Slide 3: Current options based on IMS
User
Traditional Personal Voice
VR/AR
One IMS network
(S-CSCF/I-CSCF/P-CSCF/HSS…; Media plane(IMS-AGW/MRFP))
MCPTT/MCVIDEO
Option 1: Initial Filter Criteria (IFC) trigger
Big challenge to introduce a new service
Performance, signaling routing, and connection management challenge.
ifc1
ifc2
ifc3
Option 2: Standalone configuration
Traditional Personal Voice
VR/AR
One IMS network
MCPTT/MCVIDEO
User account1
One IMS network
One IMS network
User account2
User account3
User
User account1
Not efficient on investment
Too many user account, hard to manage.
High OPEX.
Notes: Intro (Option 2):
Each IMS network can be distinguished by its unique IMS home domain name. Each IMS network includes the whole IMS components, such as S-CSCF/I-CSCF/P-CSCF/HSS…; Media plane(IMS-AGW/MRFP). Different services can use different IMS networks as shown in the above diagram.
The UE registers to each IMS network with different IDs and then support different services(MO/MT) with different IDs.
Cons (Option 2):
Each IMS network need one set of ID (IMPU/IMPI) for the UE. Multiple IMS networks need multiple IDs. But the user often does not like so many IDs and expect only one set of ID.
The UE needs to send register request and keep alive to each IMS network, which consumes more network resources (e.g. multiple IMS registration processing resources).

## Slide 4: IMS Slicing option
V2X
V2X
V2X
V2X
User
User account1
IMS Common Part (access, register, user database) , optional for slice selection
IMS
VoLTE
VR/AR
MCPTT/MC-VIDEO
IP PBX
(Fix/Mobile)
V2X
IMS
IMS
IMS
Slice manager
1 user account for all service
Slice management
Only necessary IMS component in the slice
IMS slice 1
IMS slice 2
IMS slice 3
IMS slice 4
ifc1
ifc2
Notes: Intro:
This does not need multiple IMS networks for one UE. It only use one IMS network with one unique IMS home domain name for one UE as shown in above diagram.
The UE only registers once to the IMS network with one set of ID (IMPU/IMPI) and then support different services(MO/MT) with one set of ID.
The IMS network is divided into multiple IMS slices and IMS common part, and this decouples registration and services. IMS common part is shared by multiple IMS slices in one IMS network, and it includes register related functions such as access, register, user database. IMS slice includes the specific service functions such as routing , media .
Pros:
The UE can use one set of ID to use multiple services.
The UE can send register request and keep alive to one IMS network, which minimizes consumption of network resources (e.g. IMS registration processing resources).
Based on multiple IMS slices in IMS network, this decouples registration and services, so it can independently extend registration and services.

## Slide 5: IMS Slice definition
IMS Slice: IMS slice is composed of all or part of IMS functional entities. It can be used to divide IMS resources and functions according to different IMS services.
Traditional Personal Voice
VR/AR
IP PBX
(Fix/Mobile)
IMS Slice1(routing;media plane)
IMS enabler
Business Service
MCPTT/MCVIDEO
V2X ToD
(tele-operated driving)
IMS Slice2(routing;media plane)
IMS Slice3(routing;media plane)
IMS Slice4(routing;media plane)
IMS Slice5(routing;media plane)
UE
One IMS network
IMS Common Part (access, register,user database)
REGISTER

## Slide 6: Difference from the existing network slicing requirement
It is already specified in the TS 22.261, that IMS can be part of a network slice. This can be implemented with the existing IMS network to support the scenario that different subscribers are served by different 5GC slice and IMS networks.
Observation #1: The existing IMS network can support different IMS subscribers to access different IMS networks via different 5GC slices, both of which are part of a network slice.
However, without enhancement to IMS, it is not possible to support a single IMS subscriber to access multiple IMS networks with either single SIM /single IMPI or different IMPIs via a single or multiple 5GC slices, as shown below in the diagrams. Since the existing IMS network requires that a single S-CSCF to serve a singe IMS subscription, and requires a single P-CSCF to serve a single IMPI, it is not possible to select the different IMS networks from deployment point of view. Furthermore, there is no way to support how to allocate different media resources, such as MRFP, AGW for a single IMS subscriber.
Observation #2: The existing IMS network is unable to support a single IMS subscriber to access multiple IMS networks with either single SIM/single IMPI or different IMPIs via a single or multiple 5GC slices.
In addition, the network management system needs to be aware whether IMS is part of network slice or IMS slice is independent of 5GC slice.
Observation #3: Enhancement to the network management system is needed to support IMS slice independent from 5GC slice.
In summary, the requirement to have IMS slice independent of the 5GC slice requires enhancement to both the IMS system and network management system, and is not possible to be supported with existing IMS system or deployment.
IMS slice independent of 5GC slice

## Slide 7: Thanks