## Slide 1: Discussion on V2XIMP
SungDuck Chun
LG Electronics
FS_V2XIMP Rapporteur
3GPP TSG-SA WG1 Meeting #84
Notes: 1

## Slide 2
First Topic
Notes: 1

## Slide 3: Short summary of the study:
3GPP System
Third party (e.g. V2X application)
3GPP System
Third party (e.g. V2X application)
Information Request
Information Response
(e.g estimated information)
Option B
Option A
In Rel15, V2X application requests a certain quality of service to the Network to support V2X communication. In case of network problem, the communication is dropped after that V2X application is notified.
Based on various use cases, the SID concluded to allow the Network to provide detailed information on quality of service of V2X communication/bearer using a 3GPP connection to the application to avoid impact to V2X communication as much as possible.
During the study, use cases on option B were discussed, not on option A, so consolidated requirements and associated normative text are illustrating this Option B
estimation capability
Estimation capability
Information Request
Information Response
(e.g. statistics data)
Statistics data
Statistics data
Notes: 1

## Slide 4
Second Topic
Notes: 1

## Slide 5: Terminology: ‘quality of service’ vs “xxx”
During months of SA1 TR discussions, text agreed enabled the V2X application to be aware of quality of service changes for the bearer it uses for its V2X communication.
3 types of requirements have been consolidated:
Network warns the application if the current quality of service of a UE’s communication cannot be fulfilled (so might be dropped soon)
Networks changes the UE’s communication quality of service to another quality of service in line with application needs when the current QoS cannot be supported anymore
Network provides the V2X application with some estimated quality of service a UE communication might obtain in a certain area/time, based on past statistics
For these 3 types of requirements, the term quality of service used is appropriate as it is the quality of service of the UE’s communication, i.e. usual 3GPP term.
We see no need to define another term to replace existing quality of service of a UE bearer/communication
Notes: 1

## Slide 6: Conclusion of session
This session was held from 13:00 to 13:50 Tuesday and agreed following
Requirements aligned to option B in slide 3 will be in the normative CR to TS.
Figure in slide 3 with update (i.e. interface between estimation and data) will be captured into Annex of TS
Current terminology ‘quality of service’ is kept
Notes: 1