## Slide 1: Use Case for Determination of 5G Time Synchronization Budget
Michael Bahr, Siemens

## Slide 2: Time Synchronization in Vertical Domains
Different vertical domains have their specific requirements on and profiles for time synchronization:
  IEC/IEEE 60802 Time-sensitive networking profile for industrial automation
  Energy distribution IEC 61850-9-3 [3]
  Audio/Video production

## Slide 3: IEEE 60802 – Definitions Time Synchronization
Relative time error TER(A,B) is the difference between the time of clock A (TA) and the time of clock B (TB), i.e., TER(A,B) = TA – TB. (IEC/IEEE 60802 [1-3.2] [14])
Maximum absolute relative time error max|TER| is the maximum of the absolute value of the relative time error. (IEC/IEEE 60802 [1-3.2][14])
Constant time error cTE is the time error or relative time error that is constant in time (i.e., static). (IEC/IEEE 60802 [1-3.2] [14])
Dynamic time error dTE is the zero-mean, random component of the time error. (IEC/IEEE 60802 [1-3.2] [14])
The term time synchronization or synchronicity budget of the 5G system corresponds to the maximum absolute relative time error of the 5G system.

## Slide 4: IEEE 60802 – Requirements on Time Synchronization
 | Constant Time Error | Dynamic Time Error
PTP Link [1-5.1.8.2] | 10 ns | 0 ns
PTP Instance [1-5.1.8.2] | 5 ns | 50 ns
Transfer of time from ClockSource to ClockMaster entity at sync master [1-5.1.8.3] | 10 ns | 20 ns
Transfer of time from ClockSlave to ClockTarget entity at sync device [1-5.1.8.3] | 10 ns | 20 ns
Working Clock domain
Longest path between sync master and any sync device is 64 hops [1-5.1.5]
max|TER| <= |1µs| [1-5.1.5] between application clock outputs of sync master and any sync device

## Slide 5: From wired TSN networks to integrated 5G networks / TSN networks
preferred deployment

## Slide 6: Use Case 1: Manufacturing Robots (wireless/wired)

## Slide 7: Use Case 1b: Manufacturing Robots (wireless/wired) with Sync Master in network

## Slide 8: Use Cases: Manufacturing Robot (wireless)
graphic only simplified illustration of mobile robot  can be much more complex in reality
time-synchronized devices are connected in line topology  up to 16+ wired hops inside mobile robot
UE in „non-rotating“ part to have stable position of antenna  UE rather at the beginning of local network

## Slide 9: Use Case 2: Manufacturing Robots (wireless)

## Slide 10: Smart Grid - PMUs

## Slide 11: Proposal for 5GS Time Sync Budget Requirement
Sync budget level | Integration scenario (one/two wireless links) | Clock synchronicity requirement | Synchronicity budget requirement for 5GS | Scenario
1 | one wireless link | ±1 µs | [750 ns] | smart grid - PMU
2A | one wireless link | ±1 µs | 667 ns | two manufacturing robots (wireless/wired) – minimum
2B | two wireless links | ±1 µs | 700 ns | two manufacturing robots (both wireless)
3A | one wireless link | ±1 µs | 500 ns | two manufacturing robots (wireless/wired) – general

## Slide 12: References
[{12}] IEC 65C/987/CD. “Time-sensitive networking profile for industrial automation”, Committee Draft (CD), Sep 2019
[14] IEC/IEEE 60802, "Constraints about Sync", v1.0, 23 Aug, 2019, 60802-Steindl-ConstraintsAboutSync-0919-v10.pdf.
[15] IEC/IEEE 61850-9-3: "Communication networks and systems for power utility automation – Part 9-3: Precision time protocol profile for power utility automation“
3GPP TR 22.832 “Study on enhancements for cyber-physical control applications in vertical domains”