## Slide 1: Disscussion paper of Addition of requirements on Inner Trustiness Network Function
China Unicom
weiqun5@chinaunicom.cn

## Slide 2: Motivation
The requirement of data temper proof in verticals
  Data collected from IoT devices/sensors is mostly sent to service platform directly at the present, e.g. position data in logistics services.
  However IoT data for finance related services may be very crucial. Hence verticals such as supply chain finance and insurance have strict requirements for data integrity and traceability, e.g. environment data(e.g. temperature and windspeed) for agricultural insurance and warehouse data (e.g. number and weight of goods) for inventory financing. Those services require to guarantee data tamper-proof and data traceability from UE to SP（service provider).
  Gap between 3GPP and requirement of verticals
3GPP Network
3GPP UE
Data integrity and Encryption in 3GPP
  The green line indicates data integrity protection applied in the current 3GPP and there is still requirements remained for data tamper-proof from UPF to SP. Data transportation between 3GPP network and SP may be based on clear-text of application layer.
  Moreover, data tamper-proof in a period of time is important for data traceability services(e.g. an insurance claim may need to make tamper-proof for the non-real-time data ).
  Though 3GPP network has its own method to ensure data integrity, there is still a gap between 3GPP network and SP. The means to make tamper-proof for non-real-time data is also necessary to be studied.
UPF
SP
gap
Notes: 3GPP 原有的安全机制是分段保证的 hop-by-hop UPF到SP使用原有隧道的方案，可能在UPF处会看到用户的关键数据 因此需要end-to-end的一种方式来做

## Slide 3: What SA1 can do?
Inner Trustiness of application data
  This WID is designed to provide a end-to-end IoT data temper-proof and traceability, from 3GPP UE to SP base on 3GPP network.
  MNOs's value to fulfill the requirement
  Leading companies of logistics can build its own mechanisms to realize end-to-end data temper-proof and traceability inside its own ecosystem. However, many medium or small scale sized enterprises are searching for a brief way.
  In any case, all kinds of IoT UEs of the enterprises above are connected to MNO’s networks.
  Therefore, 3GPP network is very suitable to achieve data tamper-proof and traceability in data sensitive services.
3GPP Network
3GPP UE
Data integrity and Encryption in 3GPP
Data integrity from UE to SP
UPF
SP
WID Study Area

## Slide 4
Cold chain logistics
During the transportation of vaccines/drugs, vaccines/drugs containers in cold chain logistics may be equipped with IoT sensors which send data to the vehicles. Those vehicles connect to a SP platform by 3GPP network for data gathering and processing. Real-time monitoring is very critical since the products in the container may exceptionally sensitive to changes in pH, temperature and even light conditions.
Ensuring the trustiness of the collected environment data in each container/sensor is necessary to the service in order to guarantee vaccine/drug activity.
In this use case, the requirements are to achieve the data tamper-proof and traceability for the environment data from IoT sensors to the SP.
Moreover, If problems arose, SP (hospital or vaccine company) would claim to trace all the environment data during transportation afterwards and the data tamper-proof may be non-real-time.
Example Use Case

## Slide 5: Requirement Gap Analysis
AKMA
  TS 33.535 specifies the security features and mechanisms to support authentication and key management aspects for applications based on subscription credential(s) in 5G system.
  GAP1: AKMA is an authentication mechanism.
  GAP2: The keys used in AKMA would be refreshed.
Study on Inner Trustiness
  This WID is designed to provide a end-to-end IoT data temper-proof and traceability from 3GPP UE to SP based on 3GPP network..
  NOTE: Only 3GPP UE is considered in this study.
GBA
  TS 33.220 describes the security features and mechanisms to bootstrap authentication and key agreement for application security.
  GAP1:GBA provide an authentication mechanism.
  GAP2: The keys used in GBA would be refreshed.

## Slide 6: Thank you
Notes: Conlusion：
Blockchain is a promising technology to enhance the vertical applications and is an important component in the application layer over 5G network.
  1)In a summary, we can see that the blockchain applications have a tight realtionship with both verticals and 5G newtwork, most of the vertical use case related to blockchain have been studied, what we do is pick it up and summarize it,and study what blockchain can do for the existing use cases in the application layer.
it is in the scope of 3GPP.
2)Applications of blochchain in verticals are based on existing 5G network, and the blockchain application has no impact on the exsiting network architecture and existing functionalities or procedures.
3)SA6 can do
  Summarize the scenarios of the blockchain in application layer supporting verticals over 5G networks.
  Develop key issues, corresponding architecture requirements and solution recommendations to enable the blockchain in application layer support for verticals over 5G networks.
  Deployment models to facilitate tight integration with the underlying 3GPP system architecture.
  Provide suitable application layer APIs.