## Slide 1
Some examples for time bounded communication for FS_SOBOT
-
Source: Ki-Dong Lee, LG Electronics [kidong.lee(at)lge.com]
Agenda item: 4
Document for: Discussion
.
3GPP SA1#92E
Nov 10-19, 2020
.
S1-204295
Supplementary for
S1-204140
※ After some offline discussions on Day 2, it was suggested to provide some simple examples that can help more concretely understand the Study objective.
Some examples are presented in order to show how App layer info can be utilized in transport layer to help improve Service Robots operation.

## Slide 2: 1) Example of Immediate Status Report Operation: eCall (Post-accident response) (1/2)
4) Transport layer:
Initiates eCall + sends status data (MSD)
3) App layer:
PCSSF provides indication
UE
Network
(or PSAP)
1) pre-crash sensing (detected)
2a) Accident happened
2b) Accident avoided
※ PCSSF: pre-crash system sensing function (or PCSS, pre-crash safety system);
Role: Predicts a collision before it happens
※ flow: 1)  2a) or 2b)  3)  4)

## Slide 3: 1) Example of Immediate Status Report Operation: eCall (Post-accident response) (2/2)
4) Transport layer:
Initiates eCall + sends status data (MSD)
3) App layer:
PCSSF provides indication
UE
Network
(or PSAP)
1) pre-crash sensing (detected)
2a) Accident happened
2b) Accident avoided
Reporting procedure is initiated at state 2 (i.e., 2a);
If communication module failed, Report cannot be sent out

## Slide 4: 2) Example of time bounded communication: a network of service robots (case 1)
3) Transport layer:
Initiates Status Sharing
2) App layer:
provides indication
UE1 (robot)
Cloud server (Service Robot operation center)
1) pre-crash sensing (detected)
4a) Accident happened
4b) Accident avoided
(pre-)Reporting procedure is initiated at state 1;
If communication module failed at state 4, Status is already shared
If robot body is lost (fell from cliff) or damaged, Status is already shared
If accident is avoided, robot (UE1) can give indication to server to ignore
UE1 Confirms Positive
UE1 Confirms Negative
※ App layer info (indication) is utilized to improve transport layer feature, in order to improve the quality of robot operations.
※ flow: 1)  2)  3)  4a) or 4b)
Notes: Immediate Status Sharing Operation

## Slide 5: 3) Example of time bounded communication: a network of service robots (case 2: neighbors assist)
3) Transport layer:
Initiates Status Sharing
2) App layer:
provides indication
UE1 (robot)
Cloud server (Service Robot operation center)
(pre-)Reporting procedure is initiated at state 1;
Neighboring robots (UE’s) assist
If communication module failed at state 4, Status Sharing is assisted by neighboring robots (even in OOC): e.g., listen – wait – forward/not
If robot body is lost (fell from cliff) or damaged, Status Sharing is assisted by neighboring robots (even in OOC)
If accident is avoided, robot can give indication to ignore
5)
Listen – Wait – Forward (or ignore)
Neighboring UE’s (robots)
※ The same scenario except the fact that neighboring UE’s (if exist) assist Status Sharing of UE1.
1) pre-crash sensing (detected)
4a) Accident happened
4b) Accident avoided
※ flow: 1)  2)  3)  4a) or 4b)  5)
Notes: ※This example is more relevant for a collaboration scenario (a group/network of robots in a site/hotel/CCRC).