## Slide 1: FS_TACMM discussion
China Mobile, Xiaomi, KPN, Futurewei
3GPP TSG-SA1 Meeting #94bis-e
Electronic Meeting, 5 – 12 July 2021
S1-212078
Source：China Mobile, Xiaomi, KPN, Futurewei

## Slide 2: Coordination among data flows
The existing of multiple data flows may occurs in:
5G Core
UDM
PCF
NEF
AMF
SMF
NSSF
5G Core
UDM
PCF
NEF
AMF
SMF
NSSF
5G Core
UDM
PCF
NEF
AMF
SMF
NSSF
Modality input1
Modality input2
Modality output
Modality input
Modality output1
Modality output2
Modality input1
Modality input2
Modality output1
Modality output2
Upstream
Downstream
Upstream & downstream
  Application server(s) collects data with same or different modalities from multiple sources for analysis and determines multiple data flows as the outputs.
  Application server(s) collects data from one data flow for analysis and determines multiple data flows as the outputs
  Application server(s) collects data with same or different modalities from multiple sources for analysis and determines one data flow as the output
Notes: Coordination happens when there’s multiple data flows
There are three conditions of multiple data flows

## Slide 3: Benefits of Coordination assistance provide by Network
  For application/service:
    Reduced service logic complexity by
      Receiving multiple data for the same event at the same time
      Reduce complexity real time coordination between different application endpoints which may be in different UEs for a multi-modality service.
    Less waiting time with synchronous transmission of inputs
    Better E2E QoE guarantee with the assistance from the network.
  For network:
    Best place for coordination for different flows from different UE, as Network is the centralized aggregated point for those flows.
    Better utilizing network resource
    Less interaction frequency between network and application
    QoS management among multiple data flows
  For user
    Improved QoE

## Slide 4: Potential scenarios regarding synchronization and coordination
Synchronization/coordination assistances provided by network can be:
  Coordinated network action(s) for predefined Important time spot/event within one service among different flows
  QoS status Analyzing for multiple flows within one multi-modality service.
  Coordinated Network and UE Interactions while there’re different UEs within one service
  A synchronized User Data delivery for different flows within a modality service based on pre-agreed policy between application and network

## Slide 5: Network assisted solution VS Pure Application based solution
 | Network | Application
Pros | Better knowledge and access to QoS control for the efficient usage of network resource Could use capability exposure on information(resource, network condition, location, etc.) Flexibility in adding new UEs into service Reduce the complexity of UE Lower power consuming Easy Charging for multi-modality service | Better access to content No more requirements in data transmission Easy handle all modalities Less impact to network
Cons | May need additional inspection on package to do coordination on packet level Need QoS enhancement for the multi-modality service Need application assist | Need customized UE for specific application May result in longer latency Adjustment not in time and less accuracy Limit location and network resource information Complexity in application for the coordination of multiple data flows

## Slide 6: Way forward
Hope we can reach agreement that:
  Assisting application in synchronizing different data flows (include same UE and different UEs) as listed in the slice #4, need to be considered in this study
  There’s advantage of network based/assisted solution thus further enhancement is needed on network capability regarding TACMM service.