## Slide 1: [FS_PIN]s Outstanding issues (defs and req consolidation)v2
SA1#94e pre-call

## Slide 2: Definition – what is a PIN?
vivo | Nokia | Intel | LG | Futurewei
Personal IoT Network: one or more PIN Elements that communicate with each other using either PIN direct connection, direct network connection or Customer Premises Network. | Personal IoT Network: one or more PIN Elements that communicate with each other using either PIN direct connection or direct network connection or Customer Premises Network. | Personal IoT Network: one or more PIN Elements that communicate with each other using either PIN direct connection or direct network connection via PIN Element Gateway. | Personal IoT Network: a network composed of one or more PIN Elements, outside of operator’s network | Personal IoT Network: a small local area network being created for the communication between the PIN Elements of this network. NOTE: The communication between the PIN elements can be direct device connection.
Rapporteurs analysis |  |  |  | 
 | Adds in connectivity types | Adds direct network connection via PN Gateway | Adds in term network. Adds in “outside operators network” | Adds qualifier of “small” + “local area”
Questions
Do we say it’s a network?
Add in connectivity types? If so do we also cover PIN Elements using NR-RAN?
Does Gateway need to be included?
Qualifiers such as “Small” or “local area” provide value?
ONLINE RESULT
HERE IS WHAT WE DRAFTED ONLINE
“…one or more PIN Elements that communicate with each other …”

## Slide 3: Definition – What is a PIN Gateway?
vivo | Nokia | Intel | LG
PIN Element with Gateway Capability: can act as a gateway that provides access to and from the public operator’s network (fixed/mobile/cable) and a PIN. | PIN Gateway Element with Gateway Capability: can act as a gateway that provides access to and from the public operator’s network (fixed/mobile/cable) and other a PIN Elements. | PIN Element Gateway: use direct network connection to provides access to and from the public operator’s network (fixed/mobile/cable) and for other a PIN Elements. | PIN Gateway Element with Gateway Capability: can act as one form of a gateway that routes traffic between provides access to and from the public operator’s network (fixed/mobile/cable) and a PIN, and within a PIN.
Rapporteurs analysis |  |  | 
 |  | Qualifies type of connectivity to operators network. Adds clarity that is just for communications external to the PIN | Adds routing between networks. Adds routing within a PIN
Questions
Do we want to mention types of connectivity on either side of the gateway?
Do we want to indicate a gateway performs any functionality within a PIN e.g. routes traffic within the PIN?
ONLINE RESULT
HERE IS WHAT WE DRAFTED ONLINE
“…provides access to and from the public operator’s network and other PIN Elements…”

## Slide 4: Definition – What is PIN direct connection?
Current definition | LG | Nokia | Intel
direct device connection: See definition in TS 22.261 [2]. direct network connection: See definition in TS 22.261 [2]. ….. PIN direct connection: the connection between two PIN elements without any 3GPP RAN or core network entity in the middle. NOTE 1: A PIN direct connection could internally be relayed amongst other PIN elements or other entities (such as a WLAN access point). Editor's Note: It is for FFS if further clarification to the term is needed and whether a separate term for an indirect connection or relayed connection is needed. | - PIN Internal direct connection: Direct communication between two PIN elements without any other entity in the middle - PIN Internal indirect connection: Communication between two PIN elements via other entity in the middle. - PIN External connection: Communication between a PIN element and operator’s network - inter-PIN connection: Communication between PIN elements belonging to different PINs | PIN direct connection: connection between two PIN elements, potentially including relay by other PIN elements, without any 3GPP RAN or core network entity in the middle. NOTE: signalling connectivity to the 5G network is required when a PIN direct connection uses 3GPP radio. | PIN direct connection: connection between two PIN elements, including relay by other PIN element with Gateway Capability, without any 3GPP RAN or core network entity in the middle.
 | Proliferation of terms. New aspects are: Inter PIN communications PIN External communications would seem be covered by already existing 3GPP term direct network connection | Takes relay aspect from the NOTE and adds into the term. | Adds gateway into the term
Questions
Do we need to add gateway into the term?
Should we have a single term that covers when a relay and no relay is in “intra PIN communications”? If single term is ok should we mention relay in a NOTE (existing TR def) or as part of the term?
Should we have a term for every possible or some communications of communications e.g. inter PIN, intra PIN (direct or via relay)?
ONLINE RESULT
HERE IS WHAT WE DRAFTED ONLINE
“…a connection between 2 PIN Elements…”

## Slide 5
PIN
Home Automation
GW
Relay
Relay
Relay
Relay
Notification
On smartphone
Ethernet
5G Core Network
Non 3GPP Direct device connection
Non licensed spectrum 3GPP Direct device connection
Licensed spectrum 3GPP Direct device connection
3GPP Direct Network connection
Guest PIN
Element

## Slide 6: Inter PIN communications
PINa
Wearables
PINb
Wearables
Guest PIN
Element

## Slide 7: Backup

## Slide 8
5G Core Network
UE
RAN
UE
What TS22.261 supports in description of connection:
Direct Network connection
Indirect Network connection
Direct device connection(via 3GPP or non-3GPP RAT)
UE
Definitions in TS22.261, UE also covers IoT device
User Equipment: An equipment that allows a user access to network services via 3GPP and/or non-3GPP accesses.
IoT device: a type of UE which is dedicated for a set of specific use cases or services and which is allowed to make use of certain features restricted to this type of UEs.
5G Core Network
UE
RAN
Remote UE
What TS22.261 supports for 5G LAN:
Direct Network connection
Indirect Network connection
Private communication in 5G LAN-VN
UE
5G LAN VN
Definition in TR21.905:
User Equipment (UE): Allows a user access to network services. For the purpose of 3GPP specifications the interface between the UE and the network is the radio interface. A User Equipment can be subdivided into a number of domains, the domains being separated by reference points. Currently the User Equipment is subdivided into the UICC domain and the ME Domain. The ME Domain can further be subdivided into one or more Mobile Termination (MT) and Terminal Equipment (TE) components showing the connectivity between multiple functional groups.

## Slide 9
5G network
UE enabled to access the NIN
Device1
Gateway
(e.g. PIN element GW)
Device2
Device3
Network in a network (NIN) (e.g. PIN)
Key:
Direct network connection
NIN direct connection
NIN direct connection with relay
Basic NIN Connection types
REMOVED
Notes: REMOVED – This used to have a PRAS in it and the Device 1 used Direct Network connection (Uu) to communicate with the PRAS. Given the PRAS was removed this slide is not correct.

## Slide 10
5G network
UE enabled to access the NIN
Device1
Gateway
(e.g. PIN element GW)
Device2
Device3
Network in a network (NIN) (e.g. PIN)
Key:
3GPP connection
3GPP/non-3GPP connection
Non-3GPP connection
3GPP/non-3GPP NIN Connection types

## Slide 11
5G network
Radio access
Device1
Gateway
Device2
Device3
Network in a network (NIN) 1
Key:
Intra NIN connection
Cross NIN connection
Cross NIN Connection
Device1
Gateway
Device2
Device3
Network in a network (NIN) 2
UE enabled to access NIN1 e.g., as guest