## Slide 1: SA1 Rel-18 Normative Work - with indications of possible RAN impact -
S1-214195

## Slide 2: Introduction
This presentation aims to give an outline of the normative work done by SA1 in the context of Rel-18 and list the possible RAN topics that could be affected.
Slide number 3 presents an indication of possible RAN impacts elaborated by the respective rapporteurs. It addresses only RAN Rel-18 topics that might be impacted by SA1 Rel-18 normative work.
Rel-18 Stage 1 will freeze in Dec 2021. As of today, all normative work items but one have been completed to a minimum of 80%.
List of RAN Rel-18 topic email discussions RP-212657

## Slide 3: SA1 Rel-18 work - indications of possible RAN impact -
RedCap evolution
Expanded and improved Positioning
Ranging Services
Personal IoT and Residential Networks
Smart Energy and Infrastructure
Vehicle-Mounted Relays
Uplink enhancements
Mobility enhancements
Additional topological improvements (IAB & VMR)
Enhancements for XR
Sidelink enhancements
NTN evolution
Evolution for broadcast & multicast services
AI/ML for air interface
Network energy savings
5GS with Satellite Access to Support Control and/or Video Surveillance
5GS with Satellite Backhaul
Tactile and Multi-Modality Comm. Services
Enhanced Access to and Support of Network Slice
Low Power High Accuracy Positioning for Industrial IoT scenarios
5G Timing Resiliency System
AI/ML for NG-RAN
Network slicing enhancements
X
X
X
X
X
X
X
X
X
X
X
X
Disclaimer: This slide contains an indication of possible RAN impacts suggested by SA1 Rel-18 rapporteurs.
X
Networks Providing Access to Localized Services
X
X

## Slide 4: SA1 Rel-18 Normative Work
Evolution of IMS Multimedia Telephony Service
Enhanced Access to and Support of Network Slice
AI/ML Model Transfer in 5GS
5G Timing Resiliency System
Ranging Services
Personal IoT and Residential Networks
Networks Providing Access to Localized Services
Vehicle-Mounted Relays
Tactile and Multi-Modality Communication Services
Subscriber-Aware Northbound API access
Support for Service Function Chaining
Data Integrity in 5GS
Signal Level Enhanced Network Selection
Smart Energy and Infrastructure
FRMCS Evolution
Low Power High Accuracy Positioning for Industrial IoT scenarios
Service Exposure Interfaces for Industry
Sharing Administrative Configuration between Interconnected MCX
Ad Hoc Group Communication in Mission Critical Services
MPS when Access to EPC/5GC is WLAN
Guidelines for Extra-territorial 5G Systems
5GS with Satellite Backhaul
5GS with Satellite Access to Support Control and/or Video Surveillance
Enhancements (TS 22.261)
New Features (TS 22.261)
Verticals + NTN focused (TS 22.261, TS 22.104, others)
The following slides address only SA1 Rel-18 work items that might be relevant to the RAN Rel-18 topic e-mail discussions. Normative working items with no RAN impacts are included in an Annex I.

## Slide 5
New Features
5G Timing Resiliency System [5TRS] |  |  | 
Rapporteur: | Betsy Covell (Nokia) | Output : | TR 22.878 (new) TS 22.261 (new clause 6.36 5G Timing Resiliency )
Summary | The 5G timing resiliency system introduces holdover and frequency stability capabilities enabling the 5G system to receive information from RAN nodes (e.g., GNSS reports) to determine the status of the overall system and influence consistent operation of timing resiliency. With timing resiliency capabilities, the 5G core network can provide a consistent and fault tolerant solution for all or parts of the network. The 5G system can also provide an alternative timing source to verticals currently relying on GNSS timing solutions. |  | 
Possible RAN impact | Noting that RAN groups are considering sidelink enhancements to increase resiliency, it would be desirable to have a consistent solution whether sidelink is in use or not. The 5TRS requirements provide guidance on increased timing resiliency mechanisms that should be met by the 5G system with or without sidelink. |  | 
Ranging Services [Ranging] |  |  | 
Rapporteur: | Xiaowei jiang (Xiaomi) | Output : | TR 22.855 TS 22.261 (new clause 6.37 Ranging based services)
Summary | The work specifies the functional and performance requirements for Ranging based services(i.e. applications utilizing angle and direction between UEs). It mainly focuses on commercial use cases, e.g. smart home, smart city, etc. Some example KPIs include distance/angle accuracy, latency, confidence level, availability, ranging interval, effective ranging distance, concurrent ranging operations. |  | 
Possible RAN impact | Ranging requires RAN to design Sidelink based ranging architecture, methods(AOA/AOD/RTT etc.) and PHY reference signals and measurements. The use of unlicensed spectrum will also need RAN to design support of sidelink on unlicensed band. |  | 

## Slide 6
Personal IoT and Residential Networks [PiRates] |  |  | 
Rapporteur: | Xiaowan Ke (Vivo) | Output : | TR 22.858 (Resident Study - new) TR 22.859 (Personal IoT Networks Study - new) TS 22.261 (new clause 6.38 Personal IoT Networks and Customer Premises Networks)
Summary | Personal IoT Networks (PINs) and Customer Premises Networks (CPNs) provide both local connectivity and, via a gateway, access to 5G network services. CPNs and PINs have in common that in general they are owned, installed and/or (at least partially) configured by a customer of a public network operator. A Premises Radio Access Station (PRAS) is a base station installed in a CPN to provide in-home 5G coverage. The PRAS provides access to the CPN and/or 5G network services. The PRAS can be configured to use licensed and/or unlicensed frequency bands. A Personal IoT Network (PIN) consists of PIN Elements that communicate using PIN Direct Connection (sidelink) or direct network connection. Examples of PINs include networks of wearables and smart home / smart office equipment. |  | 
Possible RAN impact | "Personal IoT Networks generally can use direct connections between the different devices (PIN Elements). This direct communication can use 3GPP sidelink, either in licensed or unlicensed spectrum. PIN elements may also set up an connection to the 5G network through a PIN element with gateway capability which can be a sidelink relay.“ PIN elements/CPN entities of PIRates can include e.g. wearable device, which could be UE with reduced capabilities. Although there are no specific requirements in Pirates that relate to Redcap, the scenario of PIRates may be considered as references to RAN Redcap work, up to RAN’s decision. |  | 
New Features

## Slide 7
New Features
Vehicle-Mounted Relays [VMR] |  |  | 
Rapporteur: | Francesco Pica (Qualcomm) | Output : | TR 22.839 TS 22.261 (new clause 6.42 Mobile base station relays)
Summary | The VMR work introduces service requirements (in TS 22.261) for 5GS support of mobile base station (BS) relays, e.g mounted on moving vehicles, which provide 5G coverage and communication to UEs (inside the vehicle and/or in its vicinity), and are connected wirelessly to the 5G network via RAN nodes. Requirements include support for mobile BS relays configuration & provisioning, UE access control, QoS, charging, Multi-PLMN RAN sharing, mobility, service continuity, multi-link connectivity, roaming, priority/emergency services, security, RAN management. |  | 
Possible RAN impact | Part of the RAN email discussion #18, on Additional_Topological_Improvements-IAB-VMR |  | 
Networks Providing Access to Localized Services [PALS] |  |  | 
Rapporteur: | Lola Awoniyi-Oteri (Qualcomm) | Output : | TR 22.844 TS 22.261 (new clause 6.41 Providing Access to Local Services)
Summary | This work item provides new service (functional) requirements to enhance 5G system support of UEs accessing to a hosting network and local services offered by service providers, the hosting network operator or third parties, at a given time and geographical location. The normative requirements cover UE and hosting network configuration, provisioning, authentication, authorization, discovery, selection and access. They also covers regulatory services and multicast and broadcast services over the hosting network. |  | 
Possible RAN impact | Likely RAN impact on 5GS support for multicast and broadcast PALS requirements. |  | 

## Slide 8
Tactile and Multi-modality Communication Services |  |  | 
Rapporteur: | Xiaonan Shi (China Mobile) | Output : | TR 22.847 TS 22.261 (normative work expected in Dec2021)
Summary | FS_TACMM aiming at identifying new use cases and potential service requirements for 5GS support of tactile and multi-modality communication services. Use cases involve immersive VR, remote control robot, support of skillset sharing for cooperative perception and maneuvering of robots, haptic feedback for a personal exclusion zone in dangerous remote environments, live event selective immersion, support for IEEE P1918.1 architecture and virtual factory. Requirements involves service exposure requirements to enable 5G system support of tactile and multi-modality applications. |  | 
Possible RAN impact | TACMM requires RAN on supporting processing and handling of multiple flows within one TACMM service according to possible QoS policy enhancements. |  | 
New Features

## Slide 9
Enhancements
Enhanced Access to and Support of Network Slice [EASNS] |  |  | 
Rapporteur: | Ki-Dong Lee (LGE) | Output : | TR 22.835 TS 22.261 (clause 6.1 Network slicing updated)
Summary | This work introduces the support for a UE’s access to a network slice when different types of restrictions apply (e.g. related to radio resources, frequency bands), with minimized interruption of services when there is a change of network slices or allocated resources and support for service exposure for 3rd party control/configuration of network slices. |  | 
Possible RAN impact | EASNS addresses aspects on enhanced support for deployment and operational scenarios with various restrictions, e.g., geographical locations in slice deployment in access, minimizing service interruption, which are relevant to RAN’s interests. |  | 

## Slide 10
Verticals + NTN
Smart Energy and Infrastructure [SEI] |  |  | 
Rapporteur: | Xu Xia (China Telecom) | Output : | TR 22.867 TS 22.261 (clause 6.28 updated) TS 22.104 (clauses 5.2 and 5.6 updated, new clause 8 Recovery of infrastructure for electrical distribution)
Summary | Smart Grid is a term that refers to enhanced cyber-physical control of electrical grids and to related application. Smart Grid operation can cover power generation, transmission, distribution, and consumption, which may require high communication service availability and communication service reliability, and in some cases a low end-to-end latency with more accurate clock synchronization. The SEI WID introduces the Smart Grid specific service requirements in control, monitoring, availability assurance, service security and isolation for 5G systems. |  | 
Possible RAN impact | … |  | 
Low Power High Accuracy Positioning for Industrial IoT scenarios [LPHAP] |  |  | 
Rapporteur: | Yuan Wang (Huawei) | Output : | TS 22.261 (clause 7.3.2.3 updated) TS 22.104 (new clause 5.7.2 Energy efficiency requirements for high accuracy positioning)
Summary | This work specifies requirements on low power high accuracy positioning service for industrial IoT device. |  | 
Possible RAN impact | Enable a device type that has low communication capability with high positioning capability, so that the power efficiency can be improved. The device architecture is to facilitate positioning functionality only, and all communication via radio access is to assist the location service. |  | 

## Slide 11
5GS with Satellite Backhaul [5GSTAB] |  |  | 
Rapporteur: | Hui Xu (CATT) | Output : | CRs to TS 22.261 (clauses 6.5.1, 6.7.2 and 9.1 updated)
Summary | This work introduces new requirements on support of multiple wireless backhaul connections (e.g. satellites and/or terrestrial), QoS control considering satellite backhaul characteristics (including dynamically changed latency and/or bandwidth), and differentiation of charging information for traffic over satellite backhaul. The work has been completed in SA1#94E. |  | 
Possible RAN impact | 5GSATB requires RAN to enhance the mechanism to dynamically handle the backhaul change (e.g., satellite backhaul or terrestrial backhaul). |  | 
Verticals + NTN
5GS with Satellite Access to Support Control and/or Video Surveillance [SVCS] |  |  | 
Rapporteur: | Dong Chen (Xiaomi) | Output : | CRs to TS 22.261 (clause 7.4.2 updated)
Summary | Equipment control (includes controlling commands from console to the equipment as well as equipment status data reporting information to the console) and/or video surveillance (picture or video taken by camera installed on the equipment to console) by mobile and stationary UEs are supported with this WI for 5G system with satellite access. Characteristic of the requirement is that UL data rate (3M) is higher than DL data rate (0.5M). |  | 
Possible RAN impact | SCVS would require RAN to support data rate for UL 3Mbps and DL 0.5Mbps |  | 

## Slide 12
SA1’s TEI-18 CRs that might impact RAN*
S1-tdoc# | CR name | Author | Possible RAN Area affected
S1-213272 | Clarification of requirements for clock synchronization with direct device connection and indirect network connection communication | Nokia, Qualcomm | SL enhancements
TEI-18
*CRs impacting several WGs should not use “TEI” code, but these CRs might still be of interest for RAN

## Slide 13
SA1’s Rel-18 FSs that might impact RAN*
Studies
*FSs should not impact normative work, but these FSs might still be of interest for RAN
Guidelines for Extra-territorial 5G Systems [5GET] |  |  | 
Rapporteur: | Nicolas Chuberre (Thales) | Output : | TR 22.926
Summary: | A guidelines document is produced that should also be useful as a basis for technical work in other 3GPP Working Groups to the provision of services when considering extra-territoriality of the corresponding 5G public network or access. The following topics will be addressed: identification of use cases and conditions generating extra-territoriality of public 5G systems (e.g. HAPS covering multiple countries, satellite access covering international waters, aeronautical networks), identification of 3GPP features (e.g. emergency calls, PWS, LI, charging) and technical aspects (e.g. MCC/MNC, location of UE/NW) for which extra-territoriality may be relevant, and types of regulations that may be applicable. |  | 

## Slide 14: Annex
Normative working items with no RAN impacts

## Slide 15
New Features
AI/L Model Transfer in 5GS [AMMT] |  |  | 
Rapporteur: | Jia SHEN (OPPO) | Output : | TR 22.874 (new) TS 22.261 (new clause 6.40 AI/ML model transfer in 5GS)
Summary | This work introduces the 5GS to support for AI/ML operations for various applications (e.g. image/speech recognition, media editing/enhancements, robot control, automotive). The work specifies performance requirements (for end-to-end latency, experienced data rate, communication service availability) and service requirements (for AI/ML QoS management, AI/ML model /data distribution/transfer, network performance and resource utilization monitoring/prediction). Different use cases where under study: AI/ML operation splitting between AI/ML endpoints; AI/ML model/data distribution and sharing over 5G system; Distributed/Federated Learning over 5G system. |  | 
Subscriber-Aware Northbound API access |  |  | 
Rapporteur: | Atsushi Minokuchi (NTT Docomo) | Output : | CRs to TS 22.261
Summary | Requirements are specified for a UE (or a UE application) to utilize northbound APIs with appropriate authentication and authorization. This feature could potentially increase the effect of “Enhancements for XR”. |  | 

## Slide 16
New Features
Support for Service Function Chaining |  |  | 
Rapporteur: | Ellen Liao (Intel) | Output : | CRs to TS 22.261 (clause 6.35)
Summary | This work item enables enhancement of service function chaining for 5G networks beyond the requirements for FMSS in TS 22.101, the network operator defines service function chaining policies for service function chaining to steer the traffic associated to the application and its users on per UE basis to appropriate ordered service functions. The corresponding service support of service function management and charging aspects for 5G network are also specified. |  | 
Data Integrity in 5GS |  |  | 
Rapporteur: | Qun Wei (China Unicom) | Output : | CRs to TS 22.261
Summary | Data Integrity adds requirements of data integrity verification service on the 5G system, in order to fulfill the demand such as supply chain finance and insurance, etc., which have strict requirements for services that employ IoT device communication for data integrity. |  | 

## Slide 17
New Features
Signal Level Enhanced Network Selection |  |  | 
Rapporteur: | Kurt Bischinger (Deutsche Telekom) | Output : | CR to TS 22.011 (clause 3.2.2)
Summary | For certain UEs introducing an Operator controlled signal threshold per access technology on the USIM to enhance the automatic network selection procedures in that way that in case the threshold is set in a first iteration the UE additionally applies the threshold as an additional criterion in each step of the network selection process, and if registration cannot be achieved during the first iteration a second iteration of the process is performed as today, i.e. without applying the Operator controlled signal threshold. |  | 

## Slide 18
Enhancements
Evolution of IMS Multimedia Telephony Service |  |  | 
Rapporteur: | Hu Yue (China Mobile) | Output : | TR 22.873 CRs to TS 22.261
Summary | This work introduces the support for AR telephony communication and support for 3rd parties (e.g. enterprise) to securely demonstrate to the called party that the caller (e.g. employee) is authorized to use or reference specific business information when placing a call. |  | 

## Slide 19
Verticals + NTN
Service Exposure Interfaces for Industry |  |  | 
Rapporteur: | Joachim W. Walewski (Siemens) | Output : | CRs to TS 22.261
Summary | This work updates TS 22.261 following the results of the gap analysis done against the updated version of the document “Exposure of 5G Capabilities for Connected Industries and Automation Applications” from 5G Alliance for Connected Industries and Automation (5G-ACIA). |  | 
FRMCS Evolution |  |  | 
Rapporteur: | Guillaume Gach (UIC) | Output : | TR 22.989
Summary | SA1 has refined existing critical applications related use cases coming from a gap analysis between the newly released set of UIC FRMCS specifications and latest version of TR 22.989 (e.g., Railway emergency communication, Inviting-a-user-to a voice communication), limited to use cases in on-network mode. |  | 

## Slide 20
Verticals + NTN
Sharing Administrative Configuration between Interconnected MCX |  |  | 
Rapporteur: | Jens Toobe (BDBOS) | Output : | TR 22.881 CRs to TS 22.280
Summary: | Mission Critical Organizations can deploy their own 3GPP standardized mobile, local, countrywide or national broadband mission critical communications systems. In order to grant visiting MCX Service Users access to a Partner MCX Service System and its services, a mechanism is required, which allows the exchange of administrative configuration between connected MCX Service Systems. This work introduces enhancement of architecture and protocols to allow the exchange of administrative information between connected MCX Service systems. |  | 
Ad Hoc Group Communication in Mission Critical Services |  |  | 
Rapporteur: | Erik Guttman (Samsung) | Output : | CRs to TS 22.280
Summary | This work introduce the support for Ad hoc Group communication feature as part of MCX Services and thereby available for MCPTT, MCVideo and MCData. Ad hoc Group communication will be treated as a type of MCX service Group communication and it supports the mechanism of call processing and call termination identical to MCX service Group communication. |  | 
MPS when Access to EPC/5GC is WLAN |  |  | 
Rapporteur: | Ray Singh (Peraton Labs) | Output : | CRs to TS 22.153 (new clause)
Summary | This work introduces support MPS communications when the access to the EPC/5GC is WLAN. Support of MPS when the UE has WLAN access is important during certain disaster scenarios such as when 3GPP access networks (LTE and NR) are not unavailable or degraded. In some cases, WLAN may be the only available access (e.g., inside buildings, hotels, airports, malls and stadiums) and therefore critical for MPS communications. |  |