## Slide 1
China Telecom, CATT
Discussion on Enhancing 5G System Integrating with Satellite for Rel-19

## Slide 2: Overview
TS22.261 has defined basic requirements for integrating satellite access and satellite backhaul into 5G system.
RAN WGs has defined satellite enabled NG-RAN which allows satellites to work as RRU or gNB-DU.
SA2 already enhanced 5G system architecture to support satellite enabled RAN node and satellite backhaul on NG interface, and is studying the case of UPF on GEO satellite.
Going through existing work, there will still some new use cases that are not covered, which would be worthy to be discussed in Rel-19.
Background
Based on the investigation, it is proposed to consider following use cases in Rel-19:
  Use Case 1: Temporary Networking
  Use Case 2: Positioning and Navigation Enhancement
  Use Case 3: Integration with Legacy Satellite System
  Use Case 4: Coordination with satellite system
  Use Case 5: Coordination with multiple satellite RAT
  Use Case 6: Local Data Switching via UPFs on LEO satellite
New Use Case

## Slide 3: Use Case 1: Temporary networking
Use case description:
  As satellite can provide ubiquitous coverage, it is appropriated to be used to serve some special cases, e.g., scientific expeditions or mission critical services etc., when terrestrial network is not available. In such cases, the user, e.g., scientists, may need to setup local data center on the site for data storage, analytics or retrieval locally.
  To support this and allow the scientists to visit the local network directly via the satellite, without going back to the core network deployed far away, a local network needs to be deployed, and can connect to satellite enabled RAN directly via a Gateway.
Potential objectives for study:
  How does the local network connect to the 5G system, including the role of the Gateway that connects the local network with the satellite (e.g. a UE vs a NTN gateway)?
  Whether 5G entities need to be deployed in the local network to support such use cases, e.g. UPF+MEC or a mini 5GC including control plane entities.
  Authentication/Authorization/Accounting for the connectivity of the local network.
  How to protect the communication from the satellite to the Gateway in the local network.
  Authentication of the end users who want to access the local network

## Slide 4: Use Case 2: Positioning and Navigation Enhancement
Use case description for Positioning enhancement:
  Current positioning requirement was defined in Rel-16, and is target to terrestrial access from our views, and some requirements or KPI can not be supported in the case of satellite access, e.g., the TTFX ( 1~10ms).
  New use cases for satellite access need to be investigated as well as their requirements on positioning, e.g. use cases for high accuracy and low latency for positioning via NTN access
  Potential Requirements
  Find the gap between existing positioning requirements for terrestrial access and the requirements that can be satisfied via NTN access, and then determine appropriate KPIs.
Use case description for Navigation enhancement:
  The navigation system may want to improve positioning accuracy or reliability, then it may request 5GS to help to broadcast navigation assistance information with higher priority, e.g., the navigation system may request 5GS to broadcast navigation assistance information in designated areas first even interrupting other services.
  When broadcasting navigation assistance information for high accuracy positioning, there may be frequent data transmission from LMF to gNB on the satellite, whereas the transport resource on inter-satellite link and feeder link are very limited, so the 5G system should consider to efficiently transmit the navigation assistance information to gNBs on the satellite, e.g., compressing navigation data.
  Potential objectives for study:
  Efficiently transmission of navigation data to gNBs on-board, especially for LEO case;
  Support of priority handling when broadcasting navigation data via 5GS.

## Slide 5: Use Case 3: Integrating with Legacy Satellite System
Use case description for Navigation enhancement:
  There are already kind of legacy satellite system running, which are not supporting 5G NR access. To utilize precious satellite radio resources to improve system capacity, the 5G system integrating with NR satellite access should also consider to integrate with legacy satellite system which can be treated as non-3GPP access.
  An example: A satellite operator who is operating legacy satellite system want to enhance his system to 5GS considering industrial ecology, so all new satellites he will launch will support 5G NR access. However, the problem is that the legacy satellites can not be transformed to support 5G NR access, so the operator would consider to connect legacy satellite access nodes into the 5GS.
  Potential objectives for study:
  Support of non-3GPP satellite access in 5GS;
  Whether to distinguish non-3GPP satellite access from general non-3GPP access considering larger latency and lower bandwidth for non-3GPP satellite access , since there may be following impacts:
    The impact to traffic offloading policy on both UE side and network side;
    The impact to access network selection.

## Slide 6: Use Case 4: Coordination with satellite system
Use case description:
  User's requirements are agnostic to the satellite operation center, i.e. NTN control function defined in RAN3, so the NTN control function can not take users' requirements into account to reserve satellite resources, e.g., space transport network resource, which then can not promise users' experience. However, for high priority users, normally the whole system shall endeavor to serve them first, i.e. reserving or even pre-empting not only radio resources but also backhaul resources to serve the them, which requires the 5GS to interact with NTN control function, e.g., to reserve transport resources on satellites providing backhaul services, and to not schedule this satellite beam for other purposes.
  Potential objectives for study
  Whether and how the 5G system can assist the resource allocation of the satellite transport network providing backhaul?
Use Case 5: Coordination with multiple satellite RAT
Use case description:
  Since the latency and coverage of LEO and GEO are different, UEs can access the 5G network through gNBs on LEO and GEO satellites based on service requirements to reduce latency and increase bandwidth.
Potential objectives for study
  add / update new requirement or KPI for the UE access the network through multi satellite access, e.g. one application traffic can be carried by both LEO& MEO access

## Slide 7: Use Case 6: Local Data Switching via UPF on-board
Use case description:
  In some scenarios, two or a group of ships or cars may roam to places far from territorial network, and then need to communicate with each other via satellite access. Whereas, if the PSA UPF is deployed on the ground, the communication among members of this group will be subject to long delay and limited data rate even 5G VN communication defined in Rel 16 is enabled, because the communication data has to travel the feeder link twice.
  Support of local data switching (e.g, 5G LAN local switch and N19 forwarding) via UPF on-board would significantly reduce communication latency and remove the data rate limitation brought by satellite backhaul, especially for case of LEO satellites with regenerative payload. Thus it is proposed to study this use case.
  Potential objectives for study
  Whether the 5G system supports local data switching via LEO satellite for UEs in a communication, considering the mobility of the LEO satellite.

## Slide 8: ANNEX

## Slide 9: Use Case 1: Temporary networking
Service flow:
  1. A scientific investigation team arrives in Antarctica, and set up a camp, where a local network is to deployed, e.g., for data collection, analytics and storage.
  2. As there is no terrestrial network, the team members have to access operator’s network and/or the local network via satellite access. So the local network has to connect with gNB on the satellite.
  3. To allow the local network to connect with gNBs on-board, in the camp, there may be a light satellite gateway which can search available gNBs on-board, establish connection with a gNB on-board., and work as a local UPF or local 5GC.
  4. To add this local UPF or 5GC, the light satellite gateway (e.g., as a UE) may send a request to remote 5GC in operator’s data center to ask for network configuration for being a local UPF or 5GC.
  NOTE: To completely isolate this local network, a standalone 5GC may be setup.

## Slide 10: Use Case 1: Temporary networking
Service flow:
  5. The remote 5GC will authenticate the light satellite gateway, and determine it can work as a local UPF or 5GC.
  6. After receiving configuration data, the light satellite gateway works as a local UPF or 5GC, e.g.,:
    The local UPF will setup N4 connection towards a SMF(s) in the operator’s data center
    The local 5GC may setup more TNL associations with the gNB on board after NG setup is completed.
  7. Any team member has to be authorized to visit the local network:
    If a local UPF is deployed, the SMF may authenticate the user, and determine whether a PDU session towards the local UPF is allowed.
    If a local 5GC is deployed, it is up to the local 5GC to authenticate the user.
  NOTE: Due to limited satellite computing resource, there may be no IP sec tunnel between gNB on-board and local UPF/5GC, so 3GPP may need to consider how to provide security protection for the connection between gNB on-board and local UPF/5GC.

## Slide 11: Use Case 4: Coordination with satellite system
  Service flow:
  1. A government user attached to the 5GS via satellite access;
  2. To serve this high priority user, the 5G system will reserve radio resources for this user, and set ARP to high priority for QoS flows belonging to this user;
  3. The 5G system also informs NTN control function to reserve transport network resources between the gNB on-board and the satellite gateway on the ground for this user, i.e., the satellite backhaul resources, so that user data transmission over N3 connection can be promised.
  4. The 5G system may also tell the NTN control function that there is a high priority user in a designated area to avoid the NTN control function to change this satellite beam to serve other services/systems, e.g., not to schedule this satellite beam to serve another area for mission critical system.

## Slide 12
Thank You!