## Slide 1: Motivation for a SID on enhancing 5G system to support additional satellite capabilities for Rel- 19
3GPP SA WG1 Meeting #97e
Electronic Meeting, 14 - 24 Feb 2022
Agenda item: 4 – New study & work items
Document type/for: discussion
S1-220131
Thales, Novamint

## Slide 2
Background
Starting with Release 17, 3GPP introduced the necessary requirements to support of satellite access and satellite backhaul in the 5G system in TS 22.261.
Additional satellite capabilities are proposed to be supported by 5G system

## Slide 3
Store and Forward (S&F) operation
  for a satellite to be able to provide autonomously service to UEs without the satellite being always connected to a gateway (i.e. S&F allows service link access to continue to be operational even at times when the feeder link is not connected). This is in particular useful for IoT service via NGSO space segment
GNSS free operation
  This allows to support UE without GNSS receiver or with GNSS receiver but no access to GNSS service for broadband or IoT services. Also it can improve UE energy efficient and reduce the cost UEs
New capability for satellite access in Release 19

## Slide 4
Reliable location service:
  For the support of regulated services (e.g. lawful intercept, emergency communications, public warning service) where Law enforcement apply, satellite access shall be able to provide a “reliable” UE location (either network verified or network provided) in all operations modes (idle and connected)
PLMN selection between GEO/MEO/LEO based networks:
  A given UE may have access to several PLMN network each based on different orbit constellation (GEO, MEO, LEO or HEO) each characterized with different latency, throughput capabilities as well as billing policy.
Temporary satellite connectivity:
  satellite network may connect on a temporary basis a local access network (with local routing capability) in un-served area (e.g. remote area for scientific expeditions, critical missions)
New capability for satellite access in Release 19

## Slide 5
Objectives
Study use cases with related pre-conditions, service flows, post-conditions, potential impacts or interactions with existing services/features associated to the support of the following new capabilities for satellite access
  Store and forward operation
  GNSS free operation
  Reliable location service: In addition, study the regulatory requirements of regulated services and associated operational requirements (e.g. during registration/PLMN selection) in order to identify the needed position accuracy, latency to obtain the position (e.g. TTFF - Time To First Fix if GNSS based) and security requirements
    Note: SA1 shall scope the activity in complement to Rel-18 RAN2 NR-NTN-enh and Rel-18 SA2 FS_eLCS_ph3 are covering some of these aspects. For example, SA1 should study the relevance of defining of border areas.
  PLMN selection between GEO/MEO/LEO based networks: In addition, study the relevance of taking into account criteria for the prioritization and selection of a PLMN based on a specific orbit satellite access.
  Temporary satellite connectivity to LAN: undertake gap analysis on Isolated Operation for Public Safety feature (IOPS) capability
Then Identify potential new requirements and/or KPIs

## Slide 6
Annex New satellite capability

## Slide 7
Store and forward operation with satellite access
NGSO constellation typically requires many satellites to provide service all over the Earth.
Moreover, it requires that the constellation connects simultaneously a service area with a Core Network via a ground network infrastructure of gateways.
Store and Forward (S&F) operation for a satellite enable to provide autonomously service to UEs without the satellite being connected to a gateway (i.e. S&F allows service link access to continue to be operational even at times that the feeder link is not connected).
Non 3GPP technologies already use S&F for IoT market.
Benefits associated with the support of S&F:
  Extending satellite service coverage in areas where satellites cannot be connected to ground stations (e.g. maritime or very remote areas with lack of ground-stations infrastructures)
  Improving ground segment affordability by enabling operation with fewer ground-stations and allowing more robust operation of the satellite under intermittent feeder link operation.

## Slide 8
GNSS free operation
Currently 5G system satellite access requires the use of GNSS service.
However, many UEs are without GNSS receiver or without availability of GNSS service.
Several non-3GPP technologies using as well satellite access technologies such as DVB or LoRa (IoT) are already capable of supporting UE without GNSS.
It is important for 3GPP to study the use cases where UE without GNSS requires using satellite access technologies