## Slide 1: Ambient IoT device power source profile
Source: Apple
Agenda item: 7.3 FS_AmbientIoT

## Slide 2: Introduction
The following items have been discussed extensively:
  differences of various energy harvesting mechanisms
  how much energy each mechanism may generate
  device power requirement
It was also noted that there could be differences on whether any energy is available at the communications module and how this would impact the eventual requirements
This contribution outlines potential behaviours of the communications module for a given energy harvesting power profile and proposes to get a common understanding of potential differences

## Slide 3: Device power sources and usage
At a high level, there appears to be no difference in the device behaviour with different energy harvesting sources

## Slide 4: Harvested energy availability scenarios
Sufficient power available
  Power is available when required by the communications module
  The power can be:
    stored on the device as a result of energy harvested from the environment, or
    taken directly from the harvested energy
Intermittent power available
  Power is not always available when required by the communications module
  The power source is not constant, for example:
    if harvesting energy from movement, the movement stopped, or
    the power storage was insufficient i.e. battery too small
Harvested (RF) energy provides both energy and a trigger to activate the communication module to transmit data

## Slide 5: Data transmission behaviour
Type 1 and 2 devices are ‘internal triggered’
Type 3 devices are ‘external triggered’

## Slide 6: Device behaviour differences
Internal triggered device
  Sends data when data is ready to transmit and sufficient power is available
  Availability of harvested energy alone does not result in data transmission
  Decision to transmit data is made by the device, subject to available power and e.g. on sensor measurement threshold, or a request from the network
External triggered device
  Sends data when a signal is received that both powers the communications module and acts as a trigger for the communications module
  Energy harvested from that signal can be stored for later use, but until another external trigger signal is received, no data is transmitted
  Decision to transmit data is made by an external entity