## Slide 1
Qualcomm Incorporated
Motivation for
SA2 Rel-13 WID Proposal Extended DRX for Idle mode

## Slide 2: Rel-12 MTC Power consumption optimization (MTCe-UEPCOP)
What was accomplished:
  Introduction of Power Saving Mode
    UE becomes unreachable for paging during PSM, it stops access stratum activities.
    How to enter PSM:
      UE negotiates Active time with MME (and optionally periodic TAU timer)
      UE starts active timer when it enters idle mode.
      When Active time expires it enters PSM.
    How to exit PSM:
      Trigger: MO data, Periodic TAU timer expires
      Action: Service request or TAU, respectively.

## Slide 3: Limitations of Power Saving Mode
PSM has limited applicability for unscheduled Mobile Terminated data with some requirement on MT data delay tolerance
  What can be done today with PSM for MT data:
    Negotiate Periodic TAU timer equal (or slightly shorter) to maximum allowed delay tolerance for MT data.
    UE needs to perform periodic TAU procedure to become available after entering PSM.
    Store & Forward functionality is required in the network:
      E.g.: SMS, SMS based triggering
    UE needs to negotiate an Active Timer large enough to allow the network to send the MT packet once UE updates registration:
      E.g.: SMS infrastructure is notified once UE performs periodic TAU
      Therefore Active timer should be 2min+
Drawbacks:
  Increased signaling due to unnecessary periodic TAUs
    Example: Delay tolerance = 30min, but only one MT data per day, there could be 47 unnecessary periodic TAUs per day per UE (if no MO data).
  Increased Power consumption due to unnecessary periodic TAUs

## Slide 4: The Importance of MT data scenarios
Many use cases for MTC are being developed or considered with different requirements for MTC device reachability delay for MT data.
  PSM is not effective in these scenarios.
MTC Application | Density (/sq. km) |  | Uplink |  |  |  | Downlink |  |  | 
 | Urban | Suburban | Use case | Messaging interval | Data per transaction (bytes) | Transactions per day | Use case | Data per transaction (bytes) | Transactions per day | Wake up interval
Electric Meter | 5792 | 1158 | Meter read | Scheduled | 584 | 24 | Utility service msg. | 160 | 1 | 15 sec
Water Meter | 5792 | 1158 | Meter read | Scheduled | 200 | 12 | s/w update | 400000 | 0.01 | 15 min
Security Panel | 5792 | 1158 | Ack or sensor state change | Ad hoc | 584 | 10 | Remote interaction | 160 | 10 | 1 sec
HVAC - Residential | 1158 | 232 | Ack | Ad hoc | 200 | 0.08 | DR instructions | 160 | 0.08 | 15 sec
Outdoor Street Light | 579 | 116 | Ack | Scheduled | 200 | 2 | On/Off state change | 160 | 2 | 60 sec
Off Street Parking Meter | 5598 | 1120 | Payment transaction | Ad Hoc | 360 | 6 | Payment transaction confirmation | 100 | 12 | 1 Sec
Parking Space Sensor | 11197 | 2239 | State change | Ad Hoc | 60 | 12 | Diag test | 160 | 0.07 | 5 min
Water Assets | 5792 | 1158 | Asset health, alerts | Scheduled | 320 | 80 | Payment transaction confirmation | 320 | 80 | 1 sec
Delay tolerance

## Slide 5: Proposal for Rel-13
Open a new Rel-13 WID to adopt a solution that is effective for MTC power consumption reduction in scenarios requiring mobile terminated data.
Proposed solution: Extended idle mode DRX
  Already introduced in TR 23.887 in Rel-12
  Benefit for MT data:
    Does not introduce additional signaling load
    DRX cycle can be set depending on the requirements on delay tolerance for MT data
    Has better power consumption than PSM for scenarios requiring mobile terminated data (see next slides for comparison)
  Proposal is to address all open issues from core network perspective in SA2 and engage RAN2 for RAN specific aspects.
    A companion Work Item will proposed in RAN plenary in September.
  Extended connected mode DRX has further issues and is limited to stationary devices: we are not interested in this at the moment.

## Slide 6: PSM vs Extended DRX – Battery Life Comparison
Model for MO data:
  Device warm-up from deep sleep = 40ms
  Service request delay = 220ms
  X=4 MO data communications per day
  Time in connected mode for data transmission/reception = 400ms
    After 400ms of transmission UE is moved to I-DRX
Model for MT data:
  Non-scheduled Y=1 MT data per day, variable delay tolerance=60, 30, 15, 5 min.
  MT data communication lasts 1 second
  For PSM:
    It is assumed that MT data is SMS message.
    Periodic TAU timer = MT delay tolerance
    Active timer = 2min.
    MT data arrives 1 minute after periodic TAU
      UE performs TAU, stays in I-DRX with 2.56s DRX cycle for 1 minute.
      UE is paged, performs SR, stays connected with data transmission/reception for 2.56s, and goes back to I-DRX
      UE stays in I-DRX for 2min before going back to PSM.

## Slide 7: PSM vs Extended DRX – Battery Life Comparison (3)
Power values assumed (based on values used in RAN2 discussion in Rel-12 UEPCOP, see R2-132560)
Parameter | Value | Comments
 | 1 unit/ms | Power consumed for RX.
 | 2 unit/ms | Average power consumed for TX
 | 0.01 unit/ms | Power consumed during sleep mode, including power consumed for low accuracy clock and memory maintaining, leakage current (e.g. caused by power management unit), etc.
 | 0.0001 unit/ms | Optimized sleep state

## Slide 8: PSM vs Extended DRX – Battery Life Comparison (2)
Observations:
  Even for 1hr delay tolerance, PSM has slightly worse power performance than extended I-DRX with DRX cycle of 2 minutes.
  For delay tolerance of 5 minutes, performance of PSM is similar to current I-DRX with DRX cycle of 2.56
Chart: Battery life comparison
| 60 min | 30 min | 15 min | 5 min
PSM | 15.807 | 9.1121 | 4.9332 | 1.7405
Extended I-DRX (2 min) | 17.0669 | 17.0669 | 17.0669 | 17.0669
Extended I-DRX (5 min) | 30.7094 | 30.7094 | 30.7094 | 30.7094

## Slide 9: Why large DRX values?
We propose to extend DRX cycle length in idle mode to values in the order of minutes.
  Exact maximum value may be studied further in RAN2 but our target is at least around 5 minutes, beyond 10.24s.
As shown in R2-132560 during RAN2 UEPCOP study phase:
  A DRX cycle of 2 min can increase battery life by around 6 times the battery life for DRX=10.24s. A DRX cycle of 5 minutes can increase it by almost 9 times.
    (Comparative performance depends on traffic characteristic)