## Slide 1: FMSS Solution Evaluation
China Mobile
SA WG2 Meeting #109 S2-15xxxx
25 - 29 May 2015, Fukuoka, Japan (revision of S2-15xxxx)

## Slide 2: Candidate Solutions
There are 4 candidate solutions
  Solution 1 (Sd) and 2 (Gx) need to work together addressing different scenarios
  Three types of solutions: Sd&Gx, Dual Classifier, St
Commonalities
  PCRF provides traffic steering policy through semantics
  Traffic classifiers are needed
Sd&Gx
  PCRF provides steering policies to TDF/PCEF
  TDF/PCEF performs classification based on the policy
Dual Classifier
  PCRF provides steering policies to TDF/PCEF & TCFd
  TDF/PCEF & TCFd performs classification based on the policy
St
  PCRF provides steering policies to SCTCF
  Classifiers performs classification based on steering policies
    TDF/PCEF traffic marking based on active PCC/ADC rules
    Classifier in Gi-LAN performs further classification based on SCTCF policies (out of 3GPP scope)

## Slide 3: Signaling Load
Sd&Gx
  PCRF need to send steering policy to PCEF/TDF
Dual classifier solution
  PCRF need to send steering policy to TCF
  When downlink classifier is used:
    The TCF send application reporting to PCRF and PCRF send downlink steering policy rule to TCFd
    TCF send downlink chain ID to TCFd leverage packet forwarding
St
  PCRF need to send steering policy to SCTCF
  When leverage PCEF/TDF for packet marking:
    The Gx and Sd interfaces are enhanced to carry a packet marking profile identifier to PCRF
    PCRF using packet marking profile identifier as steering policy rule to SCTCF
Conclusion
  Sd&Gx signaling load is less than the other two solutions

## Slide 4: Traffic Routing
Sd Interface (contains steering policies)
Sd&Gx and St causes non-optimal traffic routing
Generally, FW and NAT are the first two service enablers that downlink traffic are handled
Double the (S)Gi-LAN bandwidth and switch/router capacity consumption
Double the downlink latency
The suffering becomes even worse if the (S)Gi-LAN belong to different sites, e.g., two data centers
Conclusion
  Dual classifier solution ca avoid traffic back and forth as much as possible
(S)Gi-LAN systems*
* Contains service functions and infrastructure to steer traffic between them
(S)Gi Interface
PCEF/TDF
2
3
Internet
FW
NAT
1
PCRF
(S)Gi-LAN(s)
PCRF
Service Functions, Forwarding Entities, Classifiers etc.
PDN
SCTCF
Gx
Sd
St
FW
NAT
PCEF
/TDF
Classifier
1
2
3

## Slide 5: Co-Existence with ONF/IETF
Sd&Gx and Dual classifier solution
  Can work with either ONF or IETF mechanism is used for traffic steering
  More friendly with IETF SFC
St solution
  More consistent with ONF defined SDN architecture
All the solutions are future proof
  St solution is consistent with control and data plane separation and already to introduce the control concept
  Sd&Gx and Dual classifier solution can also evolve to a future proof solution if e.g., PCRF is collocated with SDN controller
Conclusion
  No one is dominant than others

## Slide 6: Summary
Criteria | Gx&Sd | Dual classifier | St
Meet requirement: the solution should meet the SA1 requirement. |  |  | 
Application based traffic steering: the solution should support application detection functionality and application characteristics related policies to realize application based traffic steering. |  |  | 
Co-existence with existing function: the solution should applied into the existing various 3GPP network deployments with and without ADC, with and without TDF |  |  | 
Signalling load: the solution should avoid causing heavy signalling load. |  | * | 
Scalability: the solution should avoid causing heavy user plane handling load and could be adopted by operator to handling large traffic load |  |  | 
Efficiency: the solution should be analysed on the impact on the traffic routing to the (S)Gi-LAN, on the impact of the traffic forwarding latency |  |  | 
Agnostic to the architecture/solution of (S)Gi-LAN: can co-existent with the work of other SDOs (e.g., ONF, IETF), and does not causing extra dependencies of other SDOs |  |  | 
can be avoid using data plane way to transfer steering policy

## Slide 7: Conclusion
Dual classifier solution is recommended for the normative work
If the dual classifier solution is normalized (with introducing Sts interface), the Sd&Gx and St solution can be implemented per operator preference based variant scenarios
  If no downlink classifiers are used, the solution fall back to the Gx&Sd solution
  The Sts interface can be used by the St solution rely on a new interface from PCRF towards a new entity
If 1 cannot be agreed, the traffic optimization for downlink shall be included in some extent
  Otherwise, FMSS WI loss its one of its most important goal
The GX interface shall be enhanced for traffic steering policy provision
Whether the new interface will reusing Sd is per stage 3 decision